## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [ULI design for 802.15.10 (L2R)]
Date Submitted: [14 March 2019]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expy, Santa Clara Ca, USA]
Voice:[+1.408-330-4586] E-Mail:[charlie.perkins@huawei.com]
Re: [ULI design for 802.15.10 (L2R)]
Abstract: [Description of ULI interfaces needed for IEEE802.15.10, architecture and functionality]
Purpose: [To motivate discussion in 802.15.12 WG session]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Design Overview
Making use of 15-17-0296-00-0012-l2r-operations-with-uli
L2R functional description
Internal interfaces and primitives required for PDE MMI
Configuration and provisioning
Rewiring ULI functional modules

## Slide 3: L2R functional description
Designed to handle ~104 devices
  topology discovery
  mesh maintenance
  data plane forwarding
  address management
  multiple metrics
  more robust routing
DCN 15-17-205-00-0010 has a good description of the overall protocol

## Slide 4: L2R data primitives required for PDE, MMI
L2R data service
  L2R-DATA.request
  L2R-DATA.confirm
  L2R-DATA.indication

## Slide 5: Dispatching a frame for L2R
MAC
S
A
B
D
MMI
L2R
PDE
Protocol X
MAC
MMI
L2R
PDE
MAC
MMI
L2R
PDE
MAC
MMI
L2R
PDE
Protocol X
Dispatching by looking at L2R routing IE
Dispatching by looking at Protocol ID in MPX IE.
S
A
B
D
MAC
21
octets
L2R routing IE
variable octets
MPX IE
Protocol A
Payload
Various octets
2
octets
Transaction
Control
1
octet
Protocol
Identifier
=
0
x
XXXX
2
octets
0xXXXX is for Protocol X. (e.g. IPv4)

## Slide 6: Dispatching a frame for L2R – 6LoWPAN mesh under
MAC
S
A
B
D
MMI
L2R
PDE
6LoWPAN
MAC
MMI
L2R
PDE
6LoWPAN
MAC
MMI
L2R
PDE
6LoWPAN
MAC
MMI
L2R
PDE
6LoWPAN
ULI
-
6
lo IE
2
octets
IPHC
2
octets
6
LoWPAN
NHC
1
octet
6
LoWPAN
MAC
21
octets
L2R routing IE
variable octets
Dispatching by looking at L2R routing IE
Dispatching by looking at ULI-6lo IE
S
A
B
D

## Slide 7: Internal interfaces and primitives required for PDE, MMI
Data
  Figure 7-1—Message sequence chart of a successful end-to-end data transmission
  Figure 5-25—L2R data frame processing
  Figure 5-27—Hop-by-hop retransmission procedure

## Slide 8: L2R mesh procedures
Start an L2R mesh
Stop an L2R mesh
Discover an L2R mesh
Discover an L2R mesh in associated PAN
Join an L2R mesh
Mesh selection by the next higher layer
Rejoin an L2R mesh
Leave an L2R mesh

## Slide 9: L2R address allocation procedures
Initial short address allocation
Short address maintenance
Short address release

## Slide 10: L2R route establishment procedures
US (UpStream) route establishment
US route establishment with RvS (Routing via Siblings)
Multicast route establishment

## Slide 11: P2P route establishment procedures
Processing of a P2P-RQ/P2P-RP IE in storing mode
P2P route establishment with intermediate response disabled
P2P route establishment with intermediate response enabled
Processing of P2P-RQ/P2P-RP IE in non-storing mode

## Slide 12: Routing procedures
US or DS algorithm based on the NT
P2P routing decision algorithm
L2R data frame processing
Route construction over a TMCTP
Hop-by-hop retransmission procedure
Multicast processing by the source
Multicast processing at intermediate hops

## Slide 13: Other procedures
Cold start bootstrapping procedure
Message sequence chart of a successful end-to-end data transmission
Dtag

## Slide 14: Candidates to place L2R management box
1
2
3

## Slide 15: Candidates to place L2R management box (contd.)
#1 is located at inside of L2R box. L2R specific functions can be managed here.
#2 is located at inside of PDE box. Using KMP with L2R and managing L2R security PIB can be managed here.
#3 is located at application layer. It can manage several protocol boxes from upper layer.
Since PDE is very common function among protocol boxes, placing here may be disfavored. #2 can be merged to #3.

## Slide 16: Conclusion for the architecture issue
Assumption to place two boxes to manage L2R functionalities
  A box in L2R protocol box manages L2R specific process and the boundary to the L2R is interfaced by L2R primitives and PIBs.
  A box in application layer manages PAN coordinator DC and security things.

## Slide 17: Higher layer manages:
No. | item | Page in IEEE802.15.10 | Which box should manage | Description
1 | Short address management | P.27 P.38-39 | 3 | PAN coordinator manages short addresses for all devices within the PAN using PANC DC (PAN coordinator direct connection) that is exchanged by a transport protocol other than L2R or ULI. Application layer manages it.
2 | Source rout management | P.54, P.64, P.66, P.67 | 1 | In no-storing mode, all DS path information is gathered to mesh root. Appropriate path list need to be generated everytime when data is sent.
3 | Procedure through PANC DC | P.38-39, P.77 | 3 | A mesh root with PANC DC (PAN coordinator direct connection) which is up to a higher layer of L2R need to exchange the information with PAN coordinator through PANC DC for the following two functions. 1. Short address management 2. Broadcast to all devices within a PAN
4 | PAN discovery | P.28-31 | 1 | Before starting or joining an L2R mesh, an L2R device does the discovery process in order to find an appropriate PAN to associate to. This process should be controlled by a next higher layer of an L2R sublayer.
5 | Procedure for starting a new L2R mesh | P.26 | 1 | Configuration of an L2R mesh when a device starts a new L2R mesh using profile.
6 | Procedure for joining a L2R mesh | P.32, P34 | 1 | Configuration of an L2R device when a device joins a L2R mesh using profile
7 | Mesh selection procedure | P.33 | 1 | In the case that l2rMeshSelection is FALSE, after mesh discovery process, a next higher layer of a joining L2R device needs to select a mesh to join from discovery results.
8 | Mesh root management | P.26-28 | 1 | Management related to mesh root.
9 | Mesh device management | P.28-37 | 1 | Management for join and leave..
10 | Procedure for detecting a disconnection from the L2R mesh | P.36 | 1 | When a next higher layer of an L2R sublayer is indicated that it is disconnected from the L2R mesh, it should do something.
11 | Procedure for detecting a new L2R mesh | P.43 | 1 | When L2R device finds a new L2R mesh, it should do discovery process in order to get information necessary for add ion of new entry to MT.
12 | Process for detecting an unknown neighbor | P.69 | 1 | L2R sublayer inform to its next higher layer that it detects an unknown neighbor. In this case, the next higher layer should ……
13 | Separation of concatenated frame using Dcat feature | P.73 | 1 | When Dcat is used, L2R sublayer of final destination delivers the concatenated frame to the next higher layer. It should be separated to the individual frames.
14 | Security procedure | P.78-81 | 3 | After key exchange using KMP, the exchanged key is set to the MAC PIB and other necessary security IB is set to the L2IB.

## Slide 18: Configuration and provisioning
mesh parameters
  show Table 7-38—L2IB attributes
metrics
  RSW (additive version of “signal strength”
  ETX
  Expected Airtime
modes of operation
  e.g., storing vs. non-storing

## Slide 19: L2R primitives required for PDE, MMI
Primitives to manage an L2R mesh
  L2RLME-PAN-SCAN.request, confirm, indication
  L2RLME-MESH-START.request, confirm
  L2RLME-MESH-STOP.request, confirm
  L2RLME-JOIN-MESH.request, confirm
  L2RLME-MESH-DISCOVERY.request, confirm
  L2RLME-MESH-SELECT.request, confirm
  L2RLME-LEAVE-MESH.request, confirm
  L2RLME-DISCONNECT-MESH.indication
  L2RLME-NOTIFY.indication

## Slide 20: L2R primitives required for PDE, MMI
Managing short address assignment
  L2RLME-AA-RQ.request, confirm, indication
  L2RLME-AA-RP.request, confirm
  L2RLME-ARLS.request, confirm, indication
Handling multicast route establishment
  L2RLME-MULTICAST-SUBSCRIPTION.request, confirm

## Slide 21: Rewiring ULI functional modules
Does all the forwarding modification live in the MAC regardless of ULI ?

## Slide 22: Backup slides
15-19-0164-00-0012

## Slide 23: Purpose
To identify unclear points and issues when considering incorporating L2R to the ULI by looking at the current ULI architecture, formats and functionality and to provide resolution.
The issues are summarized into two categories.
  Format
    Dispatch
    Discovery
  Architecture
    Functions and Procedures
    Security and Key management

## Slide 24: 1. Format issues
Dispatch
  Where should L2R IE be inserted?
Discovery
  How is it done with L2R discovery?

## Slide 25: Two places where a dispatch happens

## Slide 26: Discovery
L2R-D IE is included in EB or EBR for the L2R discovery to know if they speak L2R protocol and to know what routing functions are supported.
What is the ULI discovery purpose?
  To know if ULI frame is understandable? .. Whether IEs are
  To exchange capability? No
  Is it used in EB or EBR same as L2R? No
ULI discovery and L2R discovery can be happened at same time? TBD
  Including ULI IE and L2R-D IE in one EB or EBR guess not

## Slide 27: Conclusion for the format issue
Regarding L2R dispatch…,
  L2R IE should be used to dispatch to L2R box.
  L2R IE should be inserted
    between MPX IE and the payload in case that MPX IE is used.
    Between ULI-6lo IE and the MHR in case that ULI-6lo IE is used.
Need to clarify what ULI discovery is.
  Consider using L2R-D IE with ULI IE in same EB/EBR if ULI discovery concept is same as L2R’s.

## Slide 28: 2. Architecture
Other MAC protocol is managed by protocol box between PDE and MMI to use their MAC functionality.
L2R is designed so that upper layer manages by using L2R functionality (primitives and PIBs).
L2R needs a management box above it.

## Slide 29
Questions?