## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Architecture for ULI Module Interfaces]
Date Submitted: [14 May 2019]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expressway, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Re: [ULI Architecture and Autoconfiguration]
Abstract: [This document proposes an execution environment for ULI Modules, as well as the inter-module interfaces. The environment should enable autoconfiguration for adding new modules]
Purpose: [Improving the 802.12 Architecture for ULI Module Interfaces]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Data flow through ULI module interfaces
Linking a module into the ULI
Autoconfiguration for ULI modules
Receiving a frame
Profile instances and links
Transmitting a frame
Miscellaneous

## Slide 3: Linking a module into the ULI
Module data structures required
List of SAP entry and exit routines
PIB entries for profile definitions
Entry / exit points, parameter definitions
Predefined profiles (values for PIB items)
  At least a default profile with “null” entries
PIB entries required per link
Module IE processing entries

## Slide 4: Autoconfiguration for ULI modules
Every MOD-SAP routine is mapped to an array element of one of two protocol switch arrays within the ULI object file
Module entry point protocol switch
Module exit point protocol switch
This leads to re-drawing Figure 1-1 of 15-16-0656-19-0012

## Slide 5: MMI receiving a frame from interface
MMI inspects the Header IEs to see if a module needs to be invoked to process the frame
If so, deliver to module, which will determine how to handle the frame
If none, deliver to application as determined by Ethertype
  Profile not needed in this case

## Slide 6: Profile instances and links
Each module’s profile information (i.e., set of required PIB entries) identifies that module’s requirement for frame transmission over a link
A “link” (source address and neighbor’s address) needs a profile instance.
Profile information for the link is indexed by (source, nbr)

## Slide 7: Transmitting a frame
PDE basically passes the frame to MMI
To transmit, destination address of frame *must* enable lookup of a profile
  i.e., (source, dest) *must* index a “link”
  Otherwise, L2R must route (i.e., find the MHR neighbor address [Figure 5-25])
Undetermined profile entries point to a module to determine the needed profile value for the link

## Slide 8: Is the frame able to be transmitted?
Why might a destination be unreachable?
resource allocation (e.g., cells / 6top)
L2R has to route it (i.e., not a neighbor)
802.1X has to open a port for it (??)
Ranging is incomplete
Pending link acknowledgement
The link (or neighbor) requires security
Each module may place constraints

## Slide 9: Fragmentation
MMI has responsibility to determine whether or not a frame has to be fragmented.

## Slide 10: MAC and module control routines
Probably works the same say, as long as MMI has all the control SAP routines autoconfigured into its protocol switch