## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Architecture for ULI Module Interfaces]
Date Submitted: [16 May 2019]
Source: [Charlie Perkins] Company [Futurewei]
Address [2330 Central Expressway, Santa Clara Ca, USA]
Voice:[+1.408-330-4586]
E-Mail:[charlie.perkins@huawei.com]
Re: [ULI Architecture and Autoconfiguration]
Abstract: [This document proposes an execution environment for ULI Modules, as well as the inter-module interfaces. The environment should enable autoconfiguration for adding new modules]
Purpose: [Improving the 802.12 Architecture for ULI Module Interfaces]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Data flow through ULI module interfaces
Linking a module into the ULI
Autoconfiguration for ULI modules
Receiving a frame
Profile instances and links
Transmitting a frame
Miscellaneous

## Slide 3: Linking a module into the ULI
Module data structures required
Array of SAP entry and exit routines
  parameter definitions per routine
Profile attribute definitions (e.g., PIB)
Predefined profiles (values for PIB items)
  At least a default profile with “null” entries
Profile attribute values required per link
IE processing  Module SAP

## Slide 4: Autoconfiguration for ULI modules
Every MOD-SAP routine is mapped to an array element of one of two protocol switch arrays within the ULI object file
Module entry point protocol switch
Module exit point protocol switch
This leads to re-drawing Figure 1-1 of 15-16-0656-19-0012

## Slide 5
Protocol Discrimination Entity
(
PDE
)
-
Mandatory
-
Multiplexed MAC Interface
(
MMI
)
-
Mandatory
-
PD
-
SAP
PLME
-
SAP
I
E
E
E
8
0
2
.
1
5
.
1
2
I
E
E
E
8
0
2
.
1
5
.
4
L
a
y
e
r
2
L
a
y
e
r
1
IPv
6
Network
Other Networks
NWK
-
SAP
Applications
AppM
-
SAP
EPD
=
0
x
888
E
802
.
1
X
-
Optional
-
6
LoWPAN
-
Optional
-
EPD
=
0
x
86
DD
.
1
X
-
SAP
EPD
=
0
xA
0
ED
RLS
(
Ranging
&
Location
Support
)
-
Optional
-
RLS
-
SAP
Generic
(
GTS
)
-
Optional
-
TSCH
/
BE
-
Optional
-
DSME
-
Optional
-
Generic
-
Optional
-
RFID
-
Optional
-
LP
-
WAN
-
Optional
-
PSDU FRAK
Beacon
-
enabled modes
Nonbeacon
-
enabled modes
O
-
QPSK
-
Optional
-
BPSK
-
Optional
-
FSK
-
Optional
-
OFDM
-
Optional
-
CSS
-
Optional
-
I
.
E
.
s
UWB
-
HRP
-
Optional
-
MSK
-
Optional
-
Modulation type
Data Whitener
FEC
PHY optional behaviors
RCC
-
Optional
-
Low
Energy
Priority
Security
MAC optional behaviors
Association
Metrics
Channel
Hopping
Promiscuous
ASK
-
Optional
-
TRLE
M
A
C
P
H
Y
UWB
-
LRP
-
Optional
-
Ranging
Interleaver
SUN
TVWS
TSCH
-
Optional
-
SRU
.
1
X
-
SAP
RLS
-
SAP
MCPS
-
SAP
MLME
-
SAP
L
2
R
(
Layer
2
Routing
)
-
Optional
-
L
2
R
-
SAP
L
2
R
-
SAP
EPD
=
0
x
0001
KMP
(
Key
Management
Protocol
)
-
Mandatory
-
KMP
-
SAP
KMP
-
SAP
P
D
E
M
M
I
P
r
o
t
o
c
o
l
M
o
d
u
l
e
EPD
=
0
xA
0
ED
AppD
-
SAP
LP
-
WAN
/
BE
-
Optional
-
MAC PIBs
PHY PIBs
EPD
=
0
x
1381
Vendor
Specific
-
Optional
-
VS
-
SAP
VS
-
SAP
Management
Protocols
-
Mandatory
-
MPM
-
SAP
MPM
-
SAP
Mgmt
MIB
6
top
-
Optional
-
6
top
-
SAP
6
top
-
SAP
PtD
-
SAP

## Slide 6: Receiving a frame from MAC/PHY
If no IEs, MMI sends to PDE/default_app, otherwise to Mgmt Module
Mgmt parses the Payload into Payload IEs and Data Payload
Mgmt invokes MOD-SAP routines as needed to process Payload IEs
If ULI IE exists, Mgmt delivers to PDE
Otherwise, Mgmt delivers to default_app
Profile not used if going to higher-layer

## Slide 7: Profile instances and links
Each module’s profile information (i.e., set of required PIB entries) indicates its role for transmission over a link
A “link” (source address and neighbor’s address) needs a profile instance.
Profile information for the link is indexed by (source, nbr)
Transmission over the link may need information not associated with a module

## Slide 8: Transmitting a frame
PDE constructs ULI IE, passes to Mgmt
To transmit, destination address of frame *must* enable lookup of a profile
  i.e., (source, dest) *must* index a “link”
  Otherwise, L2R must route (i.e., find the MHR neighbor address [Figure 5-25])
A profile attribute lacking a value points to the module that can determine the attribute value needed for the link

## Slide 9: Is the frame able to be transmitted?
Why might a destination be unreachable?
Resource allocation (e.g., cells / 6top)
Not a neighbor (L2R has to route it)
802.1X has to open a port for it (??)
Ranging is incomplete
Pending link acknowledgement
The link (or neighbor) requires security
Each module may place constraints

## Slide 10: Miscellaneous
Fragmentation
  MMI has to determine whether or not a frame has to be fragmented.
MAC and module control routines
  Mgmt has all the control SAP routines autoconfigured into its protocol switches