## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Still More LB156 Comment Resolutions
Date Submitted: 12-Aug-2019
Source: Benjamin A. Rolfe
Company: Blind Creek Associates
Address: PO Box 798 Los Gatos CA 95031
Voice: +1 408 332 0725, E-Mail: ben.rolfe @ ieee.com
Re: LB156 Comment Resolution
Abstract: Proposed resolution on comments relating to MLME-DPS and other purposes.
Purpose: Resolve comments
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Comments Addressed
Comment IDs
i-0628
i-0632
i-1144
i-1265
i-1270
i-1781
i-2080
i-2094
i-2660
Related to DPS
3 comments x 3 times each

## Slide 3: Comment IDs: i-0632 i-1270 i-2094
Comment
I do not think this is true. The timers are initiated when both ends call MLME-DPS.request, not when sending or receiving frames.
Discussion: Comment is right, text is wrong.
Comment is on the statement “To prevent the PHYs from becoming lost as a result of this optional behavior, the MAC sublayers on both sides of the link shall initiate timers after sending the frame (for the originator) or receiving the frame (for the recipient).”
Text is incorrect (comment is right). The MSC and other text show that the timer is started by the MLME-DPS primitive. Text in 8.2.15.2 and Figure 6-48 (802.15.4-2015) show the timer beginning after the MLME-DPS.confirm is issued by the MAC.
Proposed resolution
Change to:
“To prevent the devices from becoming lost as a result of this behavior, the MAC sublayers on both sides of the link shall initiate timers after issuing the MLME-DPS.confirm with status of SUCCESS.”

## Slide 4: Comment IDs: i-0628 i-1265 i-2660
Comment :
Section 8.2.15.1 MLME-DPS.request is bit vague whether the DpsIndex is changed for one MLME-DATA.request or what. The DpsIndexDuaration says that
"The number of symbols for which the transmitter and receiver will utilize the respective DPS indices if a MCPS-DATA.request primitive is not issued."
which would indicate that DpsIndexDuration is not used at all of MCPS-DATA.request is issued, i.e., it is only used on responder side (or initiator who called MLME-DPS.request, but never followed it up with MCPS-DATA.request).
There is also text saying
"The use of the index for the transmitter and receiver is enabled or disabled exactly once per primitive request."
which is also not clear what it is trying to say. I think it is trying to say that they MLME-DPS.request only affects exactly one frame, i.e., DPS is reset back to normal after MCSP-DATA.confirm in the transmitter and MCSP-DATA.indication on the receiver are called.
Then the last paragraph has text that only applies to transmitter, as receiver will never call MCSP-DATA.request...
I think we need to fix issues in the MLME-DPS.request/confirm/indication too, so those sections should be modified by this document too.

## Slide 5: Comment IDs i-0628 i-1265 i-2660 (continued)
Discussion: MLME-DPS.request
The statement in table 8-36 “if a MCPS-DATA.request primitive is not issued.“ is incorrect.
The parameter sets the duration for which the alternate code(s) is (are) used in all cases according to the MSC and text at the end of 8.2.15.1 and in 6.9.4. The alternate preamble code is used until the timer expires as stated in the first paragraph and shown in the MSC. The Applications document (15-14-0226) also states the code remains in effect for DpsIndexDuration and reverts at expiration of the timer.
The last sentence of the paragraph following Table 8-36 “The use of the index for the transmitter and receiver is enabled or disabled exactly once per primitive request.” is probably wrong, too. There is no stated restriction (nor good reason I can think of) that the alternate codes be used for only one frame. It is unnecessary text so best to remove it.
The statement “if a following MCPS-DATA.request primitive does not occur.” is also unnecessary and possibly wrong: the ranging information may be returned by the responder in an acknowledgement, so the responder may not issue an MCPS-Data.request to return ranging data using the alternate code. The first part of the sentence stands alone and is correct.

## Slide 6: Comment IDs i-0628 i-1265 i-2660 (continued)
Discussion: MLME-DPS.confirm and MLME-DPS.indication
To the last part of the comment:
I think we need to fix issues in the MLME-DPS.request/confirm/indication too, so those sections should be modified by this document too.
Checked the confirm and indication descriptions and see no needed changes. The confirm returns error if DPS not supported, success otherwise. There are no other failures which I can think of that would be reported. The indication has no parameters, it signals that the timer has expired.

## Slide 7: Comment IDs i-0628 i-1265 i-2660 Continued
Proposed resolution:
Change the last row of Table 8-36 to delete “if a MCPS-DATA.request primitive is not issued.”
In the paragraph following Table 8-36, delete "The use of the index for the transmitter and receiver is enabled or disabled exactly once per primitive request.“
In the first sentence of the last paragraph delete “if a following MCPS-DATA.request primitive does not occur.”

## Slide 8: Proposed Resolutions: i-1144 i-1781 i-2080
MLME-DPS needs to be clarified whether it is for exactly one frame or not, and wheter it is automatically reset when timer expired. Also there are new possible values for the Dps Indexes, in Table 28, so Valid Range and table reference for TxDpsIndex and RxDpsIndex are wrong.
See discussion on i-0632 (et al). Those changes will fix the first part of the comment.
Need to fix the valid range and description for TxDpsIndex and RxDpsIndex to align with Table 28 and Table 29
Proposed resolution: Revised
Change Table 8-36, TxDpsIndex and RxDpsIndex:
Change Valid range of as follows:
0, 13–16, 21–2432, 91
Change Description of TxDpsIndex as follows:
The index value for the transmitter. A value of 0 disables the index and indicates that the phyCurrentCode value is to be used, as defined in 16.2.5.1. Other values indicate the preamble code, as defined in Table 16-7, Table 28 and Table 29.
Change description of RxDpsIndex as follows:
The index value for the receiver. A value of 0 disables the index and indicates that the phyCurrentCode value is to be used, as defined in 16.2.5.1. Other values indicate the preamble code, as defined in Table 16-7 , Table 28 and Table 29.
Comment: