## Slide 1: Licensed Narrowband Amendment Update for 802.15 WNG
Date: 2019-09-18
Author:

## Slide 2: Goals of Amendment Project
A group of industry stakeholders have come together to support amending IEEE 802.16-2017 to:
  Provide support for narrower channels of operation
  Aggregate discontinuous narrowband spectrum.
This is needed to address operations in the smaller spectrum allocations that electric utilities and other critical infrastructure industries have access to
  The 802.16s amendment defined operation between 1.25 MHz and 100 KHz.
  This amendment would define operation to as narrow as 5 KHz channels

## Slide 3: Potential Participants
Through a series of meetings at Utility, Oil, Gas, and Railroad conferences the following individuals and affiliations have expressed intentions to participate in the project
This group came to me to provide guidance on initiating the amendment process.
Craig Tedrow | GE MDS
Leonhard Korowajczuk | Celplan
Daryl Parker | Alligator
 | Telewave
Tom Peters | WCC of AAR
Bob Finch | Select Spectrum
Daoud Serang | CML Microcircuits
Zach Smith | BNSF
Jerry Roberts | Enterprise Products/ENTELEC
Klaus Bender | UTC
Tom Guttormson | Connexus Energy
Mark Crosby | EWA
Scott Schoepel | Motorola Solutions
Lon Renner | NPPD (representing UTC)
Guy Simpson/Menashe Shahar | Ondas
Rick Smith | Chevron
Rich Hawkins | WiMAX Forum

## Slide 4: Path Forward
To proceed with this amendment, there are two options:
1: Bring 802.16 out of hibernation as a Working Group
  The prior WG officers are not able to resume their pre-hibernation roles, so it would be a re-start with new people
  Most of the people with 802.16 expertise are no longer active or are working in other areas
2: Create in 802.15 Task Group to work on the project
  Scope of the project is aligned with Wireless Specialty Networks
  Task Group could operate as 802.15.16, similar to 802.15.22

## Slide 5: Activity within IEEE 802 to Date
The potential project was discussed informally with EC members at the July Plenary
The 802 Chair suggested the 802.24 TAG should host Teleconferences to provide a forum for discussion and PAR / CSD development
Two teleconferences have been hosted by 802.24
  Minutes and Draft PAR and CSD posted on Mentor
    802.24-19-0021r0 Minutes of August 5th Teleconference
    802.24-19-0022r0 Draft PAR
    802.24-19-0023r0 Minutes of Sept 3rd Teleconference
    802.24-19-0024r0 Draft CSD

## Slide 6: Scope Statement from Draft PAR
5.2.b. Scope of the project:
  This project specifies WirelessMAN TDD operation in licensed spectrum with channel bandwidth greater than or equal to 5 KHz and less than 1.25 MHz. The amendment will be frequency agnostic but will focus on spectrum less than 2 GHz. The project will introduce amendments to the IEEE Std 802.16 as required to support narrower channel widths and other functionality as needed to support operation in adjacent and non-adjacent Private Land Mobile Radio (PLMR) channels. The range and data rate supported by the narrower channels are commensurate with those of the base standard, as scaled by the reduced channel bandwidth. The project will add a modified air interface protocol at the PHY and MAC layers.

## Slide 7: Need Statement from Draft PAR
5.5 Need for the Project:
  Mission critical entities have a strong preference for private, licensed networks in for their data communications needs. Licensed channels from 5 kHz to 1 MHz are available from the FCC or in the secondary markets at a lower cost than commercial channels. Example operating frequencies include 160 MHz, 450 MHz and 900 MHz. The base standard, and thus this amendment, is not limited to specific operating frequencies. Furthermore, VHF/UHF channels have superior propagation characteristics requiring less infrastructure and are capable of meeting capacity needs of private networks. The amendment facilitates the development of innovative, cost-effective, and interoperable multivendor products for private licensed wireless access systems for mission critical networks. Applications include smart grids supporting generation, transmission, and distribution; field area networks; smart fields and smart pipes for oil and gas; intelligent transportation for rail systems; and federal, state and local uses for homeland security, environmental and seismic monitoring and military communications.

## Slide 8: Uniqueness
How are the desired use cases different than 802.15.4 SUN?
  Operation in Licensed Spectrum
  Point to Multi-point with handover between base stations. Relaying, but no mesh
  Fully Scheduled MAC supporting low, bounded latency
How are the desired use cases different than 802.15.4 LMR RCC?
  More flexibility in frequency bands and channel sizes
  Higher data rates than RCC LMR PHY
  Fully Scheduled MAC supporting low, bounded latency

## Slide 9: Licensed Narrowband Amendment
Teleconference discussion on moving project into 802.15
  Participants and stakeholders are in favor
This week in Hanoi – discuss and form recommended plan of action
  Does the 802.15 WG support taking on this project?
  Are any WG motions needed by 802.15 to confirm or support process?
  Should an 802.15 Study Group be formed?
  Should 802.15 assign SG meeting slots in November for PAR response?

## Slide 10: Licensed Narrowband Amendment Timeline
October 1st EC Teleconference
  Request agenda item to brief EC on plan for PAR
Next Licensed Narrowband 802.24 Teleconference – October 1st
  If SG is formed here, should telecon be moved to 802.15 or jointly?
  Final review and editing of PAR and CSD
PAR submittal by 30 day deadline before November plenary – October 11th
  Could be initiated by 802.15 if an 802.15 Task Group will do the project.
November Plenary
  Possible meeting slots for SG
  PAR review and response actions

## Slide 11: Discussion from 802.24 Tuesday
Continue conducting PAR/CSD development in 802.24
  Approve the PAR/CSD this week (with editorial license)
    Conduct motion to approve on Wednesday
    Send to Roger Marks for review
  Change PAR WG names to 802.24 as the TAG developing the PAR
  Circulate to EC to update them on the strategy. PAR developed by 802.24, assigned to 802.15
October 1st EC Teleconference
  Request agenda item to brief EC on plan for PAR
802.24 will submit PAR to EC by November plenary deadline
802.24 will provide a forum in November for PAR comments
EC will assign project to 802.15.
  Form Task Group 802.15.16
  Attendees of first Task Group meeting will be granted 802.15 voting rights