## Slide 1
Project: IEEE P802.15 IG VAT
Submission Title: Channel model in High-rate Optical Vehicular Communication System
Date Submitted: November 2019
Source: Tung Lam Pham, Hoan Nguyen and Yeong Min Jang [Kookmin University].
Contact: +82-2-910-5068 E-Mail: yjang@kookmin.ac.kr
Re:
Abstract : Introduce the channel model in High-rate Optical Vehicular Communication System
Purpose: To give a complete channel model in High-rate Optical Vehicular Communication System.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Channel model in High-rate Optical Vehicular Communication system

## Slide 3
Commercialize OCC for Vehicular communication still be a challenging work due to the complexity of channel model caused by various type of noise and weather condition.
Challenges in Optical Vehicular Communication system
Kookmin University
Can be modelled as two type: Additive White Gaussian noise (AWGN) and Blur (motion blur, rainy, snowy, foggy, etc.)
HS-PSK is a typical modulation scheme which had been introduced in IEEE 802.15.7-2018 standard as high-rate data scheme using in hybrid waveform of Optical Camera Communication (OCC) and Vehicle-to-Vehicle(V2V) scenario.

## Slide 4: Proposed channel model in Optical Vehicular Communication
Kookmin University
White Gaussian Noise is inevitable in OCC system, which is caused by ambient light radiation from the sun, street light.
Channel model in vehicular OCC system
Besides, due to relying on image sensors as the receiver, blur is also an issue of OCC system, especially in vehicular environment.

## Slide 5: Additive White Gaussian Noise
Kookmin University
Additive while Gaussian noise (AWGN) is a basic noise mode in communication system to simulate the effect of many random process in the real environment.
AWGN noise is added to OCC systems to simulate the effect of many random process in the real environment such as: the thermal vibrations of atoms in conductors, shot noise, black-body radiation from the earth and other warm objects, and from celestial sources such as the Sun, which effect to OCC systems.
The Gaussian distribution
Notes: The Gaussian distribution

## Slide 6: Blurring phenomenon
Kookmin University
The received image of LEDs which is contaminated by the blur process and noise can be obtained by a convolutional process of the blur kernel with a clear image of LEDs, followed by the addition of noise, as follows:
where y is the captured image matrix, h is the blur kernel matrix, x is the original image matrix, and n is the noise matrix
Note that all cells in a blur kernel will take equal values and add to one.

## Slide 7: References
[1] T. L. Pham, H. Nguyen, T. Nguyen, and Y. M. Jang, “A Novel Neural Network-Based Method for Decoding and Detecting of the DS8-PSK Scheme in an OCC System,” Applied Sciences, vol. 9, no. 11, p. 2242, May 2019.
[2] T. L. Pham, T. Nguyen, M. D. Thieu, H. Nguyen, H. Nguyen and Y. M. Jang, “An Artificial Intelligence-Based Error Correction for Optical Camera Communication," 2019 Eleventh International Conference on Ubiquitous and Future Networks (ICUFN), Zagreb, 2019