## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Extension of the 802.15.4 FSK PHY for utility applications
Date Submitted: December 2019
Source: Hiroshi Harada(NICT), Yoshio Kashiwagi(NISSIN SYSTEMS),
Tomohiro Ikuta(ROHM), Kiyoshi Fukui(OKI),
Takashi Kuramochi(LAPIS SEMICONDUCTOR)
Voice: +81-45-476-9295, E-Mail: kuramochi722@dsn.lapis-semi.com
Abstract: Presents requirements derived from utility networking experience which suggest modestly higher data rates with low power consumption for battery operated applications, and suggests simple enhancement to the existing standard to address these requirements.
Purpose: Stimulate thought and identify potential enhancements.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
Higher data rate requirements in IEEE802.15.4 derived from utility use cases
Input from utilities and system vendors
Focus on enhancing current IEEE802.15.4 PHY

## Slide 3: Motivation
Battery operated
  10 years operation
  Simple modulation scheme
Higher data rates
  Increase the number of nodes.
  Detailed information not only electricity but also gas and water.
  OTA updates.
Adaptive RF link optimization
  Mix of performance needs
  Ability to adjust to changing RF conditions

## Slide 4: Proposals
Battery operated
FSK modulation is the best choice for low power operation
Higher data rates
Modest increases – still low Mb/sec.
Adaptive RF link optimization
Multi-rate covers 50,100,150,300,400,600,800kbps in simple FSK modulation.

## Slide 5: Current FSK options in IEEE 802.15.4
Frequency band (MHz) | Parameter | Operating mode |  |  |  |  |  |  | 
 |  | #1 | #2 | #3 | #4 |  |  |  | 
920-928 MHz | Data rate (kb/s) | 50 | 100 | 200 | 400 |  |  |  | 
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK |  |  |  | 
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 |  |  |  | 
 | Channel spacing | 200 | 400 | 600 | 600 |  |  |  | 
 | Standard | 802.15.4-2015 |  |  |  |  |  |  | 

## Slide 6: Example of obvious extension
Frequency band (MHz) | Parameter | Operating mode |  |  |  |  |  |  | 
 |  | #1 | #2 | #3 | #4 | #XX | #XX | #XX | #XX
920-928 MHz | Data rate (kb/s) | 50 | 100 | 200 | 400 | 400 | 600 | 600 | 800
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK | 2-FSK | 2-FSK | 4-FSK | 4-FSK
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 | 0.5 | 0.4 | 0.5 | 0.33
 | Channel spacing | 200 | 400 | 600 | 600 | 200 * N 1≦N≦5 | 200 * N 1≦N≦5 | 200 * N 1≦N≦5 | 200 * N 1≦N≦5
 | Standard | 802.15.4-2015 |  |  |  | Proposed |  |  | 
N ≥ 6

## Slide 7: Example: Obvious extensions
Higher data rates of FSK implementations commercially available.
One single FSK modulation covers low to high date rates.

## Slide 8: What next?
We ask the Working Group to consider minor extension of the FSK in IEEE802.15.4 PHY as suggested in our examples.