## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposed High Level System Requirements]
Date Submitted: [16 Jan, 2020]
Source: [Menashe Shahar] Company [Ondas Networks]
Address [165 Gibraltar Ct, Sunnyvale, CA. 94089, USA]
Voice:[+1 669 350-0422], E-Mail:[menashe.Shahar@Ondas.com]
Re: [802.15.16t Task Group SRD]
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: [Proposed High Level System Requirements.]
Purpose: [Discussion document to help drive development of System Requirements Document (SRD)]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposed High Level System Requirements
Menashe Shahar
Ondas Networks

## Slide 3: Proposed High Level System Requirements for 802.16t
802.16t will be a standard air interface protocol focused on long range wireless communication requirements of mission critical organizations including electrical utilities, oil and gas, rails, UAVs, government security and others
802.16t will support a wide range of applications:
  Low throughput remote command and control applications referred to as Mission Critical Internet of Things (MC-IoT). These applications are best described by message length, periodicity, reliability, and latency in downlink and in uplink.
  Higher throughput applications, e.g. those data streaming (video/audio). These are best characterized by throughput, latency/jitter, and reliability in downlink and uplink.
Note: 802.16t is an air interface protocol. As such, it is focused on interoperability between base stations and remote stations from multiple vendors. Product requirements which have no direct or indirect impact on the air interface protocol are not specified

## Slide 4: Proposed High Level System Requirements for 802.16t
Support for 1000’s of endpoint devices per sector (known as “massive connectivity”) in a Point to Multi-Point architecture
  An example of massive connectivity requirement includes rapid reconnection of all remotes in a sector after a base station failure has occurred.
Throughput and latency requirements per endpoint:
  Many endpoints run low throughput, critical or non-critical latency applications. They should be served by low-end remote stations.
  Some endpoints run substantial throughput and sometimes also low latency applications. They should be served by high-end remote stations.
The air interface protocol will support concurrent operation of both low-end and high-end remotes on the same sector / base station
Low-end remote station specific requirements
  Limited throughput, Limited total bandwidth, Low power consumption, Low complexity
  Low-end device can trade off power consumption for latency
High-end remote station specific requirements
  Support high throughput over relatively high total bandwidth. Supports low latency for time critical applications.

## Slide 5: Examples of Low Throughput Applications
Solar Inverter Control (350 bytes every 5 sec)
RR Crossing Control (15-20 bps)
Drone Position Reports (tbd)
Well Pump On/Off Control (tbd)
…

## Slide 6: Examples of Higher Throughput Applications
Substation monitoring (1.4 Mbps)
Video surveillance (throughput depends on resolution and frame rate)
….

## Slide 7: General Requirements for 802.16t
Latency requirements: TBD
Frequency utilization requirements: TBD
Coverage requirements
  Long range single hop coverage (e.g., up to 50+ miles cell radius):
  Receiver sensitivity requirement
  TDD frame structure requirements
  Support of repeater for range extension (?)
Mission Critical Related Requirements
  Predictable performance
    Licensed band (mandated by the PAR)
    Central scheduling
    QOS
  High Security
  Reliability / Availability
Mobility requirements
  Maximum speed: TBD
  Need to have actual use case requirements for mobility and if mobile, what is the speed?
    Level 1 – fixed, handover only
    Level 2 – nomadic, slow movement
    Level 3 – Mobile: rapid movement - vehicular

## Slide 8: Spectrum Related Requirements for 802.16t
Operation in paired or unpaired continuous licensed bands available for private networks (e.g., AMTS, IVDS, 454 A2G, 700 MHz A-Block, RR 900 MHz, 1.4 GHz).
  Support for partition of these bands into multiple channels is required for frequency reuse and link budget/coverage considerations.
Operation in Private Land Mobile Radio (PLMR) bands (e.g., RR160 MHz).
  PLMR channels and bands are available worldwide.
  Common PLMR channel bandwidth: 6.25, 12.5, 25 and 50 kHz
  Special PLMR channel bandwidth: 5, 7.5 and 15 kHz
  Multiple adjacent or non-adjacent PLMR channels in the same band will be combined to support higher throughput services.
  Support of voice/data coexistence in low utilization voice channels. Voice will have priority over data.
    Case 1: The license is owned by the same entity for the voice and data
    Case 2: The voice license is owned by a different entity than the data system. Non-exclusive / shared use

## Slide 9: Duplexing Requirements for 802.16t
TDD will be used in unpaired spectrum and in paired spectrum if allowed by the applicable regulation authority. A highly asymmetrical or reverse asymmetrical DL:UL ratio (e.g., 1:10 to 10:1) should be supported.
  Typical IoT application is highly reverse asymmetrical.
HD-FDD or FDD will be used in paired spectrum if TDD is not allowed
FDD will be used in paired spectrum if the latency requirements cannot be satisfied by TDD