## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title : Requirements and challenges regarding OCC-based real time health monitoring system [April, 2020]
Source : Moh. Khalid Hasan and Yeong Min Jang
Company : [Kookmin University]
Address : [Seoul, Korea]
Voice : [+82-2-910-5068], E-Mail: [yjang@kookmin.ac.kr]
Re :
Abstract : This document discusses about the transmitter and receiver considerations for OCC-based health monitoring systems.
Purpose : To specify the technical requirements and considerations for OCC-based eHealth system.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Introduction
Among the communication technologies that use optical spectrum, optical camera communication (OCC) is regarded as one of the most promising technologies.
The effect of reflected component of the light signal is almost negligible for OCC, particularly rendering OCC incredibly secure.
Unlike the RF-based technologies, OCC is less affected by interference.
The interfering element can be extracted spatially from the image sensor because each pixel acts as a photo detector.
The BER using OCC is almost zero when the communication distance is short.

## Slide 3: LED patch
The patch is embedded to the arms of a patient.
Because a direct LOS communication link must be developed between the patch and camera, the patch should be mounted to a completely uncovered part of a body.
One of the suitable scenarios for applying the proposed patch circuitry is a sleeping or unconscious patient.
The body signals pass through the analog to digital converter (ADC), which presents the digitalize signals.
The ADC is connected with the LED driver circuit.
The bio-signal is modulated with a small microcontroller circuit.

## Slide 4: Technical Requirements
LED patch Requirements:
Optimized irradiation pattern of LED light source.
Narrow angle emission pattern of LED.
Use of multi-hop transmissions.
Low power.
Small size.
Receiver requirements:
Optimal placement of receiver camera (e.g., CCTV).
Enhanced focal length.
Broader field of view and high resolution image sensor.

## Slide 5: Challenges
Excellent bit-error performance.
Line-of-sight path blockage.
The impact of the patch on the patient’s movement.
Flickering free optical channel.
Congruous cost support.

## Slide 6: Conclusions
Remote monitoring of patients’ health condition using IoT is a promising approach that may result in various convenient solutions to nursing assistants.
RF spectrum is mostly licensed and regulated, and its effect on human health is also a main concern.
Moreover, the signal-to-noise-plus-interference ratio in high distance can be decreased to a considerable extent, possibly leading to the increase in bit-error rate.
Therefore, OCC that uses a camera to receive data from a light-emitting diode (LED) can be utilized in eHealth to mitigate the limitations of RF.