## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Possible allocation of the frequency bands 275-296 GHz, 306-313 GHz, 318-333 GHz and 356-450 GHz to the mobile and fixed service on a primary basis for future 802.15 devices
Date Submitted: 15 June 2020
Source: Hiroyo Ogawa, Iwao Hosako, Akifumi Kasamatsu, Norihiko Sekine, Shingo Saito, Keizo Inagaki, Atsushi Kanno, Katsumi Fujii, Hirokazu Sawada
Company: National Institute of Information and Communications Technology (NICT)
Address 4-2-1, Nukuikita, Koganei, 184-8795, Tokyo, Japan
Voice:+ 81 42 327 5043, FAX: , E-Mail: hiroyoogawa@nict.go.jp
Re: n/a
Abstract: The document provides information on how to allocate the frequency bands 275-296 GHz, 306-313 GHz, 318-333 GHz and 356-450 GHz on a primary basis which were identified by RR No. 5.564A to the land mobile and fixed service applications.
Purpose: Information to the Technical Advisory Group THz.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Background
The document [1][2] proposed to use the additional frequency band 252-275 GHz which are already allocated to the mobile service for TG3d devices so that the contiguous bandwidth over 40 GHz can be achieved.
The basic channel bandwidth for TG3d devices is 2.160 GHz. Four bonded channel bonding is applied to create the second basic channel whose channel bandwidth is 8.640 GHz, as shown below [1].
To accommodate such broadband channels, the contiguous bandwidth over 20 GHz is required for TG3d device operation.
The frequency bands 275-296 GHz, 306-313 GHz, 318-333 GHz and 356-450 GHz are identified for use by administrations for the implementation of land mobile and fixed service applications, in accordance with RR No. 5.564A [3][4].
CH1
CH2
CH3
CH4
2.160GHz
2.160GHz
2.160GHz
2.160GHz
8.640GHz
8.640GHz
8.640GHz
8.640GHz
8.640GHz
252GHz
BW=43.2GHz
295.2GHz

## Slide 3
Global Commercialization of TG3d Device from Spectrum Point of View
The first contiguous bandwidth of 44 GHz is achieved as follows:
The second contiguous bandwidth of 94 GHz is achieved as follows:
The following constraint is included in RR No.5.564A because the frequency bands are identified, but not allocated in the Table of Frequency Allocations.
WRC-27 agenda item which allocates the frequency bands for mobile and fixed services on a primary basis is preferable to globally or regionally commercialize TG3d devices and other applications such as 6G (5G Beyond).
252 GHz
275 GHz
296 GHz*
Already allocated in RR
New identified frequency band
* The frequency of 320 GHz was originally proposed by Ref.[2], but the frequency bands 296-306 GHz and 313-318 GHz were not identified for mobile service applications in accordance with RR No. 5.564A.
356 GHz
450 GHz
New identified frequency band
The use of the above-mentioned frequency bands by land mobile and fixed service applications does not preclude use by, and does not establish priority over, any other applications of radio services in the range of 275-450 GHz.

## Slide 4
Possible Table of Frequency Allocations 275-296 GHz
New Table of Frequency Allocations in the frequency band 275-296 GHz to the mobile and fixed services including Earth exploration-satellite service and radio astronomy service as primary basis.
Allocation to services | 
275-286 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
286-296 GHz | FIXED MOBILE RADIO ASTRONOMY

## Slide 5
Possible Table of Frequency Allocations 306-313 GHz
New Table of Frequency Allocations in the frequency band 306-313 GHz to the mobile and fixed services including Earth exploration-satellite service and radio astronomy service as primary basis.
Allocation to services | 
306-313 GHz | FIXED MOBILE RADIO ASTRONOMY

## Slide 6
Possible Table of Frequency Allocations 318-333 GHz
New Table of Frequency Allocations in the frequency band 318-333 GHz to the mobile and fixed services including Earth exploration-satellite service and radio astronomy service as primary basis.
Allocation to services | 
318-323 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
323-327 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE
327-333 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY

## Slide 7
Possible Table of Frequency Allocations 356-450 GHz (1)
New Table of Frequency Allocations of the frequency band 356-450 GHz to the mobile and fixed services including Earth exploration-satellite service and radio astronomy service as primary basis.
Allocation to services | 
356-361 GHz | FIXED MOBILE RADIO ASTRONOMY
361-365 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY

## Slide 8
Possible Table of Frequency Allocations 356-450 GHz (2)
Allocation to services | 
365-369 GHz | FIXED MOBILE RADIO ASTRONOMY
369-371 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
371-388 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE
388-392 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
392-397 GHz | FIXED MOBILE RADIO ASTRONOMY

## Slide 9
Possible Table of Frequency Allocations 356-450 GHz (3)
Allocation to services | 
397-399 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
399-409 GHz | FIXED MOBILE RADIO ASTRONOMY
409-411 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
411-416 GHz | FIXED MOBILE RADIO ASTRONOMY
416-424 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY

## Slide 10
Possible Table of Frequency Allocations 356-450 GHz (4)
Allocation to services | 
424-426 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE
426-434 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
434-439 GHz | FIXED MOBILE RADIO ASTRONOMY
439-442 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE RADIO ASTRONOMY
442-450 GHz | EARTH EXPLORATION-SATELLITE (passive) FIXED MOBILE

## Slide 11
Conclusion
The Table of Frequency Allocations proposed in this contribution is one example and not yet discussed in any regulatory organizations, however this information may be useful for IEEE802.15 TAG THZ to identify the future regulatory and standardization activities to globally commercialize TG3d devices.
IEEE802 should provide ITU-R more detailed technical and operational characteristics of mobile and fixed service applications operating in the frequency bands 275-296 GHz, 306-313 GHz, 318-333 GHz and 356-450 GHz if requested, because IEEE802 provided ITU-R useful technical information for sharing and compatible studies between TG3d devices and EESS passive sensors under WRC-19 agenda item 1.15.
IEEE802.15 TAG THZ should encourage administrations, from the industry point of view, to discuss the possible WRC-27 new agenda item which considers primary allocation of the frequency bands 275-296 GHz, 306-313 GHz, 318-333 GHz and 356-450 GHz to the mobile and fixed services for not only wireless PAN/LAN but also other wireless applications such as 6G (Beyond 5G).

## Slide 12
References
[1] 15-15-0038-00-003d-proposed-frequency-arrangements-to-section-10-of-tg3d-trd.
[2] 15-15-0052-01-003d-operational-frequency-band-for-tg3d-devices.
[3] 15-20-0149-01-0thz-results-of-wrc-2019-ai-1-15-and-its-impact-on-thz-communications.
[4] World radiocommunication Conference 2019 (WRC-19) Final Acts. https://www.itu.int/pub/R-ACT-WRC.14-2019