## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title : The Stripe Pattern’s Misalignment Reconstruction Based on Neural Network Scheme.
Date Submitted : [September, 2020]
Source : Md Faisal Ahmed, Moh. Khalid Hasan, Md. Shahjalal, and Yeong Min Jang
Company : [Kookmin University]
Address : [Seoul, Korea]
Voice : [+82-2-910-5068], E-Mail: [yjang@kookmin.ac.kr]
Re :
Abstract : This document discusses about the solution of deformation and displacement vector field created in the mobile condition in the image sensor using rolling shutter effect.
Purpose : To decrease the bit-error-rate (BER) that enable the system performance.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Introduction
Optical camera communications (OCC) operates in infrared or visible bands and exploit an image sensor as the receiver and light-emitting diodes (LEDs) as the transmitter. OCC offers several advantages such as lower power consumption, low cost, and high security.
A neural network is proposed for LED detection and improving the bit-error-rate in mobile scenarios. A new method based on the region-wise comparison and an existing method is used to remove the interference and noise generated from the neighboring light sources, respectively.
The NN can classify large image datasets with remarkable characteristics in several spatial layers and automatically learn from data through backpropagation.

## Slide 3: Neural network-based feature matching for reconstructing the original stripe pattern.
In mobile condition the camera and LEDs change automatically as a result some stripes in the image frame may overlap or change its position. This can decrease the performance of the system and BER goes higher.

## Slide 4: Neural network-based feature matching for reconstructing the original stripe pattern.
In NN-based feature matching technique, ﬁrst, each 5×5 kernel matrix in the image patches are checked using NN regression and compared with reference stripes.
The angle yielded due to the deformation is updated using the original inverse deformation, and the displaced vector ﬁeld is partially reconstructed by ﬁltering.
Afterward, every point of the stripes is resampled using spatial transformation to produce a warped image. Using backpropagation connected with NN regression, the steps are repeated in a loop until the original stripes are completely reconstructed.

## Slide 5: Technical considerations
In mobile condition focusing to the LED is the major consideration because of mismatch the stripe pattern can recognize properly.
However, accurately detection of the multiple LED is needed for data extraction technique. Besides each LED detection in the LED array become challenging when the gray scale value of the image cross the threshold.
The neighboring light sources create interference and distinguish, when the different kinds of receiver comes into the field-of-view of the camera. Afterward, noise can be removed by selecting the proper filter.