## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Regulatory Requirements Applicable to PLMR bands
Date Submitted: 2020-10-14
Source: Menashe Shahar, Ondas Networks
Abstract: Regulatory Requirements for PLMR Bands
Purpose: Requirements Contribution for 802.16t Working Group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
October 2020
Slide 2
Regulatory Requirements Applicable to PLMR bands
IEEE802.16t should enable compliance with applicable regulatory standards. The related air interface requirements should be considered.
Some of the requirements can be viewed as local product requirements. Others have impact on air interface protocol and interoperability.
Examples of standards applicable to PLMR bands:
  FCC Part 90
  ETSI EN 300 113

## Slide 3
October 2020
Slide 3
Transmitter Requirements
Typical emission requirements:
  Spectrum emission mask
  Adjacent Channel Leakage Ratio (ACLR)
  Adjacent Channel Power (ACP)
  Alternate channel power
  Occupied bandwidth/Max symbol rate
  Frequency utilization
The requirements vary between different standards and even between different FCC parts.
It is desired to maximize frequency utilization while meeting the out-band emission requirements.
    It is recommended to allow for a configurable symbol rate.

## Slide 4
October 2020
Slide 4
Receiver Requirements
Receiver sensitivity
Adjacent Channel Rejection/Adjacent Channel Selectivity
Blocking/Desensitization
Why receiver requirements are needed:
  Meet ETSI EN 300 113 requirements
  Support of voice/data coexistence in low utilization voice channels. Voice will have priority over data

## Slide 5
October 2020
Slide 5
FCC Part 90 Spectrum Emission Mask D

## Slide 6
October 2020
Slide 6
Examples of FCC Part 90 Requirements
FCC Part 90.209 – Bandwidth limitations:
  The standard provides a table which specifies the channel spacing and bandwidths for each frequency band, e.g., the authorized bandwidth in the 406 – 512 MHz band for 6.25 KHz/12.5 KHz and 25 KHz channels is 6KHz/11.25 KHz and 20 KHz respectively.
FCC Part 90.203(j) – Spectrum efficiency:
  Specifies minimum data rate for a given channel bandwidth, e.g., 4,800 bps/6.25 KHz channel

## Slide 7
October 2020
Slide 7
Operation in aggregated PLMR channels
Interpretation of FCC rules when operating in aggregated adjacent or non-adjacent channels:
  Unless the FCC has specific rules for aggregated PLMR channels, the rules should be followed in each channel individually, i.e., the emission constraints should be followed for each channel.
Meeting receiver performance requirements in aggregated adjacent and non-adjacent channels:
  When all channels are adjacent, traditional analog and digital bandpass filtering techniques can be used.
  When the channels are not adjacent to each other:
    The digital filter should be configurable according to the active channels and the gaps in between
    It is not practical to employ analog filtering. Good ACR and blocker performance relies on receiver dynamic range.