## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Evolution of UWB in IEEE 802]
Date Submitted: [6 November, 2020]
Source: [Ayman Naguib (Apple), Jochen Hammerschmidt (Apple)]
Address [One Apple Park Way, Cupertino, CA 95014, USA]
Voice:[], E-Mail:[ ayman_naguib (at) apple.com]
Re: [Contribution to the SC Working Group]
Abstract: [Presentation to proposed future directions and evolution of UWB wireless air interface in IEEE 802.15 to address future use case]
Purpose: [Discuss Evolution of UWB in IEEE 802]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 802.15.4z Time Line
802.15.4z TG started in May 2018.
iOS devices supporting 802.15.4z shipping since fall 2019
CCC chooses UWB as the air interface for its DCK specifications.
802.15.4z became an official IEEE standard in May 2020
Other forums and industry groups start considering UWB for its solutions (Oct 2019)
Android devices supporting 802.15.4z announced July 2020
Millions of smart portable devices devices supporting 802.15.4z are now enabling UWB applications for millions of users across the globe
802.15.4z UWB rocks …

## Slide 3: Future Directions for UWB (1)
Observations:
  An emerging trend in design new wireless air interfaces is to consider Communication, Sensing, Ranging, and Control in the design of new PHY & MAC protocols to accommodate different uses cases and scenarios.
      6G/5G Research
      802.11 already have a new PAR for MAC & PHY changes to use WiFi for sensing
  New wireless air interfaces are expected to support massive number of M2M links at very low power.
UWB and 4z actually already support some of that.
With some further improvement and development, UWB is in a good position to address many of the CSRC use cases targeted by other air interfaces in a way that strongly integrates with and builds on current 4z deployments

## Slide 4: Future Directions for UWB (2)
Spin out 4z/UWB and related building blocks from 802.15.4 into self-sufficient specification to enable strong UWB centric ecosystem
Example Phy & MAC improvements & feature enhancements relative to 4z baseline
  Enhance operating range, efficiency (complexity/power), accuracy, and integrity via suitable new waveforms and signaling techniques
  Improved capabilities for native discovery / connection setup
  Further optimized protocol framework targeting specific use cases
  Improved support for data-less ranging
  Consider proliferation of new channels / frequency bands
  Enhancements for “Depth Sensing & Mapping”
  Limit use of payload bearing formats to control signaling and non-streaming data applications to prevent “self-cannibalization” of UWB’s strong nascent success
Regulatory & Coexistence Considerations