## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
  Submission Title: 870 MHz Band Designator Issue
  Date Submitted: November 7, 2020
  Source: Clint Powell (PWC LLC)
  Address: []
  Voice: +1 480 586-8457], E-Mail:[cpowell@ieee.org]
  Re: IEEE 802.15.4 2020 Error
  Abstract: Issue found with IEEE 802.15.4 2020.
  Purpose: Address Band Designator issue found in IEEE 802.15.4 2020.
  Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
  Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: 870 MHz Band Designator Issue
Clint Powell (PWC LLC)

## Slide 3
Problem Description
  The 870 MHz Band designator for the 870-876 MHz band in the EU for FSK M2 (100 kbps) lists 30 channels in Table 10-14
  The start Fc is 870.2 MHz
  Which puts the last channel Fc at 870.2 MHz + 29*0.2 MHz = 876 MHz
  This would cause the upper half of the transmit PSD to fall above 876 MHz which is not allowed
Problem Resolution
  Change the # of channels to 29 for the 870 MHz Band designator so that the last channel Fc is at 870.2 MHz + 28*0.2 MHz = 875.8 MHz