## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Proposal for directions of UWB]
Date Submitted: [15 December 2020]
Source: David Barras [3db Access, Switzerland]
Boris Danev [3db Access, Switzerland]
Re: [Contributions to the SC Working Group]
Abstract: [Propose future directions for UWB wireless air interface in IEEE 802.15]
Purpose: [Discuss on next features and evolution of UWB air interface]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Motivation
To initiate discussions on the technical features (PHY and MAC) of the next Impulse-Radio UWB wireless interface
Main focus of UWB – Key Aspects
Develop IR-UWB as a robust ranging wireless technology with a strong focus on the following features:
  Low Power & Low Energy Consumption
  High Ranging Accuracy & Reliability
  Interoperable & Verifiable Security

## Slide 3: Low Power & Low Energy Considerations
Target a low power consumption comparable or less than a Bluetooth Low-Energy device:
  Order of magnitude ≈ 10 mW average Rx/Tx power
Maintain short ranging frame for low energy consumption
  Order of magnitude ≈ 1 μJ per ranging (with small amount of data)
Low power & energy helps in building a UWB-centric system
  Optimized MAC features for standalone ranging ecosystem
  No need for a third-party wireless technology (costs, latency in connections,…)
  UWB wake-up radios

## Slide 4: Ranging Accuracy and Reliability
Consider frequency channelization for adding diversity
Running several ranging at slightly different center frequencies helps in mitigating some adverse antenna effects (notches in the radiation pattern that creates blind spots)
Some frequency agility could be advantageously used to perform multiple ranging on several channels in less than one millisecond (for optimizing the use of UWB air resource which are limited by the regulation)
Consider also new channel allocation for WiFi 6G mitigation

## Slide 5: Interoperable & Verifiable Security
Consider well specified PHY/MAC constructs for security-critical ranging applications (e.g., access control, mobile payments)
  Challenge-response protocols
Interoperable security between devices
  Defined and verifiable Security Levels for ranging
  Precise definitions and implementation guidelines
  Include application notes to the standard