## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Technical Proposal on Channel Numbering for TG4aa JRE]
Date Submitted: [19th January, 2021]
Source: [Hiroshi Harada, Ryota Okumura] Company [Kyoto University]
Address : Kyoto University [Yoshidahonmachi, Sakyo-ku, Kyoto 606-8501 Japan]
Voice:[+81-75-753-5318], FAX: [], E-Mail:[hiroshi.harada@i.kyoto-u.ac.jp]
Re: [] Abstract: [This document includes Technical Contributions toward the development the amendment of IEEE Std 802.15.4-2020] Purpose: [Technical Proposal for TG4aa JRE.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
Frequency band (MHz) | Parameter | Operating mode |  |  |  |  |  |  | 
 |  | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8
920-928 MHz | Data rate (kb/s) | 50 | 100 | 200 | 400 | 400 | 600 | 600 | 800
 | Modulation | 2-FSK | 2-FSK | 2-FSK | 4-FSK | 2-FSK | 2-FSK | 4-FSK | 4-FSK
 | Modulation index | 1.0 | 1.0 | 1.0 | 0.33 | 0.5 | 0.4 | 0.5 | 0.33
 | Channel spacing (kHz) | 200 | 400 | 600 | 600 | 200 * N 1≦N≦5 [2] | 200 * N 1≦N≦5 [2] | 200 * N 1≦N≦5 [2] | 200 * N 1≦N≦5 [2]
 | Standard | 802.15.4-2020 [1] |  |  |  | Proposed |  |  | 
Note: N is integer number
Proposed Parameters
Overlapped channel spacing was proposed

## Slide 3
Current Channel Numbering [1]
Table 10-14
Only one type of channel spacing per operating mode
a)
a) Modification for 38 is proposed in Cor2 [3]

## Slide 4
Current Channel Numbering
Only one type of channel spacing per operating mode
Frequency (MHz)
920
928
922
924
926
 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37
 | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓
0 |  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 10 |  | 11 |  | 12 |  | 13 |  | 14 |  | 15 |  | 16 |  | 17 |  | 
↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | 
SUN FSK operating mode #1
TotalNumChan=38, ChanSpacing=0.2MHz, ChanCenterFreq0 =920.6MHz
SUN FSK operating mode #2
TotalNumChan=18, ChanSpacing=0.4MHz, ChanCenterFreq0 =920.9MHz
↓: Center Frequency

## Slide 5
Proposed Serial Channel Numbering
N=1
Channels
200kHz spacing
N=2
Channels
400kHz spacing
N=3
Channels
600kHz spacing
N=4
Channels
800kHz spacing
N=5
Channels
1MHz spacing
in MHz,
for
in MHz,
for
in MHz,
for
in MHz,
for
in MHz,
for
Channel numbers for different spacings are defined in continuance
: ChanCenterFreq
ChanCenterFreq0 for each N
: TotalNumChan for each N
SUN FSK operating mode #5, #6, #7, #8

## Slide 6
Proposed Serial Channel Numbering
Channel numbers for different spacings are defined in continuance
 |  | 34 |  | 35 |  | 36 |  | 37 |  | 38 |  | 39 |  | 40 |  | 41 |  | 42 |  | 43 |  | 44 |  | 45 |  | 46 |  | 47 |  | 48 |  | 49 |  | 50 |  | 
 |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | ↓ |  | 
 |  |  |  | 51 |  |  | 52 |  |  | 53 |  |  | 54 |  |  | 55 |  |  | 56 |  |  | 57 |  |  | 58 |  |  | 59 |  |  | 60 |  |  | 61 |  |  | 62 | 
 |  |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ |  |  | ↓ | 
 |  | 63 |  |  |  | 64 |  |  |  | 65 |  |  |  | 66 |  |  |  | 67 |  |  |  | 68 |  |  |  | 69 |  |  |  | 70 |  |  |  | 71 |  | 
 |  | ↓ |  |  |  | ↓ |  |  |  | ↓ |  |  |  | ↓ |  |  |  | ↓ |  |  |  | ↓ |  |  |  | ↓ |  |  |  | ↓ |  |  |  | ↓ |  | 
 |  | 72 |  |  |  |  | 73 |  |  |  |  | 74 |  |  |  |  | 75 |  |  |  |  | 76 |  |  |  |  | 77 |  |  |  |  | 78 |  | 
 |  | ↓ |  |  |  |  | ↓ |  |  |  |  | ↓ |  |  |  |  | ↓ |  |  |  |  | ↓ |  |  |  |  | ↓ |  |  |  |  | ↓ |  | 
Frequency (MHz)
920
928
922
924
926
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 
 |  | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | 
N=1
Channels
200kHz spacing
N=2
Channels
400kHz spacing
N=3
Channels
600kHz spacing
N=4
Channels
800kHz spacing
N=5
Channels
1MHz spacing
↓: Center Frequency
SUN FSK operating mode #5, #6, #7, #8

## Slide 7
Proposed Serial Channel Numbering
Channel numbers for different spacings are defined in continuance
In a PAN, either channels 0–33, 34–50, 51–62, 63–71, or 72–78 are used.
 | ChanSpacing | ChanCenterFreq0 for N | Last ChanCenterFreq | NumChan | TotalNumChan for N
=1 | 0.2 MHz | 921.0 MHz | 927.6 MHz | 0–33 | 34
=2 | 0.4 MHz | 921.0 MHz | 927.4 MHz | 34–50 | 17
=3 | 0.6 MHz | 921.0 MHz | 927.6 MHz | 51–62 | 12
=4 | 0.8 MHz | 921.0 MHz | 927.4 MHz | 63–71 | 9
=5 | 1.0 MHz | 921.0 MHz | 927.0 MHz | 72–78 | 7
 | ChanSpacing | ChanCenterFreq0 for N | Last ChanCenterFreq | NumChan | TotalNumChan for N
 | 0.2 MHz | 921.0 MHz | 927.6 MHz | 0–33 | 34
 | 0.4 MHz | 921.0 MHz | 927.4 MHz | 34–50 | 17
 | 0.6 MHz | 921.0 MHz | 927.6 MHz | 51–62 | 12
 | 0.8 MHz | 921.0 MHz | 927.4 MHz | 63–71 | 9
 | 1.0 MHz | 921.0 MHz | 927.0 MHz | 72–78 | 7
Sum: 79

## Slide 8
Example: Channel Numbering in IEEE 802.15.4d-2009 [4]

## Slide 9
Example: Channel Numbering in IEEE 802.15.4d-2009 [4]
Channel Num | Center Frequency (MHz)
0 | 951.2
1 | 951.8
2 | 952.4
3 | 953.0
4 | 953.6
5 | 954.2
6 | 954.8
7 | 955.4
Channel Num | Center Frequency (MHz)
8 | 954.4
9 | 954.6
Channel Num | Center Frequency (MHz)
10 | 951.1
11 | 951.5
12 | 951.9
13 | 952.3
14 | 952.7
15 | 953.1
16 | 953.5
17 | 953.9
18 | 954.3
19 | 954.7
20 | 955.1
21 | 955.5
1mW BPSK
10mW BPSK
GFSK
Define channels for different systems with a single serial channel number

## Slide 10
Reference
[1] IEEE, “IEEE 802.15.4-2020,” July 2020.
[2] ARIB, “ARIB STD-T108 920MHz-BAND TELEMETER, TELECONTROLAND DATA TRANSMISSION RADIO EQUIPMENT ver 1.3,” Apr. 2019.
[3] IEEE 802.15-20-0397-00-Cor2, Dec. 2020.
[4] IEEE, “IEEE 802.15.4d-2009,” Apr. 2009.