## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title : Optical Camera Communication based Real-Time Health Monitoring System
Date Submitted : [January, 2021]
Source : Md Faisal Ahmed and Yeong Min Jang
Company : [Kookmin University]
Address : [Seoul, Korea]
Voice : [+82-2-910-5068], E-Mail: [yjang@kookmin.ac.kr]
Re :
Abstract : This document discusses about the application of optical camera communication (OCC) for health monitoring application.
Purpose : To illustrate the feasibility of OCC in eHealth application.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Introduction
The healthcare data are collected using a wearable sensor connected to a communication device to provide healthcare services across the users.
The transmission of health information can be done wired and wireless. Wired-connected sensors are odd, costly, and consume high power.
On the other hand, currently, radio-frequency (RF)-based devices, such as Bluetooth, ZigBee, and 6LowPAN are mostly used for wireless communication objectives.
However, it can cause serious damage to human health and negative biological effects in the human body when long-term involvement with electromagnetic radiation (EMR) originating for RF.

## Slide 3: Overview of the proposed health monitoring system
In this study, we propose an optical camera communication (OCC) system to transmit data. Generally, OCC is a line-of-sight (LoS) technology that uses an LED as a transmitter, a camera image sensor as a receiver, and visible light as the communication medium. OCC supports several constructive characteristics such as low cost, high security, low power consumption, and enhanced reliability. Because the system uses visible light, it is free from electromagnetic interferences and completely risk-free to human health.

## Slide 4: Overview of the proposed health monitoring system
In this work, an indoor scenario is considered, wherein a patient’s health is continuously monitored. Using a sensor fixed in a finger of the patient, we collected the patient’s healthcare data, specifically the HR and SpO2 data.
The sensor is connected with a patch circuit attached as an armband in the patient’s body. The patch is composed of an LED array, modulated using the sensing data.
A CCTV camera is used for surveillance and receiving data from the LED array using OCC simultaneously. Afterward, the data are processed and accessed in real-time by the remote monitor.
Simultaneously, the data are transmitted to a cloud server, which can be further accessed by any authorized person using a private user ID and password. Figure 1 shows a block diagram of the proposed system.

## Slide 5: Technical considerations
In this technical paper, we design and implement an optical camera communication system for real-time remote monitoring of patient's heart rate (HR) and oxygen saturation (SpO2) data.
The data is collected and transmitted by a patch circuit which comprises a MAX30102 sensor and an RGB LED array.
A close circuit television camera is used not only for surveillance but also for receiving the data simultaneously. The LED is modulated using color intensities, and the data can be retrieved regardless of any orientations of the LED array.