## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: The 5 Criteria table and differences in technical requirements for NG UWB – edits to data streaming rows
Date Submitted: February 8th 2021
Source: Frederic Nabki (Spark Microsystems)
Address: 1201 rue Barré Suite 201, Montreal QC, Canada
E-Mail: frederic.nabki@sparkmicro.ca
Re: Criteria for Standards Development (CSD) and PAR for next generation UWB project]
Abstract: Summary table of features and main characteristics in next generation UWB for CSD and PAR – attempt at filling in data streaming rows
Purpose: Discuss low-power low latency data communications applications
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
1/3

## Slide 2
Five Criteria (5C) requirements, or “The 5 Critters” for UWB NG
Table for CSD
2/3
Classes of Devices​ | Application / Use cases​ | Broad Market Potential​ | Compatibility​ | Distinct Identity​ | Technical feasibility​ | Economic feasibility​
​ | ​ | a) Broad sets of applicability​ b) Multiple vendors and numeours users​ | a) Will comply with 802?​ b) supply response if a) = no​ c) Compatibility with IEEE 802.15​ d) Conformance with IEEE 802.15 MAC​ | Substantially different from other 802.15 specs/solutions​ | a) demonstrated feasability​ b) proven similar technology via test/mod/sim​ c) confidence in reliability​ | a) known cost factors​ b) balanced costs​ c) installation costs​ d) operational costs​
Data streaming​ | Audio Real time / low latency streaming​ - headphones, hearables​ | a) Yes, see applications ​ b) Yes, many players already there​ and have significant latency and audio quality limitations | TBD :​ MAC enhancement and PHY​ | Enable very low power operation (e.g. sub 10 mW)​, very low latency​ (e.g. 5ms), high data rate​ (e.g. 1.5 Mbps uncompressed audio payload) Enable merged operation with low latency controlelrs/peripherals data streams | a) Yes​, demonstrated operation b) TBD c) Yes​ | a) yes​, POCs validated b) no infrastructure cost​ c) no sinificant installation cost d) no operational cost​
 | Audio/Video real time / low latency streaming​ - AR with multi-channel a/v (Gaming)​ | a) Yes, see applications ​ b) Yes, many players already there​ | TBD :​ MAC enhancement and PHY​ | Enable very low power operation​ (sub 10 mW) Very low latency​ High data rate​ Sub 10us controller synch. | a) Yes​ b) TBD c) Yes​ | a) yes​ b) no infrastructure cost​ c) no sinificant installation cost d) no operational cost​
 | Network of objects​ with frequent data transport - Sensors networks (Medical , Transport, Agriculture...)​ - BAN (Medical, ER, Gaming)​ - PAN (Gaming, Home office)​ | a) Yes, see applications ​ b) Yes, many players already there​ | TBD :​ MAC enhancement and PHY​ | Enable very low power operation while streaming telemetry or control data at high polling rates​ (e.g. microwatt-scale system power consumption with sub second of second scale intervals) Very low latency​ when required High data rate​ when required | a) Yes​ b) TBD​ c) Yes​ | a) yes​ b) no infrastructure cost​ c) no sinificant installation cost d) no operational cost​

## Slide 3
3/3
Classes of Devices​ | Application / Use cases​ | Link budget​ | Payloads​ | Current cons. (in active state)​ | Market acceptance criteria​
​ ​ ​ ​ | ​ | classification (assumptions: 0dBi antenna):​ - very high (PL > 90 dB, d > 100m)​ - moderate (PL≈ 80 dB, d ≈ 30 m)​ - proximity (PL≈ 60 dB, d ≈ 3m)​ | classification:​ - short payload, small duty cycles​ - continuous payload, larger duty cycle​ | classifications:​ - very low to low (up to 10 mA)​ - moderate to high (100mA+)​ | key words:​ cost, reliability (QoS), integrity, security​
Data streaming​ ​ | Audio Real time / low latency streaming​ - headphones, hearables​ | Proximity to moderate​ | continuous payload, ​ moderate duty cycles (e.g. 2-10 Mbps payload at low latency) ​ with spectrum sensing mitigation | very low to low​ (headphone, in-ear devices, ...)​ | Cost, reliability​ [consumer]​ ​
 | Audio/Video real time / low latency streaming​ - AR with multi-channel a/v (Gaming)​ | Proximity to moderate​ | continuous payload, ​ moderate duty cycles ​(e.g. 2-10 Mbps payload at low latency) with spectrum sensing mitigation | very low to low​ (AR glasses, controllers...)​ | Cost, reliability​ [consumer]​
 | Network of objects​ - Sensors network ( Medical , Transport, Agriculture...)​ - BAN (Medical, ER, Gaming)​ - PAN (Gaming, Home office)​ | Proximity to moderate​ | Short payload​s Low duty cycles​ | very low to low​ (remote sensors)​ | Cost, reliability, security (industrial, consumer, medical]​
Differences in technical requirements and constraints
Main Features and characteristics