## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [802.15.4z - HRP UWB PHY - HPRF mode preamble sequence cross-correlation properties]
Date Submitted: [9th March 2021]
Source: [Billy Verso, Jarek Niewczas ] Company [Qorvo, Inc.]
Address [ ]
E-Mail:[billy.verso (at) qorvo.com]
Re: [An omission from the published IEEE Std 802.15.4z™‐2020 standard]
Abstract: [This submission makes public some text relating to the preamble sequence’s cross-correlation properties, which was (accidentally) omitted from IEEE Std 802.15.4z and provides additional background information giving the cross-correlation results upon which the omitted paragraph was based.]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
It has been brought to our attention that an informative paragraph present in the final balloted draft P802.15.4z™/D08 was omitted from the published standard IEEE Std 802.15.4z™‐2020.
  The missing paragraph relates to the cross-correlation properties of the preamble sequences
This submission provides the omitted text, which we expect is not publicly available elsewhere given that the 4z drafts are private to the IEEE 802.15 working group.
  In addition, we provide results to further inform interested parties about the cross-correlation properties of the chosen preamble sequences.

## Slide 3: Omitted paragraph
The following paragraph should have appeared beneath Table 15-7a, Length 91 ternary codes for the HRP-ERDEV in IEEE Std 802.15.4z™‐2020:
Note that among these codes the pairs of codes selected by code indices {25 and 26}, {27 and 28} or {29 and 30} have the lowest cross-correlation value between the codes of the pair, and therefore would be the preferential choice to use where there are two independent networks co-existing, i.e., choosing one code from the pair for each network.

## Slide 4: Cross-Correlation Results
The table below gives the cross-correlation results upon which the omitted paragraph was based:
Cross correlation |  | Code index |  |  |  |  |  |  | 
 |  | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32
Code index | 25 | 81 | 15 | 25 | 24 | 24 | 17 | 27 | 18
 | 26 | 15 | 81 | 24 | 17 | 25 | 24 | 24 | 23
 | 27 | 25 | 24 | 81 | 15 | 17 | 24 | 25 | 24
 | 28 | 24 | 17 | 15 | 81 | 24 | 25 | 20 | 27
 | 29 | 24 | 25 | 17 | 24 | 81 | 15 | 18 | 20
 | 30 | 17 | 24 | 24 | 25 | 15 | 81 | 23 | 25
 | 31 | 27 | 24 | 25 | 20 | 18 | 23 | 81 | 24
 | 32 | 18 | 23 | 24 | 27 | 20 | 25 | 24 | 81
Cross-correlation between HPRF mode preamble sequences (length 91 ternary codes) for the HRP-ERDEV |  |  |  |  |  |  |  |  | 

## Slide 5
THE END