## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title : Data Collection from LED Matrix in Different Rotation of LED in Optical Camera Communication
Date Submitted : [March, 2021]
Source : Md Faisal Ahmed, Moh. Khalid Hasan, Md. Shahjalal, and Yeong Min Jang
Company : [Kookmin University]
Address : [Seoul, Korea]
Voice : [+82-2-910-5068], E-Mail: [yjang@kookmin.ac.kr]
Re :
Abstract : This document discusses about the orientation of LED matrix during data collection from the patient’s body.
Purpose : To collect data from the patient’s body at any rotation without hampering the communication.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release : The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Slide 1

## Slide 2: Introduction
The retrieval of the received signal significantly depends on the orientation of the transmitter.
It will not be sophisticated to maintain a fixed position of the patch as the placement of the hand may be altered on the basis of the patients’ requirements.
However, different orientations of the LED array will generate substantial errors in the data.
By measuring the amount of inflection of the LED array, we have avoided the challenge.

## Slide 3: The orientation procedure and data collection
Figure 1 shows different orientations of the LED array compared with the original image. Here, three LEDs are reserved in the OFF position to indicate the starting and ending points of each IR, BPM, and SpO2 data. The three positions will be unchanged in the LED matrix, disregarding any inflection.
Figure 1: 360 degree orientation solution during data collection in OCC

## Slide 4: The orientation procedure and data collection
Thus, in the original LED matrix, the amount of orientation is calculated to locate the positions of the OFF LEDs.
The data may vary significantly; thus, any other LEDs can progress in the OFF state if the data are too small.
However, as we defined the OFF LEDs at the end of each dataset, the newly OFF LEDs will appear sequentially just before the specific OFF LED, determining the positions of the OFF LEDs easily.
The starting point of the dataset is defined after measuring the inflection angle. Then, the symbols are decoded using the color code sequence in the LED matrix.

## Slide 5: Technical considerations
A real-time health monitoring system is designed with a MAX30102 sensor that is used to collect the IR, SpO2, and BPM data and connected to a patch mounted on the patient′s hand.
The LED array was modulated using CIM and the data were encoded with a unique key to enhance the security.
Each LED in the array was detected using an NN, and another feature-extraction-based NN was used to recognize the colors precisely.
A mechanism was also developed to assuage the challenge of different LED array orientations in the decoding procedure.