## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: SG15.6a Channel and Environmental Models Including EMC/EMI of Human and Vehicle Body Area Networks(HBAN and VBAN)
Date Submitted: May 13th, 2021
Source: Takumi Kobayashi, Minsoo Kim, Marco Hernandez, Ryuji Kohno
Company: (1)Yokohama National University (2) YRP International Alliance Institute
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp, Kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract: This provides how channel and environmental model should be defined and developed for human body area network(HBAN) and vehicle body area network(VBAN) for amendment of IEEE802.15.6-2012 for wireless medical body area network(BAN) with enhanced dependability.
Purpose: Material for discussion in P802.15.6a SG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: SG15.6a Channel and Environmental Models of Human and Vehicle Body Area Networks (HBAN and VBAN)Including EMC/EMI Issues
Takumi Kobayashi
(YNU/YRP-IAI)

## Slide 3: Channel models and scenarios in IEEE802.15.6-2012
IEEE 802.15.6-2012 channel models considered
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
CM1, 2, 3, 4
Scenario 1, to Scenario 7. (S1 – S7)
IEEE P802.15-08-0780-12-0006-TG6

## Slide 4: Classification of Channel and Environment Models for Human and Vehicle Body Area Networks (HBAN&VBAN)
Note:
HBAN-model:
-Environment with co-existing systems is not considered.
VBAN model:
Key-less entry system
Localization in-body, on-body
Most dominant model should be defined and separatory defined as Mandatory and Optional.
Channel model
HBAN model
VBAN model
In-body (Implant)
On-body
Around body
Outdoor
Indoor
Home
Office
Medical (e.g. Hospital)
In-vehicle
On-vehicle
Around vehicle
Engine room
Cabin
Through engine room and cabin
Roof
Side Right/Left/Front/back
Bottom
Static vehicle
Moving vehicle
※Covered by IEEE 802.15.6-2012
※not covered yet
※mandatory
※mandatory
※Around meaning;
Desk, WiFi AP in the room etc.
Channel model
With environment
※
※
※
※
※
※mandatory

## Slide 5: Channel and Environmental Models
Path loss
Reflection
Multipath
Fading
LOS / NLOS model
White Gaussian noise
Interference from co-existing wireless systems e.g. Bluetooth, IEEE 802.11, IEEE 802.15.4 etc.
Interference from the other BANs.
Interference from the other electric systems, devices and components (Electro-magnetic interference; EMI from electric motors, spark plugs in vehicles, etc.
Electro-magnetic compatibility; EMC. Possibility to affect to the other systems and human body.
VBAN  HBAN interference
VBAN and HBAN  Vehicle control and human body impacts.
Colored noise (Impulse noise, spike noise, ignition noise etc.)
Time-varying channel and interference modeling (Statistic, non-static, pseudo static model)
※optional
or
?
Environment model
Channel model
Channel model
EMI EMC
Colored noise
Other wireless systems
Environment model
Time-varying modeling
※mandatory
※mandatory
※mandatory
※mandatory
※optional
※optional
※optional
※IEEE802.15.6-2012
※will be defined in this amendment
※mandatory
or
?
※mandatory
※Comment on 1st session

## Slide 6: Various Interference in Coexistence
＊ IEEE 802.11a (wi-fi) （5GHz） overlaps
Other UWB-BAN
user ？
User “B”
User “A”.
A wants to connect to “B”.
UWB-WBAN
IEEE 802.15.6
Other UWB system.
e.g. IEEE 802.15.4-2020 IEEE 802.15.4z
user ？
user ？
interference
interference
Inter-user interference
“IUI”
“ISI”
Interference from a system using the same standard.
Inter-system interference
Known signal. Pre-knowledge can be used to mitigation
Interference from a system using overlapped frequency
Unknown signal.
EMI / EMC issues
Other BAN
Inter-BAN interference
“IBI?”
Other NB-BAN
VBAN  HBAN interference

## Slide 7: Automotive Systems and EMC
The inclusion of new technologies in automotive systems has resulted in
new challenges across the radio spectrum

## Slide 8
Today’s electronic and electric systems in vehicles contain many more active
components than in the past.
Those components and assemblies may emit electromagnetic (EM) noise, or be exposed to external sources of energy/EM noise, resulting in unanticipated changes in systems operation (vehicle’s control, on-board radio equipment)
Wireless/radio equipment: cellular communications, Wi-Fi, Bluetooth, NFC,
automotive radar, sensors, infotainment, GPS, etc.
Assemblies include high speed digital circuits that may be radiating EM noise.

## Slide 9: Environment Model in Vehicle
5
1
2
3
4
6
Engine/motor diagnostic sensor and controller
Air pressure sensor, wheel health sensor and controller
Transmission monitoring sensor and controller
Cabin environment sensor (temperature, brightness, humidity etc.)
Sheet sensor, health care sensors for driver
Sheet sensor, health care sensors for passenger
Engine/Motor room environment model
Cabin room environment model
https://media.istockphoto.com/photos/transparent-car-design-wire-model3d-illustration-my-own-car-design-picture-id594040008?k=6&m=594040008&s=612x612&w=0&h=XE8LiBjpM51aB4pH2CFt6-MT6IvALRPnlxPcac0RXhg=
Note:
Various type of car/vehicles
Bus, Bulldozer, Heavy construction equipment needed each different sensors.

## Slide 10: Engine/Motor Room Environment
Many metallic components
Components existing in densely
Ignition noise, motor noise
Larger path-loss than free propagation
A lot of reflection of RF signal
Electro-magnetic interference, EMI issues
Ignition coil
Electric motor
High current battery and cable
Spark plug
Electric generator
https://www.as-web.jp/car/575374/attachment/03a_sub_dsc01273
Especially EV

## Slide 11: Electromagnetic Environment
Lane departure system
Night vision
Front object CCD camera
Front airbag sensors
Nighttime pedestrian warning
Drowsiness sensos
Front object laser radar
Active park assist
Tire pressure sensor
Rear object monitor CCD camera
Rear camera
Blind spot detection
Cross traffic alert
Central computer
Rear object laser radar
Wheel speed sensor
Tire pressure sensor
Side airbag SRS
Adaptive cruise control
Steering angle sensor
Automatic brake actuator
Wheel speed sensor
Nighttime pedestrian warning IR sensor
Sensors, monitors and vehicle controlling systems in modern vehicle

## Slide 12: Electric and hybrid vehicle environment
Wheel motor
High current cables
High capacity Li-ion batteries
Motor controller / inverter
Battery charge and discharge controller
Electric generator
etc….
Motor controller / inverter
Brake controller
Central computer
Battery charge and discharge controller
Sensors, cameras, etc….
Power electronics systems and its circuits radiate EM wave which causes colored noise EMI. VBAN and HBAN should be protected from such EMI.
Vehicle control systems and sensors are electronically sensitive system in general.
Those systems should be protected from EMI from HBAN and VBAN and guaranteed EMC.

## Slide 13: EMC model
Source
Sources of EM near and far field: may be off board and on board sources
Path: radiated or conducted
Sink: intended receiver or unintended receiver
Path
Sink
Radar application
Radar application
Engine control application
Body control applicaition
Head unit
Camera application
Camera application
Dashboard application
Multimedia application
rear seat entertainment
Camera application
Camera application

## Slide 14
Vehicle Original Equipment Manufacturer (OEM) practice is to address
EMC/EMI at the component and system design phase. Moreover, the
resolution of EMC/EMI issues must take in high volume and complex
manufacturing process with the Goal to balance EMC/EMI requirements
with market-based vehicle usage, as in our case HBAN and VBAN.
15.6a does not intend to address all these items and issues.
We would like to use the knowledge base on these issues:
EMI is been categorized into four areas: conducted & radiated
emissions, and conducted & radiated susceptibility; with
their specific compliance standards and limits

## Slide 15
OEMs design EMC-proof circuits and components for immunity, with the ultimate goal to achieve certification of the vehicle to relevant standards, including EMC/EMI.
So far we have been relaying on international standards for EMC/EMI environments for on-board and off-board sources in internal combustion vehicles, electric vehicle and hybrid-electric vehicles.
CISPR 25 v4 , SAE J551/1, ECE R10 r5, Nissan NDS02
We may add support from Japanese automotive industry and/or others
for testing EMC/EMI over UWB systems in-vehicles based on CISPR 25,
SAE J551/1 or relevant Standards.

## Slide 16: Cabin Room Environment
A lot of metallic components
Human being moves in the cabin room
Ignition noise, motor noise
Larger path-loss than free propagation
Human body absolve RF energy. Dynamic path loss issue and safety issue for passengers should be considered.
Even smaller effect than engine room environment, electro-magnetic interference should be considered.
Note:
Noise and interference through the glass windows cannot be ignored.
Interference from BT/WiFi/ cellular / ETC (Electric toll correction system), car navigation system.

## Slide 17: On Vehicle Environment
Around roof
・mostly free propagation can be applicable except reflection on the metallic roof
Side
mostly free propagation can be applicable
Between right hand side and the left, front and back, NLOS model should be applied. (Glass window)
Bottom
Reflection at the body bottom and the ground should be considered. => maybe ignorable. => Depends on pavement
https://illust8.com/contents/2559
Note:
・open car
・in-door roof<=in body
Note:
・key-less entry system

## Slide 18: Environment models that can be applicable against different type of vehicles
Engine
Cabin
Engine
Cabin
Policy:
IEEE 802.15.6a defines several common environment models against most dominant use cases as mandatory models.
Categories:
Categorize several type of vehicle like “for passengers”, “bus”, “small cargo”, “middle cargo”, “Large cargo” and “special purpose vehicles” such as a construction machines and build models for various categories.
Different
Size;
Structure;...etc.
https://nohat.cc/f/heavy-truck-illustration-isolated-on-a-white-background/comvecteezy328938-201908251309.html

## Slide 19: Channel and Environment Model Categories
https://illust8.com/contents/5097
Small / medium size vehicle
Large / long size vehicle
Special purpose vehicle
With engine
Electric vehicle
On-vehicle body
Around vehicle body
In-vehicle body
channel / Environment
channel / Environment
channel / Environment
channel / Environment
channel / Environment
channel / Environment
channel / Environment
channel / Environment
channel / Environment
channel / Environment
CM-V1 / EM-V1
https://frame-illust.com/?p=8372
Most dominant case
Mandatory / optional
channel / Environment
CM-V2 / EM-V2
channel / Environment
CM-V3 / EM-V3
or

## Slide 20: In-Vehicle Body Model Categories
https://illust8.com/contents/5097
Small / medium size vehicle
Large / long size vehicle
Special purpose vehicle
With engine
Electric vehicle
Through engine room and cabin
Engine room
Cabin
Mandatory / optional
Channel / Environment
CM-V1 / EM-V1
channel / Environment
channel / Environment
channel / Environment
channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Most dominant case

## Slide 21: On-Vehicle Body Model Categories
https://illust8.com/contents/5097
Small / medium size vehicle
Special purpose vehicle
With engine
Electric vehicle
Channel / Environment
CM-V2 / EM-V2
channel / Environment
channel / Environment
channel / Environment
channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Roof
Side Right/Left/
Front/Back
Bottom
Most dominant case
Mandatory / optional
Large / long size vehicle
or

## Slide 22: Around Vehicle Body Model Categories
https://illust8.com/contents/5097
Small / medium size vehicle
Special purpose vehicle
With engine
Electric vehicle
channel / Environment
CM-V3 / EM-V3
channel / Environment
channel / Environment
channel / Environment
Static vehicle
Moving vehicle
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Most dominant case
Mandatory / optional
Large / long size vehicle
or

## Slide 23: Inter Vehicle (Vehicle to Vehicle) Model Categories
https://illust8.com/contents/5097
Small / medium size vehicle
Special purpose vehicle
With engine
Electric vehicle
Channel / Environment
channel / Environment
channel / Environment
channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
Most dominant case
Mandatory / optional
Large / long size vehicle
or
With engine
EV
Channel / Environment
Channel / Environment
Channel / Environment
Channel / Environment
CM-V4 / EM-V4
channel / Environment

## Slide 24: Summary
Environment model which has wider meaning than channel model has been proposed.
Environment model including not only channel characteristics but also including interference, colored noise, EMC and human impact issues.
Environment models has been categorized against several typical vehicle categories.
Most dominant environment models in individual categories were assigned as "Mandatory".