## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Some UAS Use Cases for UWB]
Date Submitted: [12 May, 2021]
Source: [Stuart W. Card] Company [multiple affiliations, this submission made individually]
Address [7417 S. Main Street, P.O. Box 61, Newport NY 13416 USA]
Voice:[+1 315-845-6249], FAX: [+1 315-845-6255], E-Mail:[stu.card@critical.com]
Re: [revision of 15-21-0170-00-nuwb response to Call for Contributions - IG UWB-NG, 5 March 2021]
Abstract: [A brief introduction to some Unmanned Aircraft System (UAS) use cases for UWB]
Purpose: [Consider UAS use cases in scoping NG-UWB and/or NS-UWB.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Some Unmanned Aircraft System (UAS) Use Cases for UWB
A hasty introduction to an incomplete list of maybes, now w/some guesses at requirements

## Slide 3: Potential UWB applications to UAS (“drones”)
Indoor & Outdoor (latter more challenging):
Remote Identification & tracking (UAS RID)
Self-Separation & Collision Avoidance
Positioning, Navigation & Landing
  Adjunct to GNSS for greater precision
  Alternative when/where GNSS unavailable
Command & Control (C2)
Telemetry

## Slide 4: Remote Identification & tracking (UAS RID)
Mandated by Civil Aviation Authorities’ performance based rules
  European Union Aviation Safety Agency (EASA), “Commission Delegated Regulation (EU) 2020/1058...” https://eur-lex.europa.eu/legal-content/EN/TXT/?uri=CELEX%3A32020R1058
  Federal Aviation Administration, “Remote Identification of Unmanned Aircraft” https://www.federalregister.gov/documents/2021/01/15/2020-28948/remote-identification-of-unmanned-aircraft
Industry consensus technical standards
  Primarily ASTM International F3411-19 “Standard Specification for Remote ID and Tracking” http://www.astm.org/cgi-bin/resolver.cgi?F3411
Currently Bluetooth & WiFi Aware/NAN (need >273m range)
  Preferably 628 meters, see next use case for why
All data inc. position self-reported (~150 payload bytes/sec./UA)
Authentication optional & largely TBD
  IETF Drone Remote Identification Protocol (DRIP) https://datatracker.ietf.org/wg/drip
  Ranging between UA & observer device could help

## Slide 5: Self-Separation & Collision Avoidance
Expected to be mandated by CAAs, also operator self-interest
  Self-Separation is coordinating to stay “well clear”, avoiding risk of collision: Sense And Avoid (SAA) now Detect And Avoid (DAA), w/ & w/o ground help
    UWB almost certainly can’t achieve necessary range to coordinate staying well clear
  When Self-Separation fails, Collision Avoidance initiates urgent maneuver
    if well clear is violated, not only CA but also RID would be very useful (see previous use case)
  RID or coordinated CA at edge of well clear implies a slant range of 628m
  May include UAS avoiding collisions w/structures, trees, etc.
Industry consensus technical standards
  RTCA, EUROCAE, et al
Manned mature (e.g., TCAS), UAS emerging (e.g., ACAS Xu)
Currently narrowband aviation spectrum
  Ranging between UA & other aircraft could help
  Precise positioning could help avoid known fixed obstacles

## Slide 6: Positioning, Navigation & Landing
Intrinsic to flight operations
No standards for small UAS at low altitudes – vendor innovation
Urban Air Mobility (UAM) / Advanced Air Mobility (AAM) will transport humans (still no pilot onboard) in densely occupied airspace volumes over other humans, so regulations likely
Currently based on [GIS terrain & structure data plus]
  GNSS (dominates)
  Radar (only on larger UA), lidar, optical machine vision
  Laser or acoustic height finders
  Magnetic compass (rare)
Dedicated spaces emerging (flying club parks, nets, indoors)
UAM expected to be based largely on many small “vertiports”
Small UAS hangar sorties suggest a required range of ~100m
  Precise positioning obviously could help greatly, especially with [automatic] landing (I have watched landings w/height errors of less than a meter wreck small multicopters)

## Slide 7: Command & Control (C2) and Telemetry
C2 intrinsic to flight operations, telemetry also very common
Some de facto protocol standards (e.g., MAVLink)
Currently uses mostly ISM & NII bands
  incl. 433 MHz which is Amateur in US but much used illegally for long range
  typically C2 on 915 or 2400 MHz & video streaming on 5 GHz
  ranging (w/minimal data) to max usable 5 GHz 802.11 HD stream range?
UA “fly-away”, often causing loss of or damage to aircraft, potentially causing harm to others, usually due to losing C2 link
  Ranging between UA and Ground Control Station (GCS) could help avoid exceeding C2 link & regulatory operating range limits
  Ranging also provides context for telemetry
  Interoperation with IEEE 1588 Precision Time Protocol (PTPv2) would add value to telemetry, C2 & other apps by synchronizing link layer clocks with network provided global consensus time

## Slide 8: Indoor/Outdoor issues
 restrictions on use of UWB aboard aircraft
  Regulatory relief likely for UAS, especially if not carrying human passengers
 restrictions on use of UWB outdoors
  Regulatory relief likely depends on demonstrating non-interference
What is “indoors” (to agencies such as the FAA & FCC)?
  In a 90 dB Faraday cage?
  In a typical metal roofed & sided aircraft hangar?
  In a typical wood frame structure with many windows?
  Under a pavilion? Inside a net? At a dedicated UAS flying park?
Operations may involve takeoff inside a GNSS-starved hangar, exit, GNSS-enabled outdoor flight, hangar re-entry & landing.
Oneida County, at Griffiss International Airport (formerly AFB), as an extension of the New York UAS Test Site, is constructing a SkyDome facility for experimentation & testing w/all the above.
  Despite hurdles, let’s scope UWB-NG for at least some of these.

## Slide 9: Initial Answers to some of Ben’s Questions
Range: depending on use case, 100 – 628 meter 3D slant range
#: in that range of center of “hockey puck” (w/ground below & no emitting UA above) < (30 UA + 30 Ground Control Stations)
Data volume requirements: negligible
  Maximum Transmission Unit (MTU) >225 B would avoid fragmentation
  1 – 10 frames/second assuming no fragmentation
  Multiplying these, under 20 kbps/node, under 660 kbps total in footprint
Latency: E2E mean <200 mS, prefer <100 mS (jitter irrelevant)
Reliability: high frame loss rates are tolerable if no fragmentation
Dynamics: depending on use case,1-10 position updates / sec.
Energy: power is no problem iff running from propulsion battery; but energy is flight time thus range; recharge between flights
Topology: flat peer to peer LAN, sometimes w/Internet gateway
Timing/synch: error vs GNSS time < position update interval
Colocated radios: GNSS, Bluetooth, 802.11, 915 MHz, 433 MHz