## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Receiver Requirements for Realistic Interference Scenarios
Date Submitted: May 11, 2021
Source: T. McKay (GLOBALFOUNDRIES)
Contact:
Voice: +1 408 395 7207, E-Mail: tgmckay@ieee.org
Re: Study Group 4ab: UWB Next Generation
Abstract: Consideration of receiver requirements for Realistic Interference Scenarios
Purpose: Assist in developing technical content
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2: Receiver Requirements for Realistic Interference Scenarios
T. McKay
tgmckay@ieee.org
IEEE Sr. Member, 2014
Notes: Jul 12, 2010
Page 2

## Slide 3: Motivation
WiFi 6E FCC TX Power Ruling
  Threatens Use of UWB Channel 5 Completely
  May Impact Cost of Channel 9-only implementations due to roofing filter requirements
Ultra-Wideband receiver 2nd order distortion may cause link loss due to modulated interferers
Quality receiver designs can achieve high second order intercept through mixer calibration
  D. Kaczman et al., “A single-chip 10-band WCDMA/HSDPA 4-band GSM/EDGE SAW-less CMOS receiver with DigRF 3G interface and +90 dBm IIP2,” IEEE J. Solid-State Circuits, vol. 44, no. 3, pp. 718–739, Mar. 2009.
  Added power consumption likely can be made negligible
Notes: Jul 12, 2010
Page 3

## Slide 4: Background
Direct Conversion Receivers are Simple, Low Cost, Fully Integrable in CMOS
Second-order distortion (IP2) of Direct Conversion Receiver Maps
  CW Blocker to DC at IF
    Relatively easy to mitigate this effect
    Existing vendors have established de facto standard
  AM Modulated Blocker to “Noise” in IF
    May not be so easy to mitigate
  For basic lineup calculations, see, for example
https://www.analog.com/en/technical-articles/understanding-ip2-and-ip3-issues-in-direct-conversion-receivers.html
Notes: Jul 12, 2010
Page 4

## Slide 5: Proposal
Follow 802.11 by specifying
  sensitivity
    Is anything specified in 802.15.4 now?
  blocking - CW is def acto
  blocking - Modulated
Work plan to identify practical scenarios of value and identify a minimum requirement
  Blocker Power vs. Distance from WiFi 6E APs
  Other important scenarios
  Anticipate that elaborate mitigation schemes would drive power consumption up
  Focus on requiring quality (not costly) RF/Analog hardware to protect the standard
Notes: Jul 12, 2010
Page 5

## Slide 6: Thank You
Notes: Jul 12, 2010
Page 6