## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: CID 32 Proposal
Date Submitted: 14 May, 2021
Source: Chris Hett, Landis+Gyr; Alpharetta, GA USA
Voice: +1-678-258-1398, E-Mail: chris.hett@landisgyr.com
Re: LB183 Comment Resolution
Abstract: Proposed resolution for CID 32
Purpose: Resolve comment ID 32 from LB183
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: CID 32 Proposed Resolution
19.6.8 Receiver interference rejection
Change the first paragraph as indicated:
For all operating modes other than mode #5,#6,#7 and #8 in the 920 MHz band, the adjacent designated channels are those on either side of the desired designated channel that are closest in frequency to the desired designated channel. The alternate designated channel is more than one removed from the desired designated channel in the operational frequency band. For operating modes #5,#6,#7 and #8 in the 920 MHz band specified in Table 19-8, and Table 19-9a, the adjacent channel rejection is measured on those channels on either side of the desired designated channel that is N*200 kHz away in frequency to the designated channel center frequency, and the alternate designated channels are those on either side of the desired designated channel that are 2*N*200 kHz away in frequency to the designated channel center frequency.

## Slide 3: CID 32 Proposed Resolution
19.6.8 Receiver interference rejection
Insert the following paragraphs at the end of 19.6.8:
Operating modes #5,#6,#7 and #8 in the 920 MHz band allow for overlapping channels, thus co-channel rejection is also specified for these operating modes.
For co-channel rejection the desired signal and co-channel interferer shall be a compliant SUN FSK PHY signal, as defined in 19.3, of pseudo-random data at the center frequency of the desired channel.
-- The co-channel rejection ratio shall be at least -12 dB