## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Input to tech requirements for the NG UWB project]
Date Submitted: [17th May 2021]
Source: [Billy Verso, Michael Mc Laughlin, Jarek Niewczas, Carl Murray, Igor Dotlic, Ciaran McElroy] Affiliation [Qorvo]
Address [ ]
E-Mail:[billy.verso (at) qorvo.com]
Re: [Proposed enhancements to 802.15.4 UWB]
Abstract: [Input to the technical requirements discussion for the 4ab project]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction:
This submission is intended to encourage discussion and agreement on the technical requirements for the new and enhanced features to be added by the 4ab project.
  This submission is HRP UWB PHY focused.
The features discussed herein are selected based on enhancements identified in various peoples’ previous submissions to 802.15 in the 4z, WNG, NG-UWB and 4ab groups.
  This incudes: data rates, channels, sensing, and, narrowband signalling.
In each case we make some recommendations for the technical framework.

## Slide 3: Item: New HRP UWB PHY Data Rates
Higher data rates have been proposed to reduce packet sizes and support higher density and larger volume data applications.
Some lower / intermediate data rates at the higher PRF may also be attractive to increase data communication operating range and allow more steps to trade off throughput performance against error rate.
Our recommendations for the technical framework are that:
  The enhanced PHY continues to use IR-UWB techniques based on 802.15.4z and continues to require inclusion of the 4z modulations to support interworking.
  All new data rate modulation and coding proposals are examined in terms of operating range, power consumption, complexity and latency.
  Interference is evaluated for co-located data users and two-way ranging users.

## Slide 4: Item: New HRP UWB PHY Channels
It has been suggested to define additional channel frequency band options to allow for future regulations and for interference mitigation.
Our recommendations for the technical framework are that:
  The enhanced PHY continues to utilise and support existing 802.15.4 HRP PHY channels.
  Any new HRP PHY channel proposals are based on the 802.15.4 HRP PHY clock frequency and its 499.2 MHz channel bandwidth.
  Any new channel frequencies are non-mandatory.

## Slide 5: Item: Sensing and Presence Detection
It has been suggested to add sensing capabilities to support presence detection and environment mapping.
  While monostatic radar may not need standardization, we should specify the sequences for multistatic radar to facilitate interworking and multivendor support.
Our recommendations for the technical framework are that:
  The sensing and presence detection radar functionality, whether multistatic or monostatic, should be designed and specified to guard against it causing significant disruption or interference to either co-located two-way ranging users or data networking users.

## Slide 6: Item: Narrowband Radio
It has been suggested that a narrowband radio be specified to work alongside UWB. (Not a new idea).
  802.15.4f added an MSK PHY for controlling the TX only tags.
  FiRa and CCC use BLE to negotiate and initiate UWB ranging.
    BLE has a well-defined, ready specified protocol.
    Do we want another narrowband radio? Will TG4ab specify its use completely or will we leave it to another organization to develop and specify a new upper layer protocol using it?
Our recommendations for the technical framework are that:
  Any proposed narrowband radio should not be a source of interference to UWB
    It should be placed outside the UWB channel bands of interest.
    It should have strict out-of-band limits to not bleed into and disrupt adjacent UWB channels.
    It should have low duty-cycle.

## Slide 7: Conclusion:
This submission presented our thoughts on some of the features proposed for the next generation UWB enhancement project and made related recommendations for the technical framework.
We hope this will stimulate discussions and lead to agreement on the key parameters to consider in proposals to TG4ab.
Thank you.

## Slide 8
THE END