## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Report of the results regarding a liaison statement to ITU-R WP 5A
Date Submitted: 18 May 2021
Source: Hiroyo Ogawa, Iwao Hosako, Akifumi Kasamatsu, Norihiko Sekine, Shingo Saito, Keizo Inagaki, Atsushi Kanno, Katsumi Fujii, Hirokazu Sawada
Company: NICT
Address 4-2-1, Nukuikita, Koganei, 184-8795, Tokyo, Japan
Voice:+ 81 42 327 5043, FAX: , E-Mail: hiroyoogawa@nict.go.jp
Re: n/a
Abstract: The channel arrangement provided from IEEE 802 SC THZ was added in the working document of M.[252-296 GHZ.LMS.FS.COEXIST] and was also added in the working document of a revision of M.2417-0. Additional information on the results of WP 5A May meeting is also provided.
Purpose: To report the results of ITU-R WP 5A regarding a liaison statement from IEEE802.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
LS to WP 5A

## Slide 3
New Annex 3 was added to include channel arrangement in the frequency 252-296 GHz provided by IEEE802.15.SC.THZ.
The channel bandwidth of 51.8 GHz was deleted from the table of LMS characteristics in the frequency range 252-296 GHz.
This working document includes co-channel and adjacent channel analyses between LMS and FS applications and co-channel operation may interfere with receivers.
Question to SC.THZ: Can IEEE802.15.3d device operate in the condition of the following channel arrangement to
Update of working document of M.[252-296 GHZ.LMS.FS.COEXIST]
Coexistence between land-mobile and fixed service applications operating in the frequency range 252-296 GHz
avoid co-channel operation between LMS and FS applications?

## Slide 4
The right figure was successfully replaced with the channel arrangement provided by IEEE 802.15.SC.THZ in Annex 1 of the working document.
A change of the frequency range from 275-450 GHz to 252-450 GHz in the title of M.2417-0 was proposed by one administration due to information from IEEE802.15.SC.THZ, but no consensus was reached at May 2021 meeting.
This issue will be discussed at November meeting and if the change of the minimum frequency of the title would be agreed, its scope and other parts of Report M.2417-0 should be further reviewed.
Revision of working document of M.2417-0
Technical and operational characteristics of land-mobile service applications in the frequency range 275-450 GHz

## Slide 5
WP 5A sent a liaison statement to WP 5C asking three questions:
  Can the technical and operational characteristics provided in Report ITU-R F.2416-0 be used for coexistence studies between LMS and FS applications operating in the frequency range 252 296 GHz?
  Can the I/N value of −10 dB in Recommendation ITU-R F.758-7 be
This work was financially supported by the Ministry of Internal Affairs and Communications of Japan.
Additional information to IEEE802.SC.THZ
used for coexistence studies.
Can FS aggregate interfering scenarios based on the deployment scenarios provided by Report ITU-R F.2416-0, as shown in the right side, be used for coexistence study?
I suppose that WP 5C may send a liaison to IEEE802 in November 2021 meeting to confirm whether the current characteristics in the frequency range 275-325 GHz is valid in the frequency range 252-296 GHz or not.
FS link density=8.4/km2