## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Preamble codes for Data Communications in 802.15.4ab
Source: Carlos Aldana (Facebook), Qiyue Zou (Facebook)
Address : [1 Hacker Way, Menlo Park, CA 94025]
E-Mail: [caldana (at) fb.com]
Re: Study Group 4ab: UWB Next Generation
Abstract: [preamble code enhancements to 802.15.4z for data communications]
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2: Technical Guidance [1]
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases. | Preambles shown to have good cross correlation properties with legacy devices.
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs). | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging; s | 
Reduce complexity and power consumption; | 
Hybrid operation with narrowband signaling to assist UWB; | 
Enhanced native discovery and connection setup mechanisms; | 
Sensing capabilities to support presence detection and environment mapping; | New preamble codes could be used for this application
Low-power low-latency streaming | New preamble codes could be used for this use case.
higher data-rate streaming allowing at least 50 Mbit/s of throughput. | New preamble codes are proposed
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols; | 
Infrastructure synchronization mechanisms. | 

## Slide 3: Preamble codes for Data Communications in 802.15.4ab

## Slide 4: Objective
Propose preamble codes (SYNC field) candidates for data communications over IEEE 802.15.4a “UWB” channels [2]

## Slide 5: Background
4 configurations defined 802.15.4z[3]
This contribution focuses on the SYNC field

## Slide 6: Key Considerations
Excellent periodic autocorrelation properties -> improved ranging and channel estimation
Good cross-correlation properties with HRP and LRP preambles -> coexist with legacy UWB devices
Good periodic cross-correlation properties -> coexist with other data communication UWB devices
Reduced SYNC field length -> reduced air time and improved PHY efficiency

## Slide 7: Periodic Autocorrelation
Good periodic autocorrelation makes channel estimation easy (via matched filter)
  Ternary preamble sequences (S1-S32) [4] specified in the UWB standards have “perfect” periodic autocorrelation function (i.e., out-of-phase autocorrelation = 0)
  Matched filter output is equal to the channel impulse response plus noise (assuming symbol length Tsym ≥ channel duration)
  IEEE 802.15.4a CM1 – CM9 channel models defined in [2] have PDP channel duration in the range 80ns – 850ns. All channel models except CM6 and CM8 have PDP duration < 400ns
Preamble Code | Preamble Code Length | Length of Delta Spreading Function | #Chips Per Symbol | Tsym
S1-S8 | 31 | 16 | 496 | 0.994us
S1-S8 | 31 | 64 | 1984 | 3.974us
S9 – S24 | 127 | 4 | 508 | 1.018us
S25 – S32 | 91 | 4 | 364 | 0.729us

## Slide 8: UWB Channel Model (CM1)
CM1 channel model: residential, LOS
PDP channel length = 113ns (-40dB)
mean RMS delay = 16.9ns

## Slide 9: UWB Channel Model (CM2)
CM2 channel model: residential, NLOS
PDP channel length = 211ns (-40dB)
mean RMS delay = 19.3ns

## Slide 10: UWB Channel Model (CM3)
CM3 channel model: indoor office, LOS
PDP channel length = 95ns (-40dB)
mean RMS delay = 10.1ns

## Slide 11: UWB Channel Model (CM4)
CM4 channel model: indoor office, NLOS
PDP channel length = 117ns (-40dB)
mean RMS delay = 13.2ns

## Slide 12: UWB Channel Model (CM5)
CM5 channel model: outdoor, LOS
PDP channel length = 199ns (-40dB)
mean RMS delay = 28.7ns

## Slide 13: UWB Channel Model (CM6)
CM6 channel model: outdoor, NLOS
PDP channel length = 806ns (-40dB)
mean RMS delay = 79.3ns

## Slide 14: UWB Channel Model (CM7)
CM7 channel model: industrial, LOS
PDP channel length = 79ns
mean RMS delay = 8.7ns

## Slide 15: UWB Channel Model (CM8)
CM8 channel model: industrial, NLOS
PDP channel length = 841ns (-40dB)
mean RMS delay = 89.2ns

## Slide 16: UWB Channel Model (CM9)
CM9 channel model: farm
PDP channel length = 403ns (-40dB)
mean RMS delay = 21.4ns

## Slide 17: Periodic Autocorrelation
m-sequences have quasi-optimal periodic autocorrelation
  quasi-optimal -> Out-of-phase autocorrelation = -1 while autocorrelation peak = N
  Although not “perfect”, N can be chosen such that N/1 is large and does not degrade system performance significantly, e.g., 20*log10(N/1) ≥ 20dB
m-sequences are bipolar, where only “+1” and “-1” are transmitted
Number of 1s = Number of 0s + 1
  More pulses are transmitted compared to equal length ternary sequences
  For example,
  S1 – S8 (length = 31) - each sequence has 15 0’s
  S9 – S24 (length = 127) - each sequence has 63 0’s
  S25 – S32 (length = 91) - each sequence has 10 0’s

## Slide 18: S9 Length 127 sequence vs Length 63 m-sequence
ternary preamble sequence S9
m-sequence of length 63
Ternary preamble sequence S9n
M- sequence of length 63

## Slide 19: Implementation
m-sequences are generated using linear-feedback shift registers (LFSR), and have low implementation cost and complexity
An n-bit LFSR generates a m-sequence of length 2n-1
LFSR is determined by the feedback polynomial
A 10-bit LFSR with feedback polynomial 0x291(Hex) = 10’b 10 1001 0001
0x291 = 1 0 1 0 0 1 0 0 0 1

## Slide 20: Periodic Cross-Correlation
Periodic cross-correlation between different proposed sequences should be small in order to limit the interference within a piconet
Goal is to maximize Sidelobe Suppression Ratio (SSR)
= 20log10(

## Slide 21: Periodic Cross-Correlation of S25 (Length 91)
Maximum Sidelobe Suppression Ratio = 20log10(81/15) = 14.65dB
Minimum Sidelobe Suppression Ratio = 20log10(81/27) = 9.54dB
Average Sidelobe Suppression Ratio = 20*log10(81/21.43) = 11.55dB
Consistent with Table in [5]

## Slide 22: Periodic Cross-Correlation of m-sequences of length 63
Maximum Sidelobe Suppression Ratio = 20log10(63/15) = 12.47dB
Minimum Sidelobe Suppression Ratio = 20log10(63/23) = 8.75dB
Average Sidelobe Suppression Ratio = 20*log10(63/19) = 10.41dB

## Slide 23: Cross-Correlation with HRP and LRP Preambles
Cross-correlation between proposed sequences and legacy HRP and LRP preambles needs to be small
Binary m-sequences have length 2m -1, e.g.,15, 31, 63, 127, 255, …
m-sequences of length 31 and 127 have relatively large cross-correlation with length-31 and length-127 legacy preamble sequences (i.e., S1-S8, S9-S24)
m-sequences are robust to LRP preambles (see subsequent slides)
m-sequences of length 15 does not provide enough rejection.
Therefore, m-sequences of length 63, 255, 511, 1023, … are considered

## Slide 24: Shorter Sync Length for Existing Codes
sync_length = Tsym × Nsync = Tc × K × L × Nsync
K (preamble code length) | L (length of delta spreading function) | #Chips Per Symbol | Tsym | Sync Length (Nsync = 16 Symbols) | Sync Length (Nsync = 64 Symbols)
31 | 16 | 496 | 0.994us | 15.897us | 63.590us
31 | 64 | 1984 | 3.974us | 63.590us | 254.359us
127 | 4 | 508 | 1.018us | 16.282us | 65.128us
91 | 4 | 364 | 0.729us | 11.667us | 46.667us

## Slide 25: Sync Length for Short Preamble
Short preamble length less than 16.5us reduces PPDU duration (K<=511)
  Smaller Nsync for LOS short-distance channels
    Nsync ≥ 16 for HRP UWB preambles
    Nsync = 4 or 8 can work for short-distance LOS channels
  To reduce sync length, smaller L for long sequences
    For long sequences, e.g., m-sequences of length 1023, 2047 (with L=1)
K (preamble code length) | L (length of delta spreading function) | #Chips Per Symbol | Tsym | Sync Length (Nsync = 4 Symbols) | Sync Length (Nsync = 8 Symbols) | Sync Length (Nsync = 16 Symbols)
63 | 8 | 504 | 1.010us | 4.038us | 8.077us | 16.154us
255 | 2 | 510 | 1.022us | 4.087us | 8.173us | 16.346us
511 | 1 | 511 | 1.024us | 4.095us | 8.189us | 16.378us
1023 | 1 | 1023 | 2.049us | 8.197us | 16.394us | 32.789us
2047 | 1 | 2047 | 4.101us | 16.402us | 32.805us | 65.609us

## Slide 26: Spectrum Characteristics of Existing UWB Preambles
Preamble Code | K (preamble code length) | L (length of delta spreading function | #Chips Per Symbol | Tsym | SPAR (frequency domain)
S1 – S8 | 31 | 16 | 496 | 0.994us | 0.4dB
S1 – S8 | 31 | 64 | 1984 | 3.974us | 0.4dB
S9 – S24 | 127 | 4 | 508 | 1.018us | 0.5dB
S25 – S32 | 91 | 4 | 364 | 0.729us | 0.9dB

## Slide 27: Spectrum Characteristics of m-sequences
K (preamble code length) | L (length of delta spreading function) | #Chips Per Symbol | Tsym | Sync Length (Nsync = 4 Symbols) | Sync Length (Nsync = 8 Symbols) | Sync Length (Nsync = 16 Symbols ) | SPAR (frequency domain) | Delta Peak EIRP over peak EIRP of preamble code 9 with L = 4 (dB) | Delta SPAR over SPAR of preamble code 9 with L = 4 (dB)
63 | 8 | 504 | 1.010us | 4.038us | 8.077us | 16.154us | 0.5dB | -3.5dB | 0dB
255 | 2 | 510 | 1.022us | 4.087us | 8.173us | 16.346us | 0.5dB | 0dB | 0dB
511 | 1 | 511 | 1.024us | 4.095us | 8.189us | 16.378us | 0.5dB | +2.6dB | 0dB
1023 | 1 | 1023 | 2.049us | 8.197us | 16.394us | 32.789us | 0.4dB | +2.9dB | -0.1dB
2047 | 1 | 2047 | 4.101us | 16.402us | 32.805us | 65.609us | 0.4dB | +3.0dB | -0.1dB

## Slide 28: M-Sequences of Length 63
Code Index | Feedback Polynomial | Code Sequence
M63_1 | 21 | -1,-1,-1,-1,-1,1,1,1,1,1,1,-1,1,-1,1,-1,1,1,-1,-1,1,1,-1,1,1,1,-1,1,1,-1,1,-1,-1,1,-1,-1,1,1,1,-1,-1,-1,1,-1,1,1,1,1,-1,-1,1,-1,1,-1,-1,-1,1,1,-1,-1,-1,-1,1
M63_2 | 30 | -1,-1,-1,-1,-1,1,-1,-1,-1,-1,1,1,-1,-1,-1,1,-1,1,-1,-1,1,1,1,1,-1,1,-1,-1,-1,1,1,1,-1,-1,1,-1,-1,1,-1,1,1,-1,1,1,1,-1,1,1,-1,-1,1,1,-1,1,-1,1,-1,1,1,1,1,1,1
M63_3 | 2D | -1,-1,-1,-1,-1,1,1,1,-1,-1,-1,-1,1,-1,-1,1,-1,-1,-1,1,1,-1,1,1,-1,-1,1,-1,1,1,-1,1,-1,1,1,1,-1,1,1,1,1,-1,-1,1,1,-1,-1,-1,1,-1,1,-1,1,-1,-1,1,1,1,1,1,1,-1,1
M63_4 | 36 | -1,-1,-1,-1,-1,1,-1,1,1,1,1,1,1,-1,-1,1,-1,1,-1,1,-1,-1,-1,1,1,-1,-1,1,1,1,1,-1,1,1,1,-1,1,-1,1,1,-1,1,-1,-1,1,1,-1,1,1,-1,-1,-1,1,-1,-1,1,-1,-1,-1,-1,1,1,1
Sidelobe Suppression Ratio (dB)
= 20log10(autocorrelation peak / cross-correlation peak)
Cross-correlation Sidelobe Peak Value

## Slide 29: M-Sequences of Length 255
Code Index | M255_1 | M255_2 | M255_3 | M255_4 | M255_5 | M255_6 | M255_7 | M255_8
Feedback Polynomial | 95 | AF | A6 | F3 | B4 | B8 | C6 | E1
Sidelobe Suppression Ratio (dB)
Cross-correlation Sidelobe Peak Value

## Slide 30: M-Sequences of Length 511
Code Index | M511_1 | M511_2 | M511_3 | M511_4 | M511_5 | M511_6 | M511_7 | M511_8
Feedback Polynomial | 143 | 15E | 17A | 1C2 | 167 | 1E5 | 1A7 | 1E6
Sidelobe Suppression Ratio (dB)
Cross-correlation Sidelobe Peak Value

## Slide 31: M-Sequences of Length 1023
Code Index | M1023_1 | M1023_2 | M1023_3 | M1023_4 | M1023_5 | M1023_6 | M1023_7 | M1023_8
Feedback Polynomial | 204 | 240 | 291 | 312 | 237 | 3D8 | 262 | 28C
Sidelobe Suppression Ratio (dB)
Cross-correlation Sidelobe Peak Value

## Slide 32: M-Sequences of Length 2047
Code Index | M2047_1 | M2047_2 | M2047_3 | M2047_4 | M2047_5 | M2047_6 | M2047_7 | M2047_8
Feedback Polynomial | 40B | 56A | 5E4 | 767 | 416 | 44A | 4FB | 67B
Sidelobe Suppression Ratio (dB)
Cross-correlation Sidelobe Peak Value

## Slide 33: Cross-Correlation with HRP Preambles

## Slide 35: Cross-Correlation with LRP Preambles
LPR preambles are a continuous stream of pulses
Mode | Modulation | PRF (MHz) | SHR
Base Mode | OOK | 1.0 | 16 - 128 pulse (non-ERDEV); 16 – 256 pulses (ERDEV)
Dual-frequency modes | PBFSK | 1.0 | 16 – 256 pulses
 | PBFSK | 2.0 | 
 | PBFSK | 4.0 | 

## Slide 36: Cross-Correlation with LRP Preambles
 | Channel Band Number | ERIP
HRP | 9 | Mean EIRP = -14.3dBm
LRP | 2 (center freq. identical to HRP channel 9) | Peak EIRP = 12dBm
Correlation between HRP preambles and LRP preambles

## Slide 37
Correlation between m-sequences and LRP preambles are not worse than HRP preambles

## Slide 38
Transmit m sequences and receive LRP

## Slide 39: Autocorrelation and Cross-correlation of Legacy Preambles

## Slide 40: Conclusions
m-sequences could be used as preamble codes for 802.15.4ab data communications
Excellent periodic autocorrelation
Good cross-correlation properties with HRP and LRP preambles
Good periodic cross-correlation properties
  They could provide up to 30dB/24dB rejection (12 dB/ 6dB better than length 127 sequences) in the vicinity of 3/7 other devices
Sync Length can be reduced by using shorter delta spreading function (L=1, 2) and fewer number of preamble symbols (e.g. Nsync = 8, 16) leading to reduced air time

## Slide 41: Strawpoll
M-sequences should be adopted in 802.15.4ab for data communications
Y
N
A

## Slide 42: References
[1] 15-21-297-01 15.4.ab Technical Guidance Doc
[2] A.F. Molisch et al., IEEE 802.15.4a Channel Model - Final Report, IEEE TG802.15.4a, 15-04-0662-08-004a, November, 2004.
[3] IEEE Std 802.15.4z-2020
[4] V. P. Ipatov, “Ternary sequences with ideal autocorrelation properties” Radio Eng. Electron. Phys., vol. 24, pp. 75−79, Oct. 1979.
[5] 15-21-152-00 802.15.4z - HRP UWB PHY - HPRF mode preamble sequence cross-correlation properties
[6] 15-05-737-01 Length 127 Preamble codes for 500 MHz and 1500 MHz bands

## Slide 43: Questions?

## Slide 44: APPENDIX

## Slide 45: Channel Estimation
  Matched filter output is equal to the channel impulse response plus noise (assume symbol length ≥ channel length)
matched filter correlates 1 preamble symbol
matched filter correlates 4 consecutive preamble symbols

## Slide 46: Channel Estimation
m-sequences can perform well as the ternary sequences in matched-filter based channel estimation
4 preamble symbol is used for channel estimation
matched filter correlates 1 preamble symbol
matched filter correlates 4 consecutive preamble symbols

## Slide 47: Channel Estimation
Performance of channel estimation can be improved by using least squares
1 preamble symbol is used for channel estimation
4 preamble symbol is used for channel estimation

## Slide 48: Channel Estimation
Compare the performance of the matched-filter based channel estimator
In the simulations, we let the total preamble length about the same, i.e.,
 | K | L | # Symbols | Total Length
S9 | 127 | 4 | 64 | 32512
M63 | 63 | 8 | 64 | 32256
M255 | 255 | 2 | 64 | 32640
M511 | 511 | 1 | 64 | 32704
M1023 | 1023 | 1 | 32 | 32736
M2047 | 2047 | 1 | 16 | 32752

## Slide 49: Channel Estimation

## Slide 50: Channel Estimation

## Slide 51: Channel Estimation
Preamble received signal at ADC is quantized to 5 bits
Performance is similar to non-quantized cases.

## Slide 52: Channel Estimation

## Slide 53: Channel Estimation

## Slide 54: LRP Modes
LRP base mode (1 Mb/s)
  Tsym = 1us, Tchip = 1us, 1 chip per symbol
  Each pulse is much shorter than Tchip
  Preamble: a continuous stream of pulses with length 16 – 128 at the base mode PRF of 1 MHz

## Slide 55: LRP Modes
LRP extended mode (250 kb/s)
  Tsym = 4us, Tchip = 1us, 4 chips per symbol
  Preamble: a continuous stream of pulses with length 16 – 256

## Slide 56: LRP Modes
LRP long-range mode (31.25 kb/s)
  Tsym = 32us, Tchip = 0.5us
Preamble consists of 3 parts:
  Part 1: a continuous stream of 1024 - 8192 pulses
  Part 2: - - - P - P - - P - - P P P - P (“P” – pulse; “-” – no pulse)
  Part 3: a stream of 16 – 64 “1” symbols

## Slide 57: Carrier Frequency Offset
Carrier frequency offset (CFO) can be estimated from the matched filter output
Let x[n] be the received preamble (sync) signal, and the matched filter output is
where s[n], n = 0, 1, …, KL-1, is the preamble symbol sequence
Assume n0, n0 -KL, n0 -2KL, n0 -(P-1)KL are the ending indices of each preamble repetition in the preamble. The autocorrelation of y[n0 -pKL], p = 0, 1, …, P-1 is
with its phase equal to 2πKLf. Thus, the carrier frequency offset f is estimated by

## Slide 58: Carrier Frequency Offset
y[n0]
y[n0-KL]
y[n0-2KL]
received sync signal x
correlator output
symbol 0
symbol 1
symbol 2
KL
KL
(·)* - complex conjugate

## Slide 59: Preamble Correlator
s
received sync signal x
preamble pattern s
KL
K – sequence length
L – spreading factor
x[n]
x[n-(KL-1)]
s[KL-1]
s[0]
correlator output
The preamble correlator requires
KL-1 adders
KL-1 memory elements
#adders and #memory are about KL (i.e., length of one preamble symbol)
multiply-and-sum corresponding elements

## Slide 60: Carrier Frequency Offset
The assumption |KLf| ≤ 0.5 requires KL to be not large
With max. ±20ppm clock frequency error, the max. CFO is ±40ppm
Assuming max. carrier frequency = 9984.0 MHz (Channel 14). The max. f is
±40ppm × 9984.0 / 499.2 = ±0.0008
Preamble Code | K (preamble code length) | L (length of delta spreading function | #Chips Per Symbol | Max. CFO | Max. f | Max. KLf
S1 – S8 | 31 | 16 | 496 | ±40ppm | ±0.0008 | ±0.3968
S1 – S8 | 31 | 64 | 1984 | ±40ppm | ±0.0008 | ±1.5872
S9 – S24 | 127 | 4 | 508 | ±40ppm | ±0.0008 | ±0.4064
S25 – S32 | 91 | 4 | 364 | ±40ppm | ±0.0008 | ±0.2912

## Slide 61: Preamble Correlator for Long Symbols
If a preamble symbol is too long to satisfy the condition |KLf| ≤ 0.5, we need to break the long preamble symbol into shorter segments
received sync signal x
preamble pattern s
KL
K – sequence length
L – spreading factor
x[n]
x[n-(KL-1)]
s[KL/2]
s[0]
The correlator output associated with the long symbol is replaced by the outputs of two short correlators, i.e.,
y0[n] for segment 0
y1[n] for segment 1
The 1st output y0[n] requires
KL/2-1 adders
KL/2-1 memory elements
The 2nd output y1[n] requires
KL/2-1 adders
KL/2-1 memory elements
Total #adders and #memory are about KL (length of one preamble symbol)
s[KL-1]
s
segment 0
segment 1

## Slide 62: Preamble Correlator for Long Symbols
received signal x
Symbol 0
Symbol 1
y0[n] for segment 0
y1[n] for segment 1
y0[n0-KL]
y1[n0]
y0[n0]
y1[n0-KL]

## Slide 63: Correlator Design for Long Symbols
K (preamble code length) | L (length of delta spreading function) | #Chips Per Symbol | Max. CFO | Max. f | J | Q | Max. Qf
63 | 8 | 504 | ±40ppm | ±0.0008 | 1 | 504 | 0.4032
255 | 2 | 510 | ±40ppm | ±0.0008 | 1 | 510 | 0.4080
511 | 1 | 511 | ±40ppm | ±0.0008 | 1 | 511 | 0.4088
1023 | 1 | 1023 | ±40ppm | ±0.0008 | 2 | 511, 512 | 0.4096
2047 | 1 | 2047 | ±40ppm | ±0.0008 | 4 | 511, 512, 512, 512 | 0.4096

## Slide 64: Carrier Frequency Offset
To simulate the CFO estimation performance, we assume the total preamble length is about the same for different preamble sequences
 | K | L | # Symbols | Total Length
S9 | 127 | 4 | 64 | 32512
M63 | 63 | 8 | 64 | 32256
M255 | 255 | 2 | 64 | 32640
M511 | 511 | 1 | 64 | 32704
M1023 | 1023 | 1 | 32 | 32736
M2047 | 2047 | 1 | 16 | 32752

## Slide 65: Carrier Frequency Offset
Given 1ppm residual CFO, the phase drift is about 1.26e-4 radian/chip (about 0.064 radians per 512 chips), which can be handled by a 1st-order phase tracking loop

## Slide 66: Carrier Frequency Offset

## Slide 67: Carrier Frequency Offset