## Slide 1
Project: P802.15 Working Group for Wireless Specialty Networks
Submission Title: Response to 802.3 comments on SG 15.6a PAR and CSD
Date Submitted: July 19th, 2021
Source: M. Hernandez(YRP-IAI), T. Kobayashi(YNU), M. Kim(YRP-IAI), R. Kohno (YNU/YRP-IAI)
Company: [1;Yokohama National University(YNU), 2;YRP International Alliance Institute(YRP-IAI)]
Address [1; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan
2; YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan]
Voice:[+81-90-5408-0611], FAX: [+81-45-383-5528],
Email:[1: kohno@ynu.ac.jp, 2: kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract:
Purpose: In response to call for technical contributions
Notice: This document has been prepared to assist P802.15.6a. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6a.

## Slide 2: Draft P802.15.6a (1)
Amendment: Dependable Human and Vehicle Body Area Networks,
PAR
General – We believe the two topics should not be in a single project because the environmental, regulatory, and other concerns are so different. The scope of the project does not fit within the scope of the standard.
Response – See next slide (*).
General – We struggled to understand the scope of this PAR! Is our understanding correct that this project is to permit use of 802.15.6 BANs within the automotive environment? This is the only conclusion we could come to that made sense to the comment ad hoc. If not, then we would ask IEEE 802.3 to direct its Chair to oppose this project.
Response – See next slide (**).

## Slide 3: Continue (*)
Response (*): The PAR of 15.6 Std Wireless BAN is not constrained to humans. The project amendment, 15.6a, intends to extend 15.6 Std WBAN with a vehicle BAN, while supporting higher dependability to human BAN. Therefore, the scope of the project fits the scope of 15.6 Std within one project.
A target use case is a human wearing a BAN sitting in a vehicle or standing nearby a vehicle, communicating with a VBAN. Due to the nature of the wireless medium, both human BAN and vehicle BAN must comply with adequate performance in the shared environment and regulations for human and vehicle safe usage.

## Slide 4: Continue (**)
Response (**) – 15.6a aims to extend the operation of 15.6 WBAN to a vehicle. The scope of Std 802.15.6 is not constrained to humans. A BAN can be constructed around a vehicle (VBAN). In particular, we target the use case of a HBAN with higher dependability operating in a vehicle or nearby a vehicle, which supports a VBAN.
Obviously, the HBAN and VBAN may be designed separately, but that is not the intention. Due to the nature of the wireless medium, when a HBAN is in a vehicle or nearby a vehicle and such vehicle supports a VBAN, both share the same environment, frequency band, potential interference, etc. Hence, the idea is to design one 15.6a network that supports both HBAN and VBAN, such that when they operate close to each other, we can control how they operate.

## Slide 5: Draft P802.15.6a (2)
3.1 — Why does the WG name not agree with what is listed on http://ieee802.org? Did the WG change its name without approval of the EC, or is the EC page wrong? (The draft PAR WG name does agree with the WG name in myProject.)
Response – The 802.15 WG Chair will contact the 802 EC Secretary w.r.t. updating the multiple places still using the old WG name and to update it with the new WG name - “Wireless Specialty Networks”.
5.4 — The mix of text for medical and auto is very awkward and deserves a better change than the new second paragraph. Perhaps: "Additionally this standard provides enhanced dependability that is required for some medical use cases. This includes remote medical healthcare, therapy and other monitoring that can enhance quality of life (QoL) in various population segments.”
Response – Thank you for the feedback; we have revised the text.

## Slide 6: Draft P802.15.6a (3)
CSD: https://mentor.ieee.org/802.15/dcn/21/15-21-0260-02-006a-ieee-802-15-6a-csd-draft.docx
General – If contrary to our assumption, the project is to specify two different networks (human body versus auto), and honest CSD responses were given, the responses for auto and human body would be entirely disjoint and would not fit within a single project.
Response – The project intends to specify one extension of 15.6 WBAN with 2 use cases HBAN and VBAN sharing the same wireless medium in a vehicle or nearby a vehicle. Your assumption of 2 disjoint wireless networks is incorrect.
See next slide.

## Slide 7: Continue
In other words, there is one 15.6a wireless network with 2 use cases: human BAN and vehicle BAN. The anchor point of design is the case when HBAN and VBAN share the same wireless medium, i.e., a human in a vehicle or nearby a vehicle. HBAN and VBAN share the same frequency band, the same access control, the same environment as in the specification of Std 802.15.6, the coordinator on a BAN can communicate to an external access point.
  As a byproduct, 15.6a HBAN and VBAN may work separately.

## Slide 8
BAN
VBAN
Example use case

## Slide 9: Draft P802.15.6a (4)
1.2.1, a — "IEEE 802.15.6-2012” should be "IEEE Std 802.15.6-2012”.
Response – Accepted.
1.2.1, a – Second paragraph “Enhancement to” should be "The enhancement of”.
Response – Accepted.
1.2.4, a — "IEEE 802.15.6-2012” should be "IEEE Std 802.15.6-2012”.
Response – Accepted.
1.2.4, a – Second paragraph “Enhancement to” should be "The enhancement of”.
Response – Accepted.

## Slide 10: Draft P802.15.6a (5)
1.2.4 1, a – It is not clear what is meant by “interact”, does this mean that the body area network of a passenger would bridge into the vehicle body network? Or, is the interaction only referring to radio interference?
Response – See next slide.
1.2.4 1, b – Our participants that have attended some of your meetings do not see planned participation from individuals affiliated with automotive OEMs and suppliers – please provide.
Response – Tier 1: Denso, Bosch, Mahle. Tier 2: Infineon, NXP, Qorvo. Car manufacturer: Nissan, VW, Ford.

## Slide 11: Continue
Response – We consider the case when a HBAN coordinator talks to another VBAN coordinator as this is a target use case. An example use case is about a senior car driver, monitoring health (HBAN) and safety for preventing car incidents (VBAN). That is what we mean by “interact”. A HBAN coordinator can communicate with a VBAN coordinator as they are part of the same 15.6a design.