## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: PHY Solution for Coexisting BANs and Other Networks with Space-Time Interference Mitigation
Date Submitted: July 15th, 2021
Source: Takumi Kobayashi, Ryuji Kohno
Company: ] [1;Yokohama National University(YNU), 2;YRP International Alliance Institute(YRP-IAI)]
Address [1; 79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan
2; YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan]
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp, Kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract: This provides considerations of radio environment surrounding human body area network(HBAN) and vehicle body area network(VBAN) for enhanced dependability. As an example of PHY layer countermeasure technology of these co-existence and EMC/EMI issues, signal processing technology on space and time domains based on orthogonal matched filter is introduced.
Purpose: Material for discussion in P802.15.6a SG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: PHY Solution for Coexisting BANs and Other Networks with Space-Time Interference Mitigation
Takumi Kobayashi, Ryuji Kohno
(YNU/YRP-IAI)

## Slide 3: Various Interference in Coexistence
＊ IEEE 802.11a (wi-fi) （5GHz） overlaps
Other UWB-BAN
user ？
User “B”
User “A”.
A wants to connect to “B”.
UWB-WBAN
IEEE 802.15.6
Other UWB system.
e.g. IEEE 802.15.4-2020 IEEE 802.15.4z
user ？
user ？
interference
interference
Inter-user interference
“IUI”
“ISI”
Interference from a system using the same standard.
Inter-system interference
Known signal. Pre-knowledge can be used to mitigation
Interference from a system using overlapped frequency
Unknown signal.
EMI / EMC issues
Other BAN
Inter-BAN interference
“IBI?”
Other NB-BAN
VBAN  HBAN interference

## Slide 4: EMC (Electro-Magnetic Compatibility)
Pulse noise,
Colored noise etc..
Other devices e.g. Medical devices
Thunder,
Electrostatic discharge; ESD
Other radio devices
e.g. cellular phone, cellular base station
Power electronics
motors
Microwave oven
BAN device
Interference
Emission

## Slide 5: Medical room radio environment
Vital monitor
Cardiac output monitor
Artificial respirator
Infusion pumps

## Slide 6: Environment Model in Vehicle
5
1
2
3
4
6
Engine/motor diagnostic sensor and controller
Air pressure sensor, wheel health sensor and controller
Transmission monitoring sensor and controller
Cabin environment sensor (temperature, brightness, humidity etc.)
Sheet sensor, health care sensors for driver
Sheet sensor, health care sensors for passenger
Engine/Motor room environment model
Cabin room environment model
https://media.istockphoto.com/photos/transparent-car-design-wire-model3d-illustration-my-own-car-design-picture-id594040008?k=6&m=594040008&s=612x612&w=0&h=XE8LiBjpM51aB4pH2CFt6-MT6IvALRPnlxPcac0RXhg=
Note:
Various type of car/vehicles
Bus, Bulldozer, Heavy construction equipment needed each different sensors.

## Slide 7: Engine/Motor Room Environment
Many metallic components
Components existing in densely
Ignition noise, motor noise
Larger path-loss than free propagation
A lot of reflection of RF signal
Electro-magnetic interference, EMI issues
Ignition coil
Electric motor
High current battery and cable
Spark plug
Electric generator
https://www.as-web.jp/car/575374/attachment/03a_sub_dsc01273
Especially EV

## Slide 8: Electromagnetic Environment
Lane departure system
Night vision
Front object CCD camera
Front airbag sensors
Nighttime pedestrian warning
Drowsiness sensos
Front object laser radar
Active park assist
Tire pressure sensor
Rear object monitor CCD camera
Rear camera
Blind spot detection
Cross traffic alert
Central computer
Rear object laser radar
Wheel speed sensor
Tire pressure sensor
Side airbag SRS
Adaptive cruise control
Steering angle sensor
Automatic brake actuator
Wheel speed sensor
Nighttime pedestrian warning IR sensor
Sensors, monitors and vehicle controlling systems in modern vehicle

## Slide 9: EMC model
Source
Sources of EM near and far field: may be off board and on board sources
Path: radiated or conducted
Sink: intended receiver or unintended receiver
Path
Sink
Radar application
Radar application
Engine control application
Body control applicaition
Head unit
Camera application
Camera application
Dashboard application
Multimedia application
rear seat entertainment
Camera application
Camera application

## Slide 10: Channel models and scenarios in IEEE802.15.6-2012
IEEE 802.15.6-2012 channel models considered
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
CM1, 2, 3, 4
Scenario 1, to Scenario 7. (S1 – S7)
IEEE P802.15-08-0780-12-0006-TG6

## Slide 11: Channel model
Sink
Source
Channel model
Path loss
Reflection
Multipath
Fading
LOS / NLOS model
White Gaussian noise

## Slide 12: Environmental model
Sink
Source
Channel model
Path loss
Reflection
Multipath
Fading
LOS / NLOS model
White Gaussian noise
Interference to the other devices
Interference from the other devices
Colored noise
Human impact

## Slide 13: Channel and Environmental Models
Path loss
Reflection
Multipath
Fading
LOS / NLOS model
White Gaussian noise
Interference from co-existing wireless systems e.g. Bluetooth, IEEE 802.11, IEEE 802.15.4 etc.
Interference from the other BANs.
Interference from the other electric systems, devices and components (Electro-magnetic interference; EMI from electric motors, spark plugs in vehicles, etc.
Electro-magnetic compatibility; EMC. Possibility to affect to the other systems and human body.
VBAN  HBAN interference
VBAN and HBAN  Vehicle control and human body impacts.
Colored noise (Impulse noise, spike noise, ignition noise etc.)
Time-varying channel and interference modeling (Statistic, non-static, pseudo static model)
※optional
or
?
Environment model
Channel model
Channel model
EMI EMC
Colored noise
Other wireless systems
Environment model
Time-varying modeling
※mandatory
※mandatory
※mandatory
※mandatory
※optional
※optional
※optional
※IEEE802.15.6-2012
※will be defined in this amendment
※mandatory
or
?
※mandatory
※Comment on 1st session

## Slide 14: Classification of Channel and Environment Models for Human and Vehicle Body Area Networks (HBAN&VBAN)
Note:
HBAN-model:
-Environment with co-existing systems is not considered.
VBAN model:
Key-less entry system
Localization in-body, on-body
Most dominant model should be defined and separatory defined as Mandatory and Optional.
Channel model
HBAN model
VBAN model
In-body (Implant)
On-body
Around body
Outdoor
Indoor
Home
Office
Medical (e.g. Hospital)
In-vehicle
On-vehicle
Around vehicle
Engine room
Cabin
Through engine room and cabin
Roof
Side Right/Left/Front/back
Bottom
Static vehicle
Moving vehicle
※Covered by IEEE 802.15.6-2012
※not covered yet
※mandatory
※mandatory
※Around meaning;
Desk, WiFi AP in the room etc.
Channel model
With environment
※
※
※
※
※
※mandatory

## Slide 15: Issues on multiple BAN environment
  Inter-user interference
    IR-UWB uses the same pulse as all users signal in the same standard.
    Other users signal and/or the other network signal would be interference.
  Inter-system interference
    Interference from the other wreless system using overlapped frequency band. ⇒ Unknown
＊ 802.11a (wi-fi) （5GHz） overlaps
user C
user ？
user B
User A wants to connect to“B”.
UWB-WBAN
IEEE 802.15.6
Other UWB system.
e.g. IEEE 802.15.4a
user ？
user ？
interference
interference

## Slide 16
Purpose and Suggestion
  Sparate and Recognize each interference from different source. ⇒ Apply suitable interference mitigation method according to source of interference.
  Using both of Spatial and Temporal signal processing.
Inter-user interference
Recognize and demodulate
Remove
Interference canceller
Multi-user detection
Pulse shape multiple access
“IUI” in this presentation
“ISI” in this presentation
Interference from a system using the same pulse
Inter-system interference
Interference from a system using overlapped frequency
known
unknown
Notes: 16

## Slide 17
OMF； orthogonal matched filter
  consists a matched filter （MF1） and MF Group（MFG）
  Tap coefficients of MF1 are the same as sequence of desired signal.
  Coefficients of MF1 and each MFk that constituting MFG are orthogonal.
  Desired signal does not through MF2～K-1 because orthogonality. →only interference can through.
  MFG makes replica of interference signal by lenear combination with weight vector w of linear combiner; LC.
  Subtract interference replica from the output of MF1 .
Principle of OMF
  OMF can remove interference without any pre-knowledge of interference.
Notes: 17

## Slide 18
Matched Filter (MF) 1
Matched Filter (MF) 2
Matched Filter (MF) 3
Matched Filter (MF) 4
Matched Filter (MF) k
Antenna
Desired signal + interference
Desired signal + interference
W1
W2
W3
Wk
Linear combiner
+
subtract
Adaptive algorithm
e.g. LMS
Mixed signal EXCEPT desired signal.
Replica of interferences
Orthogonal
Orthogonal
Orthogonal
Orthogonal

## Slide 19
Apply pulse based OMF to spatial signal processing
  TDL array antenna
    Configured by multiple antennas and tapped delay line （TDL）
    TDL-AA can separate the signals which comes from the same direction by using time-domain signal processing.
  By applying OMF to TDL-AA
    Interference reduction is performed on the both of domains of time and space.
Space-temporal signal processing
Notes: 19
therefore

## Slide 20
Space-temporal interference reduction (SC.7)
System has gain against an interference →residual interference
Interference signal is reduced
TDL-AA without null-steering（ SC.6）
No gain
Gain≠0
Gain≠0
Notes: 20

## Slide 21
Space-temporal interference reduction(SC.7)
TDL-AA without null-steering （ SC.6）
Gain≠0
No gain
MHP orthogonality
System has gain against an interference →residual interference
Interference signal is reduced
Notes: 21

## Slide 22
Desired user
Undesired users
10
10
Application to V2V communication

## Slide 23
Simulation
modulation | BPSK
Spread spectrum | DSSS
code | 31bit Gold-sequence
Tx power | 10[mW]
Center freq. | 760[MHz]
Antenna | 5 elements circular array
channel | AWGN (-103.8[dBm])
User number | 4 30
Data size | 1000[bit]
Arrival angle | Desired signal: 0 deg. Interference ±180 deg. or ±10deg
Own vehicle
Desired vehicle
Interference vehicle

## Slide 24
BER-DIR performance
interference：±180 deg.
Bit error rate
DIR[dB]
interference：±10 deg.
DIR[dB]
30 users, ( 1 desired user, 29 interference)
Extended OMF can improve BER performance.
Space-temporal signal processing
Space-temporal signal processing

## Slide 25
Conclusion
  Importance of consideration of interference, EMC/EMI issues including as environmental models as well as channel models is suggested.
  Human and Vehicular BANs environmental model
  OMF based signal processing to interference reduction have been proposed.
    Interference reduction against unknown interference.
    =>Interference mitigation (reduction) against unknown source in Time-domain.
  OMF and its extension in space and time domain signal processing
    Interference mitigation on Time and space domains signal processing.
    => Space-time domain interference mitigation.
Notes: 25

## Slide 26: References (1/2)
Takumi Kobayashi Chika Sugimoto, Ryuji Kohno, “Theoretical analysis of interference canceler using modified hermite polynomials based orthogonal matched filter for IR-UWB systems in AWGN and interference channel,” Proc. 2017 20th International Symposium on Wireless Personal Multimedia Communications (WPMC) 2017, DOI: 10.1109/WPMC.2017.8301793
Takumi Kobayashi, Masato Suzuki, Chika Sugimoto, Ryuji Kohno, “Space temporal interference cancellation using TDL array antenna and waveform based OMF for IR-UWB systems,” ICT Express, Volume 1, Issue 2, pp.71-75, 2015. ISSN 2405-9595, https://doi.org/10.1016/j.icte.2015.09.006.
Takumi KOBAYASHI Chika SUGIMOTO Ryuji KOHNO, “Interference Cancellation for Intra and Inter UWB Systems Using Modified Hermite Polynomials Based Orthogonal Matched Filter,” IEICE TRANSACTIONS on Communications Vol.E99-B No.3 pp.569-577, 2016.

## Slide 27: References (2/2)
Kento Takabayashi, Shuhei Harada, Takumi Kobayashi, Katsumi Sakakibara, Ryuji Kohno, "Low-Computational Extended Orthogonal Matched Filter Structure for Multiuser Detection," Telecom, 2020, vol.1, issue.1, pp. 32-47, Jun. 2020. doi: 10.3390/telecom1010004
Shuhei Harada, Kento Takabayashi, Takumi Kobayashi, Katsumi Sakakibara, Ryuji Kohno, "Theoretical Analysis of Interference Cancellation System Utilizing an Orthogonal Matched Filter and Adaptive Array Antenna for MANET," Journal of Sensor and Actuator Networks. 2019, 8(3) 48; September, 2019. https://doi.org/10.3390/jsan8030048
Masato Suzuki and Ryuji Kohno, ”A Study on Time-Space Interference Cancellation Using Array Antenna and OMF for Inter-Vehicle Communications,” IEICE Technical Report Vol.115 No.73, Jul. 2015, pp.1-5, (in Japanese)
Masato Suzuki and Ryuji Kohno, ”Time-Space Interference Cancellation System Using OMF,” The 38th Symposium on Information Theory and Its Applications (SITA2015), Nov. 2015, pp.492-496, (in Japanese)

## Slide 28
Thank you for your attention.

## Slide 29
  Results (noise free channel)
DIR vs. BER (SC.1) Eb/N0=+∞dB.
DIR vs. BER (SC.2) Eb/N0=+∞dB.
More iteration number makes higer capacity of interference reduction
Notes: 29

## Slide 30
Simulation results
  (noise free channel)
DIR vs. BER Eb/N0=+∞dB.
More iteration number makes higer capacity of interference reduction

## Slide 31
Simulation results
  (noise & interference channel)
DIR vs. BER (SC.2) Eb/N0=+25dB.
Wopt which is generated by theory does not satisfies minimum error In high DIR condition. ⇒ Wopt is not optimal solution in environment in which noise exists.
High DIR  dominant cause of bit error is noise
Noise
enhancement

## Slide 32
  Theoretical performance
Size reduction of weight vector by a coefficient Δ
Square error using various fixed Δ and Δopt in each DIR (SC.2) Eb/N0=+25dB.
Optimum solution
  Smaller Δ
⇒residual interference is increased
⇒noise enhancement is suppressed
  Larger Δ
⇒residual interference is suppressed
⇒noise enhancement is increased
Notes: 32

## Slide 33
  Results of SC.1
Square error characteristics in various DIR(SC.1).
Adaptive algorithm does not find an optimum weights in low DIR and low Eb/N0. ⇒ ⇒ ⇒ Theoretical analysis with Noise
Eb/N0=+120dB, DIR=-40dB ~ +40dB
Square error characteristics in various DIR (SC.1).
Eb/N0=+25dB, DIR=-40dB ~ +40dB
Notes: 33

## Slide 34
Space-temporal interference reduction(SC.8)
Interference can be eliminated if either one is different from the desired signal
TDL-AA without null-steering with OMF （ SC.8）
Gain≠0
reduction
Max. gain
Max. gain
System has gain against an interference→residual interference
Notes: 34

## Slide 35
8 users
30 users

## Slide 36
BER-DIR performance
interference：±180 deg.
Bit error rate
Bit error rate
Bit error rate
DIR[dB]
5 users, ( 1 desired user, 4 interference)
Interference: ±10 deg.
DIR[dB]
BER performance is improved in high DIR situation.