## Slide 1
Project: IEEE P802.15 Working Group for Wireless Speciality Networks (WSN)
Submission Title: Next Steps for IEEE 802.15.3
Date Submitted: 15 July 2021
Source: Thomas Kürner TU Braunschweig
Address Schleinitzstr. 22, D-38092 Braunschweig, Germany
Voice:+495313912416, FAX: +495313915192, E-Mail: t.kuerner@tu-bs.de
Re: n/a
Abstract: This document describes the need for a revision of IEEE 802.15.3
Purpose: Discussion Document to form a Study Group targeting a revision of IEEE Std. 802.15.3
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Next Steps for IEEE 802.15.3

## Slide 3: Current Situation (1/4)
  Frequency Bands:
    IEEE Std. 802.15.3d-2017 covers the frequency band 252 to 321 GHz
    At WRC 2019 additional frequency bands beyond 321 have been identified for the use by Land Mobile Service (LMS) and Fixed Service (FS)
    Of specific interest are 94 GHz contigous spectrum between 356 and 450 GHz, which may be used especially for short-range applications
    =>During the May Wireless Interim the group made a motion to create a SG to amend IEEE Std. 802.15.3 (SG 3g 300 GHz Frequency Extension)

## Slide 4: Current Situation (2/4)
  Reference to IEEE Std. 802.1D:
    802.15.3 includes a reference proority mapping using 802.1D-2004
    802.1D-2004 is being withdrawn, so we would need to replace the reference priority mapping to use 802.1Q
    =>This needs to be fixed in the standard and can be done best in a revision

## Slide 5: Current Situation (3/4)
  Fixing issue with large propagation delays in Backhaul/Fronthaul applications:
    MAC in IEEE Std. 802.15.3d was largely inherited form IEEE Std. 802.15.3e
    IEEE 802.15.3e is for close proximity applications exepcting short propagation delays
    Within the H2020 EU-Japan project ThoR, IEEE 802.15.3e chipsets are used to demonstrate IEEE 802.15.3d at backhaul applications => potential time outs adn unnecessary retransmission
    To fix this, the chipsets used in ThoR allow larger retry inter-frame space, RIFS
    =>This should be also fixed in the standard and can be done best in a revision

## Slide 6: Current Situation (4/4)
  An amendment woul be the fourth amendment
  End of 2021 the time period since the last amendment will be four years
  => Both conditions will trigger a revision anyway

## Slide 7: Conclusion
  Instead of creating a Study Group on amendment 3g (300 GHz Frequency Extension) it is better to go for a revision project (3m)
  This revision should consist of at least of:
    Roll-up of IEEE Std. 802.15.3
    300 GHz frequency extension
    Fixing the 802.1D/802.1Q issue
    Fixing the RIFS issue

## Slide 8: Possible Time Line
July 2021:
  EC Approval
September 2021:
  SG3m Kick-Off, writing of PAR and CSD
November 2021:
  EC approval for TG3m
January 2022:
  Kick-off of TG3m
Target:
  Finishing revision until beginning 2023