## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [UWB Sensing in 802.15]
Date Submitted: [16 July, 2021]
Source: [Frank Leong, Wolfgang Küchler, Riku Pirhonen] Company [NXP Semiconductors]
Re: [Input to the Working Group]
Abstract: [Presentation, UWB in 802.15, sensing]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | Monostatic and multistatic radar operation
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: UWB Sensing in 802.15

## Slide 4: Sensing – Context Recap
Focus on key functionalities to be provided by UWB:
  Ranging with high integrity (handsfree access use cases)
  Localization (indoor navigation use cases)
  Sensing (presence detection use cases)
  Coordination & scheduling to support the above
Provide accurate ranging via a low-cost, mass-market solution
  Low energy-per-ranging
  Low channel-occupancy-per-ranging a.k.a. spectral efficiency (many devices operating at the same time & place)
  Re-use of hardware between use cases

## Slide 5: UWB Sensing – Terminology (1)
CIR = Channel Impulse Response (estimated characteristics)
Stations/Modules
Monostatic Operation (Nstations = 1)
Multistatic Operation (Nstations = 2...16)
  Sensing Initiator/Responder
  One-Way/Two-Way Multistatic Sensing
  CIR Transmitter/Receiver
Parallel/Sequential Multi-Antenna Operation
  Virtual Antennas (e.g., electronic beamsteering*)
*) E.g., see: U. Nickel: “Fundamentals of Signal Processing for Phased Array Radar”, in Advanced Radar Systems, Signal and Data Processing (pp. 1-1 – 1-22), 2007.

## Slide 6: UWB Sensing – Terminology (2)
Initiator
Target Y
Responder
Initiator
Target X
Monostatic Operation
Multistatic Operation
Station A
Station B
Station C

## Slide 7: UWB Sensing – Terminology (3)
Initiator
Target
Responder
One-Way vs. Two-Way Multistatic Sensing
Station A
Station B
= Sensing Packet 1
= Sensing Packet 2
= Sensing Packet 3

## Slide 8: UWB Sensing – Terminology (4)
Initiator
Target
Responder
One-Way Multistatic Sensing w/ CIR Feedback
Station B (CIR Transmitter)
Station A (CIR Receiver)
Responder
Station C (CIR Transmitter)
= Sensing Packet
= CIR Feedback Packet 1
= CIR Feedback Packet 2

## Slide 9: UWB Sensing – Applications
Short range: up to 30 m
  HRP UWB is able to support this range
Low velocity: up to 5 m/s (18 km/h)
  Vital sign detection (e.g., breathing, heart beat)
  Gesture recognition
  Approach (moving target) detection
  Object (stationary target) detection
  Direction detection (angle), trajectory mapping
  Maximum velocity may be traded against range
High measurement resolution
  Resolution down to sub-cm level (using >1.5 GHz total signal bandwith)
Target types (RCS ≥ -10 dBm2 a.k.a. dBsm):
  Adults, children, infants, pets
  Objects / vehicles (up to freight ship)

## Slide 10: Rationale (1)
Interference from concurrently operating radar systems is a growing problem in several RF bands*
Multistatic radar performance benefits from coordinated TX and RX elements
Standardize UWB sensing in order to
  Enable coexistence with ranging systems
  Enable re-use of ranging system HW
  Maximize the potential of multistatic radar by enabling interoperability / coordination / scheduling
  Avoid future interference problems
  Enable CIR exchange via standardized interfaces
*) E.g., see: https://www.sae.org/news/2021/06/mitigating-radar-to-radar-interference

## Slide 11: Rationale (2)
Interference management is central:
Coordination / Scheduling
  Enable sensors to interact with other stations
  Compact (i.e., low airtime) means of CIR exchange
Global approach to UWB waveform multiplexing methods
  Leverage preamble codes

## Slide 12: UWB Sensing & Ranging (1)
UWB suits both sensing and ranging
  However, performance metrics differ between the two modes
Ranging performance is strongly related to
  SNR (e.g., associated with the Ziv-Zakai bound*)
  Dynamic Range (also in the presence of unwanted signals)
Sensing performance is strongly related to
  Bandwidth (leveraging a unique UWB property**)
  Quality of range-velocity data processing
*) This bound is named after the same Jacob Ziv known for LZ{77,78} for data compression, recipient of the 2021 IEEE Medal of Honor; the paper in question is: J. Ziv and M. Zakai, "Some Lower Bounds on Signal Parameter Estimation", IEEE Trans. Information Theory, vol. IT-15, no. 3, pp. 386-391, May 1969.
**) E.g., see: https://www.ll.mit.edu/sites/default/files/outreach/doc/2018-07/lecture%202.pdf

## Slide 13: UWB Sensing & Ranging (2)
UWB suits both sensing and ranging
  Both modes benefit from large signal bandwidth
  Both modes benefit from waveforms with high quality autocorrelation properties (i.e., clean ranging/radar “ambiguity function”)
Packets may be used for both ranging and sensing at the same time
  Sensing may justify shifting additional energy to the preamble or adding closely scheduled packets to a (legacy) ranging exchange
Sensing may justify use of overall signal bandwidths beyond 500 MHz
  Achievable in low-cost multi-channel UWB implementations with already existing ~500 MHz pulse bandwidths
  Hardware re-use, but dedicated packet scheduling for sensing
  Define interfaces supporting multi-channel CIR exchange

## Slide 14: UWB Sensing – CIR Sharing
Multistatic operation
Responder has CIR (in case of two-way sensing, initiator also has CIR)
Initiator may request CIR (in case of two-way sensing, responder may also request CIR)
Transmission of CIR to be tightly coupled to measurement (correlation between “CIR measurement success” and “CIR transmission success”)
  Tightly coupled (i.e., timing deltas ≤ 5 ms) using wired or wireless interface (e.g., 802.15.4 UWB, NB)
Sensing station may refuse transmitting its CIR (e.g., in case of corrupted measurement)
CIR to be transmitted in a format that does not overly stress the wireless channel (e.g., compressed/delta-only/per-target)