## Slide 1: 64b67b Line Coding for PM-PHY
Date: 2021-08-27

## Slide 2
This contribution proposed 64b67b as an alternative line code for the PM-PHY.
Abstract

## Slide 3: Introduction
IEEE 802.15.13 enables line coding and channel equalization methods for the PM PHY
    8b10b
    FDE
    Both introduce overhead while improving channel adaption
Efficient line coding schemes are proposed
    Line coding overhead can be reduced with an alternative line coding method
    maintaining a good BER performance
    trade off between overhead and channel adaption

## Slide 4: Line Coding
Why optimizing Line Coding?
    Goal: DC balancing
    Low disparity = Low DC imbalance within subsequent code words (Long duration)
    Low run lengths = Low DC imbalance within subsequent modulation symbols (Short duration)
Tradeoff : DC balancing vs. Overhead

## Slide 5: Line Coding Schemes
8b10b
    Guaranteed DC balancing and disparity balancing by predetermined code book with optimized run lengths
    25% overhead
64b67b (Guided Scrambling)
    Statistical optimized DC balancing, disparity balancing and run lengths limiting by code word selection
    4.7% overhead
No Line Coding
    Statistical DC balancing by law of large numbers, (prior scrambling mandatory)
    0 % overhead

## Slide 6: Run Length after Line Coding
Line codes can reduce run lengths
    uniformly distributed input sequences (=no line coding) are obtained by scrambling before line coding

## Slide 7: Disparity after Line Coding
8b10b and 64b67b set boundaries for disparity
Uniform (w/o Line Coding) is out of bounds (note y-axis scaling)

## Slide 8: Spectrum after Line Coding
Line coding reduces low-frequency components :
    more overhead  less impairments due to baseline wander

## Slide 9: Baseline Wander after Line Coding
Calculation of baseline wander percentages
BLW = Average baseline wander amplitude
≈ Zero crossing amplitude
Stream = Average data stream amplitude
≈ Eye Amplitude
Baseline wander percentage tream

## Slide 10: Baseline Wander vs. Symbol Rate
Baseline wander decreases with increasing symbol rate

## Slide 11: BER of 8b10b
Bit error rates for 8b10b (25% overhead)
    (Post-FEC BER is greyed out)
    8b10b can reduce baseline wander also w/o EQ at clock rates <= 50 MHz

## Slide 12: BER of 64b67b
Bit error rates for 64b67b (~5% overhead)
    (Post-FEC BER is greyed out)
    64b67b needs EQ but reduces overhead to 5%
    Needs ~ 2dB more SNR compared to 8b10b with EQ

## Slide 13: BER w/o Line Coding
Bit error rates w/o Line Coding (0% overhead)
    (Post-FEC BER is greyed out)
    No Line Coding needs EQ but reduces overhead to 0%
    Needs ~ 1dB more SNR compared to 64b67b with EQ

## Slide 14: Conclusions
FDE has major impact on BER, but is not needed with 8B10B at lower symbol rates
With FDE, the loss is up to 2dB and 3dB SNR for 64B67B and No Line Coding, respectively, compared to 8B10B
Overhead of 25, 4.7, 0% for 8b10b, 64b67b and No Line Coding, respectively
Proposal is to add new MCS to PM PHY which allow
  64b67b Line Coding
  No Line Coding
Enable higher data rates for PM PHY

## Slide 15: To be specified
64b67b Line Coding scheme
No Line Coding scheme
Integration into the PM-PHY
  Decoding approach
  Padding: Mapping of FEC code words onto the used Line Code

## Slide 16: Guided Scrambling Line Coding
Exemplary: 64b67b
    N = 64, Na = 3
General encoding process
    Augment (<=N)-bit data by Na-bit values
    Scramble data
    Select code word out of 2^Na „quotients“
General decoding process
    Descramble (<=N+Na)-bit code block
    Remove augmentation bits from the beginning of the output sequence

## Slide 17: Guided Scrambling Line Coding
Encoding

## Slide 18: Guided Scrambling Line Coding
Decoding

## Slide 19: Scrambler configuration
Scrambling polynomial
    X^Na+X^0
Scrambler initialization
    Initialize each scrambler for every data block of length (<=N) at first bit
Process for each data block
    Pre-ocuppy each scrambler with augmentation values
        aug := [CNa, …, C2, C1] where CNa is MSB of augmentation value
    Scramble (<=N)-bit data block
    Mux Na-bit augmentation value and scrambled block
Scrambler, Na=3

## Slide 20: Exemplary Code Selection method
A) Specify a test vector for the first quotient for 64b67b guided scrambling LC for testing purposes
    Guided scrambler output = Q1
B) Specify a test vector for each of the eight quotients for 64b67b guided scrambling LC for testing purposes
    Guided scrambler output = Qi , i = (1 … 8)
…

## Slide 21: Block decoding
Descramble (<=N+Na)-bit code block
Remove augmentation bits from the beginning of the output sequence
…

## Slide 22: FEC segmentation and padding lengths
Data block sequences are padded to the next multiple of the FEC word length of 240 bits and 2480 bits for header and payload respectively
Padding length must be calculated with respect to the word lengths of the line coding schemes
…

## Slide 23: FEC padding lengths
Padding lengths for FEC block length fitting for 8b10b vs 64b67b vs No Line Coding
…

## Slide 24: Implementation in the PM-PHY
…
64b67b : Replace 8b10b with 64b67b in LC blocks
No LC : Do not apply line coding in LC blocks
PMA layer of PM-PHY Tx

## Slide 25: Scrambler initialization
Initialize all 2^Na LSFRs
    with the augmentation values [0 … 0 0], [0 … 0 1] … [1 … 1 1]
    at first bit of all (<=N-bit) data blocks

## Slide 26: Scrambler implementation
…