## Slide 1
Project: P802.15 Working Group for Wireless Specialty Networks
Submission Title: 15.6a, 15.4ab, 15.14 UWB Harmonization
Date Submitted: September 16th, 2021
Source: Marco Hernandez1, Ryuji Kohno1,2, Takumi Kobayashi1,2, Minsoo Kim1
Company: 1Yokosuka Research Park International Alliance Institute (YRP-IAI), Japan; 2Yokohama National University (YNU), Japan
Address: 1YRP 1, 3-4 Hikarino-oka, Yokosuka, 239-0847, Japan; 279-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan
Voice: 2+81 90-5408-0611, Fax: 2+81-45-383-5528 E-Mail:[Marco.Hernandez@ieee.org; kohno@ynu.ac.jp; kohno@yrp-iai.jp]]
Abstract: The presentation presents material for harmonization discussions of UWB technologies across UWB-based IEEE 802.15 Stds, ETSI Smart BAN, and current UWB-based P802.15 Study Groups.
Purpose: Material for discussion in P802.15.6a.
Notice: This document has been prepared to assist P802.15.6a. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.6a.

## Slide 2: 15.6a case
SG 15.6a targets an amendment to 802.15.6 BAN for dependable medical applications in a human BAN (HBAN) and a vehicle BAN (VBAN).
  The scope of Std 15.6 is not constrained to humans.
The anchor point of the design is when an HBAN and VBAN operate close to each other, sharing the same wireless channel and environment.
  A person with a BAN in a vehicle or nearby a vehicle
  Coordinators may interact for interference management, reduce collisions, increase overall performance.
  Obviously, HBAN and VBAN can work separately.

## Slide 3
BAN
VBAN
15.6a use case

## Slide 4: 15.6a case
One 15.6a system, 2 collocated use cases: HBAN, VBAN.
As mentioned, 15.6a targets the case when an HBAN coordinator interacts with another VBAN coordinator.
  An example use case is about a senior car driver, monitoring health (HBAN) and safety for preventing car incidents (VBAN).
  When an HBAN and a VBAN operate in proximity, we can control how they operate for coexistence; interference mitigation, collision control, etc. as they are part of the same 15.6a design (details are TBD).
  Of course, they can operate separately as well.

## Slide 5: 15.6a UWB use case
  Vehicles are already heavily networked, supporting Wi-Fi, Bluetooth, Cellular, Satellite, ITS.
  To avoid interference and alleviate congestion, 15.6a targets UWB systems.

## Slide 6: 15.6a PHY
15.6a aims amendments to the UWB PHY and MAC of IEEE Std 802.15.6.
UWB PHY enhancements are for interference mitigation mechanisms, higher throughput, ranging, and positioning.
  While maintaining operation under a predetermine throughput measured at MAC SAP, impacting PER, etc., (TBD).
  Hence, 15.6a shares common goals with 15.4ab and 15.14.
  Room for proposals: pulse shaping, pilot symbols, coded modulation, novel transceiver architectures, interference mitigation techniques combining PHY and MAC operation.

## Slide 7: 15.6a MAC
The Std 15.6 MAC is different from the 15.4 MAC
  At the time 15.6 had to harmonize several MAC proposals into one.
15.6a MAC enhancements are for higher QoS while simplifying the MAC mechanisms.
  Hybrid approach: some use cases may operate in a relatively isolated environment (hospitals, cars), where contention free access may support acceptable performance.
  Interference mitigation techniques for better coexistence & QoS.
  Star topology, but supporting peer-to-peer topologies.
  Interconnection to AP to support TSN domains (802.1).
  We don’t expect to harmonize the MAC with 15.4ab and 15.14, but let’s see.

## Slide 8
15.6a | 15.4ab | 15.14 | 15.4-2020, 15.8, ETSI Smart BAN
Use case: HBAN and VBAN | Numerous use cases | 15.4 IR-UWB use cases | IR-UWB use cases, Multiband-OFDM?
PHY and MAC joint optimization for higher dependability | 15.4 PHY & MAC enhancements | Legacy devices | Legacy devices
PHY enhancements: interference mitigation, higher throughput, etc. | PHY enhancements: interference mitigation, higher throughput, etc. | Coexistence | Coexistence
Comparative table

## Slide 9: Harmonization
The next step would be to discuss technical requirements commonalities for a novel UWB PHY proposal, hopefully across SGs (TGs) while coexisting with other UWB-based Stds. .
  Kind of a common (as much as possible) UWB PHY between 15.4ab and 15.6a and legacy to 15.14.