## Slide 1
NOTE: Update all red fields replacing with your information; they are required. This is a manual update in appropriate
fields. All Blue fields are informational and are to be deleted. Black stays. After updating delete this box/paragraph.
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: New MIMO Channel Estimation Sequences for the PM-PHY
Date Submitted: 15.07.2021
Source: Jonathan Schostak, Lennert Bober, Volker Jungnickel Fraunhofer HHI
Address Einsteinufer 37, 10587 Berlin, Germany
Voice: +49 30 31002-302, FAX: / E-Mail: kai.lennert.bober@hhi.fraunhofer.de
Re: [If this is a proposed revision, cite the original document.]
[If this is a response to a Call for Contributions, cite the name and date of the Call for Contributions to which this document responds, as well as the relevant item number in the Call for Contributions.]
[Note: Contributions that are not responsive to this section of the template, and contributions which do
not address the topic under which they are submitted, may be refused or consigned to the “General Contributions” area.]
Abstract: This document presents a proposal for a new type of sequence to be used as MIMO Pilot Symbols for the PM-PHY.
Purpose: [Description of what the author wants P802.15 to do with the information in the document.]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Text hinzufügen

## Slide 2
Background: MIMO/MISO in the PM-PHY
Parallel Transmission of multiple PPDUs
Concurrent Transmission of MIMO Pilot Sequences
Used to get a MIMO-Channel Estimation for
  MIMO Transmission
  Fine-Synchronization of the transmitters
Sequences currently defined in Clause 9.2.4.2
Potential to improve performance / efficiency

## Slide 3
Channel Estimation Example
Original Channel Impulse Response
Estimated Channel Impulse Response
Relevant Cut-Out

## Slide 4
Sequence Requirements
Alphabet:
  PM-PHY uses PAM-2 => Only +1 and -1 allowed
Balance:
  OFEs are AC-coupled
  Sequences must be balanced to prevent baseline wandering
Implementability:
  Generatable sequences are preferred (e.g. using LFSRs)
Basics

## Slide 5
Sequence Requirements
Length & Set Size
Shorter Sequences: Lower resistance to interference & noise
Longer Sequences: More overhead, no benefit
PM-PHY uses a Cyclic Prefix (CP)
It makes sense to utilize the CP block sizes
  N = 64, 128, 256, 512, 1024
Set Size = Number of different available sequences
Bigger Set Size => More concurrent estimations
Minimum Set Size of 8 => Up to 56 transmitters

## Slide 6
Sequence Requirements
Orthogonality and Correlation Properties
Concurrently transmitted sequences interfere…
  …with each other (Crosscorrelation, CCF)
  …with themselves (Autocorrelation, ACF)
Perfect ACF and CCF => Perfect impulse response recovery through correlation
=> Sequences should have low ACF and CCF values
=> If possible, they should be orthogonal (CCF[0]=0)

## Slide 7
Sequence Candidates
Summary

## Slide 8
Sequence Candidates
Variable Sampling Factor (VSF) Sequences
Inspired by OVSF-Sequences [1]
Use expanded Gold Sequences for the shortest stage
Combine the Sequences to make the longer counterparts using presented scheme
Special:
  Lower sample rate can be used at receiver
  Orthogonality is maintained between "stages"
[1] “3GPP TS 25.213, v16.0.0, Spreading and modulation (FDD),” Tech. Rep., 2020.

## Slide 9
Sequence Candidates
Variable Sampling Factor Sequences
Orthogonality: 𝑎(𝑛)∙𝑏(𝑛) = Σ𝑎𝑖∙𝑏𝑖 = 0
Required orthogonalities: sA and sE, sC and sG, sB and sF, as well as sD and sH
Then also orthogonal:
  sAC and sEG as well as sBD and sFH
  sABCD and sEFGH
With ideal subsampling in synchronous transmission, orthogonality is maintained
Principle can be adapted to lengths and set sizes required for the PM-PHY

## Slide 10
Results
Asynchronous Scenario
Virtually no differences between the non-Repetitive Sequences
(Repeated) Sequence currently in the standard draft does not perform well

## Slide 11
Results
Synchronous Scenario
Small differences now Visible
However, seems to be highly scenario-dependent

## Slide 12
Results
VSF Evaluation & Performance
Sequences transmitted at 200 MHz in all simulations

## Slide 13
Discussion
Why do repeated sequences perform worse?
The base sequence to be repeated is shorter than the CP
This leads to a repetition of the impulse response
Which peak is the „correct“ one? => Channel Delay cannot be determined.

## Slide 14
Conclusions
Sequence correlation properties are not as relevant at the examined lengths as anticipated
The VSF-Sequences have an Additional Feature (Variable Clockrate at Receiver)
  Therefore recommended for IEEE 802.15.13 Standard PM-PHY
See working text in doc. 15-21/0447r0

## Slide 15
Appendix

## Slide 16
Evaluation Framework
Simulation Pipeline

## Slide 17
Evaluation Framework
Optical Channel Simulation
Model from 802.11bb standardization [2]
D15 was mainly used as a test point
[2] M. Uysal, F. Miramirkhani, and T. Baykas, “IEEE 802.11bb Reference Channel Models
for Indoor Environments,” Tech. Rep., 2018. [Online]. Available:
http://csndsp2018.com/Viewproject

## Slide 18
Evaluation Framework
Optical Channel Simulation
Impulse Response of Luminaire #2
Peak Values of all Channel Impulse Responses to D15
Impulse Response of Luminaire #5

## Slide 19
Evaluation Metrics
Number of Identifiable Transmitters
  Important to test the delay measurement accuracy
  Transmitter is counted as identified when
Relative Mean Squared Error (RMSE)
  Relation of overall error energy to overall impulse response energy
: Delay Estimation Error
: PAM-2 Symbol Duration