## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Ranging QoS]
Date Submitted: [12 November, 2021]
Source: [Frank Leong, Wolfgang Küchler, Riku Pirhonen] Company [NXP Semiconductors]
Re: [Input to the Working Group]
Abstract: [Presentation, UWB in 802.15, ranging]
Purpose: []
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | High data rates, preamble modification
Interference mitigation techniques to support higher density and higher traffic use cases | High data rates, preamble modification
Other coexistence improvement | Lower data rates for control and report messages
Backward compatibility with enhanced ranging capable devices (ERDEVs) | Highly similar modulation structure
Improved link budget and/or reduced air-time | Lower data rates for control and report messages, higher data rates for reduced air-time
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | Outlining key aspects of PHY assisting UWB
Hybrid operation with narrowband signaling to assist UWB | Outlining key aspects of PHY assisting UWB
Enhanced native discovery and connection setup mechanisms | Outlining key aspects of PHY assisting UWB
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | High data rates
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | High data rates
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Ranging QoS

## Slide 4: 802.15.4ab – Context Recap
Focus on key functionalities to be provided by UWB:
  Ranging with high integrity (handsfree access use cases)
  Localization (indoor navigation use cases)
  Sensing (presence detection use cases)
  Coordination & scheduling to support the above
Provide accurate ranging via a low-cost, mass-market solution
  Low energy-per-ranging
  Low channel-occupancy-per-ranging a.k.a. spectral efficiency (many devices operating at the same time & place)
  Re-use of hardware between use cases

## Slide 5: UWB Ranging – Improving QoS (802.15.4z HRP UWB as Baseline)
Lower data rate option for link budget benefit
  Improves resilience to dispersion/fading, interference
Higher data rate option for reduced airtime
Preamble options for enhanced channel capacity
Wake-up (WUP) PHY
  Reduced system cost (RF components, energy consumption)
  Low latency
QoS improvements on Ranging will typically also (partially) carry over to Localization and Sensing

## Slide 6: Balancing Preamble and Data
Refer to 1.7 Mbit/s proposal from TG4z, see: https://mentor.ieee.org/802.15/dcn/20/15-20-0037-00-004z-hrp-lower-rate-data-format.pptx
Balance between preamble and data improves resilience to fading, and also to interference
Benefit to protocols in which UWB is used for status and timestamp signaling (e.g., Gen1 Digital Key protocols)
Recommendation: PHR rate scaling as in 802.15.4z HPRF (linked to FEC)
Mitigation of long scrambler run-in sequences could be useful (lowering Peak EIRP), if a low-complexity method can be devised

## Slide 7: Reducing Air-Time (I)
Higher data rates provide a means to reduce air-time
  Beneficial in short-range scenarios (e.g., contactless payment at a terminal)
  Performance related to properties of the wireless channel (RMS delay spread)
Find a balance between data transfer capability and implementation complexity
  Propose Burst-Level QPSK (BQPSK*)
  Consider channel estimation, equalization, FEC choice
*: BQPSK is essentially a form of QPSK; for relative comparison to other common schemes, see: https://www.gaussianwaves.com/2010/04/performance-comparison-of-digital-modulation-techniques-2/

## Slide 8: Reducing Air-Time (II)
8 pulses spread 2x, BPSK scrambled, burst BPSK modulated
guard interval (16 chips)
8 pulses spread 2x, BPSK scrambled, burst BPSK modulated
guard interval (16 chips)
1 symbol (64 chips)
BPSK Acc. HPRF
16 pulses spread 2x, BPSK scrambled, burst QPSK modulated
guard interval (32 chips)
1 symbol (64 chips)
Burst-Level QPSK (BQPSK) Equivalent
Same data rate, but 2x longer guard interval
8 pulses spread 2x, BPSK scrambled, burst QPSK modulated
guard interval (16 chips)
1 symbol (32 chips)
Higher Rate BQPSK
2x higher data rate, but same guard interval

## Slide 9: Reducing Air-Time (III)
BQPSK has 2x longer guard interval vs. BPSK for same data rate
  Better performance in dense multipath environments
  Strong benefit for low-complexity EQ schemes
BQPSK is scalable; feasibility of a specific data rate depends on UWB wireless channel properties (RMS delay spread)
  Channel sounding typically results in a delay distribution as pictured (example for LOS @ 2 m spacing in a clutter-rich indoor environment)
  RMS delay spread scales w/ distance: e.g., ~18 ns for 2 m, ~4 ns for 0.1 m (TYP across various locations in clutter-rich indoor environment)

## Slide 10: Reducing Air-Time (IV)
RMS delay spread of ~10 ns expected in short-range scenarios (both LOS and NLOS, both CH5 and CH9)
Correspondingly, BQPSK up to ~50 Mbit/s would be feasible
  54.4 Mbit/s with CCK=3+RS rate 1/2 FEC
  62.4 Mbit/s with CCK=7 rate 1/2 FEC (higher w/ puncturing*)
Delay spread in the UWB wireless channel will limit the applicability of higher BQPSK data rates
*: See: D. Haccoun and G. Begin, “High-rate punctured convolutional codes for Viterbi and sequential decoding,” IEEE Transactions on Communications, vol. 37, no. 11, pp. 1113-1125, Nov. 1989. Note that memory M in this paper is defined such that M=6 translates to K=7.

## Slide 11: Preamble Options (I)
Proposing PRFDMA (Pulse Repetition Frequency Domain Multiple Access) as means to balance UWB multi-user performance vs. hardware cost
Beneficial in dense multi-user scenarios, for example:
  Indoor Navigation (e.g., shopping mall) with a peak density of ~5 persons/m2 within a ~100 m radius
  Digital Key in a parking lot after large event, >10k parking spots within a radius of ~1 km at a peak density of ~0.1 vehicles/m2

## Slide 12: Preamble Options (II)
Subnet separation via preambles is desirable
  Mitigates receiver “blind time” when acquiring undesired signal
  Already part of HRP UWB (both BPRF and HPRF)
  Further enhancements proposed, see: https://mentor.ieee.org/802.15/dcn/21/15-21-0377-02-04ab-preamble-codes-for-data-communications.pptx
PRFDMA provides cross-correlation performance within ~1dB of proposed length-2047 m-sequences
  PRFDMA does not require major modem modifications, no increase in hardware complexity/cost
  Depending on parameter choice, PRFDMA provides ~50 subnets
  Probably makes most sense as an HPRF enhancement
  Several specific code-to-PRF assignment designs possible, either based on length-91 Ipatov sequences or length-127 m-sequences

## Slide 13: Preamble Options (III)
Proposal:
Specify chip rate clock tuning range of ±2% in 800 ppm steps
  This combination of range and step size provides 51 subnets
  Carrier frequency remains untouched
  Both chip rate and carrier clocks derived from same reference (i.e., no change compared to 15.4z)
Transmit the entire packet with the specified chip rate clock
  Avoid variable chip rate clock frequency within the packet
Support pulse shaping with a multiple of the chip rate clock (avoid re-shaping for each chip rate clock frequency)
  Accommodate the full chip rate clock frequency range in transmit masks (both time and frequency domain)

## Slide 14: WUP PHY
Additional PHY to serve as Wake-Up (WUP)
Low energy consumption, both in Scanning and Advertising mode
Sufficient link budget – not bottlenecking overall UWB application
  Tightly coupled to UWB (timing and channel properties)
  Consider interference scenarios & coexistence features
Focus on low cost
  Antenna & filter sharing
  Avoid high complexity