## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: [Beacon and Ranging Frames to Support Downlink TDOA (DL-TDOA) Location Service in 802.15]
Date Submitted: [16 November 2021]
Source: [Yongsen Ma and Zhenzhen Ye] Company [Red Point Positioning]
Re: Call for contributions to SG15.4ab
Abstract: Presentation, UWB in 802.15, DL-TDOA
Purpose: Present technical content for consideration by the group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | The proposed method for DL-TDOA scheduling is used to reduce interference between participating anchors. DL-TDOA supports a high density of tags without increasing interference potential.
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | The proposed MAC enhancements are compatible with legacy ERDEVs; All required information is conveyed using IEs in existing MAC frame formats harmlessly ignored by non-participating legacy devices.
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | The new feature will provide enhanced reliability in some high density use cases.
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | The proposed superframe structure, transmission scheme and messages are to support downlink TDOA location service.
Infrastructure synchronization mechanisms | 

## Slide 3: Beacon and Ranging Frames to Support Downlink TDOA (DL-TDOA) Location Service in 802.15

## Slide 4: Recap: Superframe Structure to Support DL-TDOA [1]
Three main periods in a superframe: Beacon only period (BOP), contention-free period (CFP), contention access period (CAP)
Similar superframe structure in 802.15.4/4z includes TVWS multichannel cluster tree PAN and RCCN. However, to support a generic DL-TDOA location service, we’d like to propose a superframe structure like following
  BOP: slot based, as a scheduled access period, for network identification, superframe configuration, frame synchronization, etc.
  CFP: slot based, as a scheduled access period, for anchors transmitting messages to provide DL-TDOA location service
  CAP: contention access period for supporting other ranging/communication modes (e.g., TWR, UL-TDOA, data communication, etc.)
BOP
CFP (for DL-TDOA)
CAP
[1] Zhenzhen Ye. Downlink TDOA (DL-TDOA) Location Service in 802.15. 15-21-0399-00-04ab

## Slide 5: Recap: Superframe Structure to Support DL-TDOA (Cont’d) [1]
Ranging block structure from 802.15.4/4z for DL-TDOA period
The inter-anchor communication during DL-TDOA procedure is similar to Two-Way Ranging (TWR)
CFP (for DL-TDOA)
A
B
M
REQ
REQ
RSP
RSP
Ranging block = DL-TDOA period
Ranging round = the period of an anchor pair
Ranging slot = the period of transmitting a REQ or RSP frame
[1] Zhenzhen Ye. Downlink TDOA (DL-TDOA) Location Service in 802.15. 15-21-0399-00-04ab

## Slide 6: Recap: Beacon Frames and IEs to Support DL-TDOA [1]
Using Enhanced Beacon Frame Format with IEs to convey superframe structure and provide control information (broadcast)
No unstructured MAC payload
HIE contains DL-TDOA PAN descriptor
PIE contains information such as beacon commands (BCMDs), routing information, and other information that may be needed.
Octets: 2 | 0/1 | 4/8/10 | Variable |  | 0 | 4
Frame Control | BSN | Addressing | IE Lists |  | MAC Payload | FCS
 |  | PAN ID and Source Address | HIE | PIE | No unstructured payload | CRC-32
 |  |  | DL-TDOA PAN descriptor | BCMD, Routing info, etc. |  | 
MHR |  |  |  | MAC Payload |  | MFR
[1] Zhenzhen Ye. Downlink TDOA (DL-TDOA) Location Service in 802.15. 15-21-0399-00-04ab

## Slide 7: Outline
Beacon Frames and IEs
  Header IE: DL-TDOA PAN Descriptor
    Frame Synchronization Specification
    Superframe Specification
  Payload IE: Beacon Commands
    Beacon Slot Request/Response/Confirm
    Pending Packet Notification
    Routing Information Example
Ranging Frames and IEs
  Header IE: Node ID Information
  Payload IE: Ranging block/round index, TX timestamp, node location, RX-to-TX reply time, ToF, CFO, etc.
  Message Examples: REQ/RSP for Anchor Pair and SS-TWR Type

## Slide 8: DL-TDOA PAN Descriptor IE
Superframe duration & slot unit duration
Beacon slot duration & number of beacon slots
DL-TDOA slot duration & number of DL-TDOA slots
CAP duration
Inactive period duration (if any)
Frame synchronization related information, e.g., Time offset from the SF start, SYNC hop, etc.
Octets: 1/7 | 2/12 | TBD | TBD
Frame Synchronization Specification | Superframe Specification | Others (e.g., STS config.) | Reserved
In-Band/Out-Of-Band Control | Superframe Time Offset Unit | Superframe Time Offset | Sync Hop
In-Band/Out-Of-Band Control | Base Superframe Slot Duration |  | Number of Superframe Slots | Number of BOP Slots | Number of DL-TDOA Slots | Number of CAP Slots

## Slide 9: DL-TDOA PAN Descriptor IE: Frame Synchronization Specification
In-band/out-of-band control: To indicate whether following fields are sent through in-band (0b01, default), out-of-band (0b10), e.g., narrowband channels, or both (0b11). Time sync between in-band and out-of-band is out of scope of this presentation.
Superframe Time Offset Unit:
  0 – Ranging Scheduling Time Unit (RSTU), default
  1 – Ranging Counter Time Unit (RCTU)
Reserved: reserved for other purposes and/or future use.
Superframe Time Offset: unsigned integer, time offset in RSTU from start of a superframe.
Sync Hop: unsigned integer, number of hops from the first sync node (or Super PAN Coordinator). If Sync Hop is 0, this node is the first sync node.
Octets: 1 |  |  | 0/4 | 0/1 | 0/1
Bits: 0-1 | 2 | 3-7 |  |  | 
In-Band/Out-Of-Band Control | Superframe Time Offset Unit | Reserved | Superframe Time Offset | Sync Hop | Reserved
Frame Synchronization Specification Control

## Slide 10: DL-TDOA PAN Descriptor IE: Superframe Specification
In-band/out-of-band control: To indicate whether following fields are sent through in-band (0b01, default), out-of-band (0b10), e.g., BLE and narrowband channels, or both (0b11).
Base Superframe Slot Duration in unit of M*RSTU. . Default is 600*1*RSTU=0.5 ms. M: TBD, or in other forms of RSTU.
Reserved: reserved for other purposes and/or future use.
Number of Superframe Slots in : unsigned integer
Number of Beacon Only Period Slots in : unsigned integer. Devices can do frame synchronization and clock adjustment at the end of BOP.
Number of DL-TDOA Period Slots in : unsigned integer
Number of CAP Slots in : unsigned integer. CAP can be slotted or not slotted.
Remaining of the superframe, if present, is for an inactive period.
Octets: 2 |  |  | 0/3 | 0/2 | 0/2 | 0/2 | 0/1
Bits: 0-1 | 2-x | (x+1)-15 |  |  |  |  | 
In-Band/Out-Of-Band Control | Base Superframe Slot Duration | Reserved | Number of Superframe Slots | Number of BOP Slots | Number of DL-TDOA Slots | Number of CAP Slots | Reserved
Superframe Specification Control

## Slide 11: Beacon Frames and IEs to Support DL-TDOA (Cont’d)
Beacon Command (BCMD) IE
  Payload IE
    Possibility to be secured
  Used for beacon allocation requests and responses, including
    Request, response, confirmation, exchange of control information.
    Command parameter specific to a command.
  Information used to maintain coordination

## Slide 12: Beacon Command Payload IE
The Beacon Command (BCMD) IE contains a list of BCMD elements used to manage beacon slots.
The BCMD list is formatted as:
Octets: 1 |  | 0-255
Bits: 0-3 | 4-7 | 
BCMD ID | BCMD Data Length | BCMD Command Data
DL-TDOA BCMD IE: List of BCMD Elements
Octets: variable | … | Octets: variable | … | Octets: variable
BCMD element 1 | … | BCMD element x | … | BCMD element N
MHR | MAC Payload IE (PIE) | MFR

## Slide 13: Beacon Command Payload IE (Cont’d)
Octets: 1 |  | 0-255
Bits: 0-3 | 4-7 | 
BCMD ID | BCMD Data Length | BCMD Command Data
Value | Description
0 | Beacon Slot Request
1 | Beacon Slot Response
2 | Beacon Slot Confirm
3 | Pending Packet Notification
4-15 | Reserved
Octets: 2/8
Node ID
Octets: 2/8 | 1
Node ID | Slot Index
Octets: 2/8 | 1
Node ID | Slot Index
dataLen=2/8
dataLen=3/9
dataLen=3/9
The Node ID field is present when BCMD ID is set to 0/1/2 (Request/Response/ Confirm). The Node ID value is the ID assigned to the DL-TDOA anchor.
The Slot Index field is present when BCMD ID is set to 1/2 (Response/Confirm). The value is the beacon slot assigned in response to the beacon request.
Pending Packet Notification: there is(are) pending packet(s), e.g., request for ranging report, over-the-air update, etc., for the destination node.
…
…
Octets: 2/8
Destination Node ID
dataLen=2/8

## Slide 14: Routing Information Example
Option 1: Routing is L2 information to be standardized
  Routing Rank: always present. Indicates the routing level (rank) in the routing graph. Unsigned integer. Range is 1 to TBD.
  Subnetwork ID: ID of the subnetwork to run the routing protocol in. When IE content length field is set to 2, field length is 1 octet. When IE content length is set to 3 or 5, field length is 2 octets. Value is an unsigned integer.
  Node ID: Present when IE content length is 5. Not present when IE content length is less than 5.
Option 2: Routing is proprietary. Use Vendor Specific IE.
Option 3: Routing is standard IP layer (e.g., RPL): use MPX IE [2] with assigned protocol ID for routing protocol. Carried as unencapsulated IP or 6loWPAN.
Octets: 1 | 1/2 | 0/2
Routing Rank | Subnetwork ID | Node ID
Octets: 3 | 1 | 1/2 | 0/2
Vendor OUI | Routing Rank | Subnetwork ID | Node ID
[2] Multiplexed (MPX) Data Service. IEEE Std 802.15.9-D6 Clause 7

## Slide 15: Ranging Frames and IEs to Support DL-TDOA
Ranging frames are transmitted between anchors in the DL-TDOA period.
Tags can overhear the ranging frames to calculate TDOA values and positions.
For anchors, the transmission procedure of the ranging frames is similar as two-way ranging with additional information.
  Two-way ranging could be single-sided with two messages, REQ and RSP, or double-sided with the third FINAL message.
  Two-way ranging could be between a pair of two anchors or a cluster of anchors.
  New header/payload IEs should be defined for the control of two-way ranging and the exchange of additional information such as anchor location, reply time, etc.
A
B
M
REQ
REQ
RSP
RSP
FINAL
FINAL
A
B
M
X
…
Anchor pair
Anchor cluster

## Slide 16: Ranging Frames and IEs to Support DL-TDOA – Header and Payload IEs
Ranging frames can be data frames (example below) or multi-purpose frames.
Header IEs (used by MAC to process the frame, e.g., security, addressing, etc.)
  Node ID information
Payload IEs (destined for another layer or SAP, as part of MAC payload)
  Ranging block and ranging round information
  TX timestamp, reply time (RX-to-TX turnaround time)
  Time synchronization information (e.g., clock frequency offset)
  Time of flight correction information
  Node location information
Octets: 2 | 0/1 | variable | variable | variable |  | variable | 2/4
Frame Control | Sequence Number | Addressing Fields | Auxiliary Security Header | IEs |  | Data Payload | FCS
 |  | PAN ID and Source Address |  | Header IEs | Payload IEs |  | 
 |  |  |  | Node ID(s), etc. | Ranging block/round index, TX timestamp, node location, reply time, ToF, CFO, etc. |  | 
MHR |  |  |  |  | MAC Payload |  | MFR

## Slide 17: Ranging Frames and IEs to Support DL-TDOA – Header IE
Octets: 2 |  |  |  |  |  | 0/2/8 | [2/8]*N
Bits: 0-1 | 2-3 | 4 | 5 | 6-13 | 14-15 |  | 
Ranging Control | Ranging Message Type | Src Node ID Present | Node ID Format | Number of Dst Node IDs | Reserved | Src Node ID | Dst Node ID List
Ranging type of this ranging block/round:
00: OWR
01: SS-TWR
10: DS-TWR
11: Reserved
Message type of this packet:
00: REQ
01: RSP
10: FINAL
11: Reserved
0: 2 octets (short)
1: 8 octets (extended)
List of short/extended IDs for destination nodes. This could be used in corresponding to lists of other information in payload IE.

## Slide 18: Ranging Frames and IEs to Support DL-TDOA – Payload IE
Octets: 2 | 2 | 4/8 | 0/12/24 | 0/2 | [1]*[0/N] | [4/8]*[0/N] | [4/8]*[0/N]
Bits: |  |  |  |  |  |  | 
Ranging Block Index | Ranging Round Index | TX Timestamp | Node Location | CFO | Dst Ranging Slot Index List | Reply Time List | ToF List
Octets: 2 |  |  |  |  |  |  |  |  |  | 
Bits: 0 | 1 | 2-3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11-15
TX Timestamp Format | Node Location Present | Node Location Type | Node Location Format | CFO Present | Dst Ranging Slot Index Present | Reply Time Present | Reply Time Format | ToF Present | ToF Format | Reserved
Payload IE Control
Payload IE Content
Should be in corresponding to Dst Node ID List in header IE
Ranging slot assigned to each destination node
Reply time, or turnaround time, for RSP or FINAL messages
ToF between certain initiator-responder pair(s)
Or in Ranging Round (RR) IE
0: 4 octets
1: 8 octets
0: 12 octets
1: 24 octets
0: 4 octets
1: 8 octets
0: 4 octets
1: 8 octets
00: absolute
01: relative
10-11: reserved
Clock Frequency Offset Compensation

## Slide 19: Ranging Frames and IEs to Support DL-TDOA – REQ Example (SS-TWR Type)
Octets: 2 |  |  |  |  |  | 2 | 2
Bits: 0-1 | 2-3 | 4 | 5 | 6-13 | 14-15 |  | 
Ranging Control | Ranging Message Type | Src Node ID Present | Node ID Format | Number of Dst Node IDs | Reserved | Src Node ID | Dst Node ID List
01 | 00 | 1 | 0 | 0x01 | 00 | 0x000a | 0x000b
Octets: 2 | 2 | 8 | 12 | 0 | 0 | 0 | 0
Bits: |  |  |  |  |  |  | 
Ranging Block Index | Ranging Round Index | TX Timestamp | Node Location | CFO | Dst Ranging Slot Index List | Reply Time List | ToF List
0x0001 | 0x0001 | t0 | x0, y0, z0 |  |  |  | 
Octets: 2 |  |  |  |  |  |  |  |  |  | 
Bits: 0 | 1 | 2-3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11-15
TX Timestamp Format | Node Location Present | Node Location Type | Node Location Format | CFO Present | Dst Ranging Slot Index Present | Reply Time Present | Reply Time Format | ToF Present | ToF Format | Reserved
1 | 1 | 01 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 00000
Payload IE Content
Payload IE Control
Header IE

## Slide 20: Ranging Frames and IEs to Support DL-TDOA – RSP Example (SS-TWR Type)
Octets: 2 |  |  |  |  |  | 2 | 2
Bits: 0-1 | 2-3 | 4 | 5 | 6-13 | 14-15 |  | 
Ranging Control | Ranging Message Type | Src Node ID Present | Node ID Format | Number of Dst Node IDs | Reserved | Src Node ID | Dst Node ID List
01 | 01 | 1 | 0 | 0x01 | 00 | 0x000b | 0x000a
Octets: 2 | 2 | 8 | 12 | 0 | 0 | 4 | 0
Bits: |  |  |  |  |  |  | 
Ranging Block Index | Ranging Round Index | TX Timestamp | Node Location | CFO | Dst Ranging Slot Index List | Reply Time List | ToF List
0x0001 | 0x0001 | t1 | x1, y1, z1 |  |  | t_reply | 
Octets: 2 |  |  |  |  |  |  |  |  |  | 
Bits: 0 | 1 | 2-3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11-15
TX Timestamp Format | Node Location Present | Node Location Type | Node Location Format | CFO Present | Dst Ranging Slot Index Present | Reply Time Present | Reply Time Format | ToF Present | ToF Format | Reserved
1 | 1 | 01 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 00000
Payload IE Content
Payload IE Control
Header IE

## Slide 21: Questions?