## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: 802.15 Presentation @ 802.1 Dec. 2nd, 2021 Technical Plenary
Date Submitted: December 1, 2021
Source: Clint Powell (Meta), Ben Rolfe (Blind Creek Associates)
Contact: SAA
E-Mail: cpowell@ieee.org, ben@blindcreek.com
Voice: +1 480 586-8457
Re: 802.15/802.1 Joint Topics
Abstract: Presentation slides for 802.1 Mtg.
Purpose: Collaboration on 802.15/802.1 Joint Topics
Notice: This document has been prepared to assist the IEEE 802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by 802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2: Prior Mtgs./Discussion Summary
Have had joint meetings in the past
  Differences between bridging and routing at L2
  Have learned some things
  Haven’t addressed specific issues and barriers head on
Have an established “status quo”
  Example: 802.15.4 is “different”, widely used - expanding in use rapidly
  Mutual tolerance has worked OK so far
There may be value in 802.1 over 802.15 standards
  Some TGs currently working on supporting parts of 802.1
  Need deeper understanding

## Slide 3: Mutual Beneficial Desire
To align 802.1 with the needs of wireless everything else and leverage the full value of 802.1 in billions of 802.15 standard based devices
  There are many question to be answered from both sides
  This is not going to be “one and done” – there is some work!
  Will need to partition, prioritize, and sequence

## Slide 4: Main Starting Points
What is WSN?
  More than one standard with unique MACs each with multiple PHYs
  Several standards support 48-bit addressing
  Adding 48-bit support where missing is possible but does it really matter?
Bridging and barriers beyond addressing
  Timing, data volumes, energy consumption
  Performance assumptions built into 802.1
  Network topology and characteristics assumed
Other 802.1 Features
  What should be of interest (usefulness) to 802.15 adopters?
  What are the barriers to applying 802.1 to the uncertain world of wireless?

## Slide 5: Thumbnail of WSN Standards
There is a lot more to 802.15 than 802.15.4 and some assumptions we’ve heard seem incorrect
  Not all 802.15 standards use 64-bit addressing
    802.15.3, 802.15.6, and 802.15.13 use 48-bit addressing
  Frame length is not always limited to 127 octets
    802.15.3 supports from large packets to very large packets (up to 2,099,200 octets): >= 802.11 and min. Ethernet MTU for all PHYs
    802.15.4 supports big (up to 4k octets) on some commonly implemented PHYs
    802.15.6 at ~250 octets but under revision and likely to support at least 1k octets
    802.15.7a 1023 and 65535 octet maximum frame sizes
    802.15.13 supports 2047 octet maximum frame size
  Data rates covered range from very low to really freakin' fast (RFF)
    802.15.3 THz at 100 Gb/s and next gen THz approaching PLAID (plaid comes after ludicrous speed)
    802.15.4 ranges from < 1.2 kb/s to 30 Mb/s

## Slide 6: The 802.15.4 Legacy
There are a lot of legacy 802.15.4 devices in the world
Early revisions support very limited extensibility [Version 0 and 1 frames]
  127 octet max frame size (up to 102 octet payload)
  No protocol discrimination mechanism
  No means to add protocol discrimination in a standardized way
  Assume we can’t change the past or those using only 2006 revision capabilities
Later revisions of the standard add extensible, flexible MAC frame (802.15.4e-2012) [Version 2 frames]
  Protocol differentiation added via payload encapsulation
  Readily extensible w/backward compatibility
Popular post-2006 PHYs added support larger frame sizes
  But at lower data rates may not be useful (interference limited)

## Slide 7: More to Bridging
48-bit addressing isn’t the only barrier?
  Could add support for 48-bit addressing in 802.15.4 but benefit is unclear
    We've been told there are timing and link reliability assumptions
    Wireless in shared spectrum is not guaranteed to any level of reliability
    Can a slow link with no such thing as “guaranteed” be made to bridge?
    Other issues bridging over wireless?
  Handling different frame sizes from one medium to another?
    How does data rate and frame size affect the ability to use 802.1 features
  If bridging as defined by 802.1 is out of reach, there are bridging-like concepts that could be useful
    What exactly determines the constraints on bridging? This must have been encountered before (802.11 is 4k octets which is different from Ethernet)
    The minimum MTU size for Ethernet is understood to be under 2k octets. What is the maximum frame size defined for Ethernet?

## Slide 8: More to Bridging (cont’d.)
  There are now multiple different sorts of addresses that are supported by various 802 standards, what with MAC address randomization and such, even of common length, so...
  If the address is not unique, is it still bridgeable?
  If the address is not constant (static), is it still bridgeable?

## Slide 9: Other 802.1 Features
Unlike cellular or 802.11, 802.15 in many cases does not have a gateway to a backhaul
  802.15 supports a wide variety of network topologies, from small point-to-point to large mesh and multi-hop
TSN appears attractive to several 802.15 use cases
  Is 802.1 expecting to interconnect between 802.15 family of standards, or through Ethernet to other networks (i.e. 802.15 to 802.11)?
  How does one envision TSN in non-deterministic wireless networks?
  Are there any special considerations w.r.t. interfacing to cellular networks - i.e. smart city and vehicle applications?

## Slide 10: Where do we Start
There are even more questions… but to start:
  What features make sense on a wireless medium?
  What are the barriers to using 802.1 features?
  What are considered “essential to be called 802.1 compliant”?

## Slide 11: What Next
Possible next steps
  Continue joint effort to understand each other
    Continue promoting common understanding
    Replace hearsay and myths with knowledge
    Collect use cases from 802.15, dependent organizations and other stakeholders to determine requirements (application, synchronization, data transfer, etc.)
  IG/SG in 802.1 to explore a project(s):
    To develop solution for 48 / 64 bit addressing
    Including bridging requirements/issues beyond resolving 48 / 64 bit in integrating 802.15.4 into the 802.1 architecture
  IG/SC(s) in 802.15 (interfacing with 802.1) to proactively support this effort with respective WG amendment project(s)
    Extend standard(s) as needed to support 802.1 in the various 802.15 standards (where effort is not currently underway)

## Slide 12: Questions?