## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: UWB Sensing Scenarios for 802.15.4ab
Date Submitted: 20 January 2022
Source: Pooria Pakrooh, Bin Tian, Steve Shellhammer and Koorosh Akhavan (Qualcomm)
E-Mail: {ppakrooh, btian, sshellha, kakhavan}@qti.qualcomm.com
Abstract: In this presentation we provide overview of sensing scenarios, clarify the terminology and define the sensing scenarios. We also provide discussion on which sensing modes to support.
Purpose: Present technical content for consideration by the group
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | Discussing possible UWB sensing scenarios
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Introduction
In this presentation we provide overview of sensing scenarios
Clarify the terminology and define the sensing scenarios
  An effort has been made to use terminology consistent with UWB ranging and 802.11bf RF sensing [1]
  In most RF Sensing scenarios, the Initiator is the device where the RF sensing application resides. The proxy scenario is the exception to this rule. Discussion is needed as to whether the proxy should be supported in 802.15.4ab
  Based on the roles of the initiator/responder in the sensing task, we present possible sensing modes for 802.15.4ab.
Discussion on which sensing modes to support is needed.

## Slide 4: Sensing terminology
Generalizing the terminology from the context of ranging to RF sensing
Term | Definition
Initiator | The sensing device that initiates the RF sensing session with one or more other UWB devices
Responder | The sensing device that responds to the sensing Initiator
Sensing transmitter | The sensing device that sends the channel sounding PPDU to enable channel estimation for RF sensing purposes
Sensing receiver | The sensing device that receives the channel sounding PPDU from the transmitter and performs channel estimation
CIR measurement report for upper layer processing | Internal device channel impulse response report to upper layer for processing
OTA CIR measurement report | Over the air channel impulse response feedback report

## Slide 5: UWB Sensing Scenarios: Mono-Static sensing
  A single UWB device acts as both the sensing transmitter and sensing receiver and runs the RF Sensing application
  No OTA CIR measurement report is required as there is only one UWB device involved.
  The single UWB device is responsible for all the sensing steps, including sensing initiation, processing of the result and generating CIR measurement report for upper layer processing.
  This scenario requires the UWB device so transmit and receiver simultaneously (e.g., Full Duplex operation)
  Full duplex (FD) operation significant challenge of self interference cancellation: Need to investigate complexity and power consumption to check feasibility of FD for 15.4ab
  Since only one device is involved, this can be implementation specific and may not need standard support.
Object being
sensed
UWB Tx/Rx

## Slide 6: UWB Sensing Scenarios: Bi-static Sensing
Mode A [Initiator is the sensing receiver]:
  OTA CIR measurement report is not required
  Initiator measures channel and generates CIR measurement report for upper layer processing
Responder/ Tx
Initiator/Rx
Object being
sensed
Sensing packet

## Slide 7: UWB Sensing Scenarios: Bi-static Sensing
Mode B [Initiator is the sensing transmitter]: OTA CIR measurement report is required
Initiator/ Tx
Responder/Rx
Object being
sensed
Sensing packet
OTA CIR measurement report

## Slide 8: Discussion of bi-static modes
  Mode A does not have feedback overhead, as no OTA CIR measurement report is required.
  Mode A is more power efficient for Responder as it does not require to send feedback and requires less processing to generate the feedback.
  May be easier to enable legacy devices for mode A, no adoption for feedback requirement.
  Assuming channel is reciprocal, mode A is preferred, so it needs to be supported. Support of mode B may be optional.

## Slide 9: UWB Sensing Scenarios: Multi-static sensing
Initiator/Rx
Responder1/Tx
Object being
sensed
Responder2/Tx
    Mode A: Initiator is the receiver. Responders are transmitters: OTA CIR measurement report is not required
  Since 15.4 does not support simultaneous transmission then mode A is basically equivalent
  to performing multiple bi-static sensing instances sequentially with multiple responders.
Sensing packet

## Slide 10: UWB Sensing Scenarios: Multi-static sensing
Responder1/Rx
Object being
sensed
Initiator/Tx
Responder2/Rx
    Mode B: Initiator is the transmitter. Responders are receivers. Multiple OTA CIR measurement reports are required.
  Mode B needs scheduling for OTA CIR measurement reports from multiple responders
  to the initiator.
Sensing packet
OTA CIR measurement report 1
OTA CIR measurement report 2

## Slide 11: UWB Sensing Scenarios: Proxy application
  Proxy enables a device to request the CIR measurement report for sensing while not being initiator or responder.
  Initiator performs sensing with one or more responders.
  Initiator reports the OTA CIR measurement report to the device which requested it.
    Useful in 802.11 where the AP can make all channel measurements and report them to the non-AP client STA.
    Usefulness for 802.15.4ab can be discussed depending on possible use cases.

## Slide 12: UWB Sensing Scenarios: Proxy application
Responder/Tx
Object being
sensed
Requesting
device
Initiator/Rx
    Mode A: Initiator is the sensing receiver, responder(s) are sensing transmitters
Sensing request
Sensing packet
OTA CIR measurement report

## Slide 13: UWB Sensing Scenarios: Proxy application
  Mode B: Initiator is the sensing transmitter, responders are sensing receivers
    Mode B requires two instances of OTA CIR measurement report.
Sensing request
Sensing packet
OTA CIR measurement report
Initiator/Tx
Object being
sensed
Requesting
device
Responder/Rx

## Slide 14: Discussion
The IEEE 15.4ab Task Group needs to decide which RF Sensing scenarios to support so that the corresponding protocol can be defined
  Following is our preliminary recommendation for discussion
RF Sensing Scenario | Recommendation | Comments
Mono-Static Sensing | Not support, open for more discussion | Requires more study on the feasibility of full-duplex implementation. May not need standard support
Bi-Static Sensing: Mode A [Initiator=sensing receiver] | Support | Core UWB sensing scenario
Bi-Static Sensing: Mode B [Initiator=sensing transmitter] | Support: can be optional | Higher overhead for OTA CIR report

## Slide 15: Discussion
The IEEE 15.4ab Task Group needs to decide which RF Sensing scenarios to support so that the corresponding protocol can be defined
RF Sensing Scenario | Recommendation | Comments
Multi-Static Sensing: Mode A [Initiator=sensing receiver] | Support: can be optional | Equivalent to multiple bi-static sensing sessions sequentially
Multi-Static Sensing: Mode B [Initiator=sensing transmitter] | Support: can be optional | Requires scheduling for OTA CIR measurement reports from responders
Proxy | Do not Support: open for more discussion | Need to establish use cases for 802.15.4ab

## Slide 16: References
Claudio da Silva, “IEEE 802.11bf Specification Framework Document,” IEEE 802.11-21/504r4, November 2021
Frank Leong, Wolfgang Küchler, Riku Pirhonen, “UWB Sensing in 802.15, IEEE 802.15-21/399r0,” July 2021
Xiaohui Peng, David Xun Yang, Chenchen Liu, Rani Keren, Kuan Wu, “CIR feedback for UWB sensing,” IEEE 802.15-21/570r0, November 2021