## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Dynamic Channel and Environmental Modeling Scheme for BANs on TG15.6a
Date Submitted: January 19th , 2022
Source: Takumi Kobayashi, Minsoo Kim, Marco Hernandez, Ryuji Kohno
Company: (1)Yokohama National University (2) YRP International Alliance Institute
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp, Kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract: This provides draft of channel and environmental model and its classification for vehicle body area network(VBAN) of amendment of IEEE802.15.6-2012 for wireless body area network(BAN) with enhanced dependability.
Purpose: Material for discussion in P802.15.6a TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Dynamic Channel and Environmental Modeling Scheme for BANs on TG15.6a
Takumi Kobayashi (1,2), Marco Hernandez (2), Minsoo Kim (2), Ryuji Kohno(1,2)
(1)Yokohama National University, (2)YRP-International Ariane Institute

## Slide 3: Channel models and scenarios in IEEE802.15.6-2012
IEEE 802.15.6-2012 channel models considered
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
CM1, 2, 3, 4
Scenario 1, to Scenario 7. (S1 – S7)
IEEE P802.15-08-0780-12-0006-TG6

## Slide 4: Classification of Channel and Environment Models for Human and Vehicle Body Area Networks (HBAN&VBAN)
Note:
HBAN-model:
-Environment with co-existing systems is not considered.
VBAN model:
Key-less entry system
Localization in-body, on-body
Most dominant model should be defined and separatory defined as Mandatory and Optional.
Channel model
HBAN model
VBAN model
In-body (Implant)
On-body
Around body
Outdoor
Indoor
Home
Office
Medical (e.g. Hospital)
In-vehicle
On-vehicle
Around vehicle
Engine compartment
Cabin
Through Engine compartment and cabin
Roof
Side Right/Left/Front/back
Bottom
Static vehicle
Moving vehicle
※Covered by IEEE 802.15.6-2012
※not covered yet
※Around means;
Desk, WiFi AP in the room etc.
Channel model
With environment
※
※
※
※
※

## Slide 5
RF
ANT
Propagation Model （based on S-V Model）
Interference from the other BAN
Interference from the other UWB (not BAN)
+
EMI from vehicle system
Colored noise
EV Switching noise
Ignition noise
etc…
RF
ANT
Channel model
Distance dependent function
Distance dependent function
Standard antenna
Standard antenna
Environmental model
Interference from the other Wireless systems
We propose to define environmental models including antenna effect. Parameter measurements will be performed by using standard antennas which will be defined separately.

## Slide 6: Channel and Environmental models between VBAN and HBAN
On-vehicle to On vehicle(LOS)
On-vehicle to On Body
On-body to On-body
In-Vehicle to On-body

## Slide 7: Scenario 3
Nodes and coordinator are in cabin room
Entertainment for passengers
  Nodes are in cabin room / coordinator is in cabin room.
  Symmetric environmental model
  EMI from engine and electric system are negligible. => channel model
Use case 3
Geometrical configuration
Noise source
Coordinator and node
 | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
3 | Entertainment for passengers | Case 3.1 |  | Case 3.3 | Same as 3.1 | ---

## Slide 8: Scenario 3’ for BUS
Nodes and coordinator are in cabin room
Geometrical configuration
coordinator
Noise source
VBAN Coordinator
HBAN Coordinator
Entertainment for passengers
  Nodes are in cabin room / coordinator is in cabin room.
Use case 3
 |  | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
3’VV | VBAN coordinator and VBAN coordinator | Case 3.1a |  | Case 3.3 | Same as 3.1 | ---
3’VH | VBAN coordinator and HBAN coordinator | Case 3.1b |  |  |  | ---

## Slide 9: Scenario 4
Key-less entry system
  Node is around user outside of vehicle / coordinator is in Engine compartment
  Asymmetric environment. Two direction model should be defined separatory.
Use case 4
Geometrical configuration
Engine compartment / body surface (outside)
 | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
4 | Key-less entry system | Case 4.1 V-H | Case 4.2 V-H | Case 4.3 V-H |  | ---
 |  | Case 4.1 H-V | Case 4.2 H-V | Case 4.3 H-V |  | ---
Noise source
VBAN Coordinator
HBAN Coordinator

## Slide 10: Scenario 5
Outside surface of vehicle / coordinator is in Engine compartment
Communication between user on pedestrian and vehicle
  Node is around user outside of vehicle / coordinator is on outside surface of vehicle (vehicle moves in walking speed (<5km/h))
  Asymmetric environmental model
Use case 5
Geometrical configuration
Moving at walking speed (<5km/h)
 | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
5 | Communication between user on pedestrian and vehicle | Case 5.1 V-H |  | Case 5.3 V-H |  | ---
 |  | Case 5.1 H-V |  | Case 5.3 H-V |  | ---
Noise source
VBAN Coordinator
HBAN Coordinator

## Slide 11: Dynamic Channel Models Situations
Channel between a user on pedestrian and a vehicle.
Users in a vehicle are slightly moving due to vibration and acceleration.
Walking and/or standing users on a bus.
Between a tractor and trailer tail.
Moving at walking speed (<5km/h)
Noise source
VBAN Coordinator
HBAN Coordinator
LOS
NLOS
LOS

## Slide 12: Dynamic on-body channel modeling
Timo Kumpuniemi, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Dynamic On-Body UWB Radio Channel Modeling”, ISMICT2015, (2015)
Dynamic channel characteristics and parameters were derived categorizing the links into three classes: high, medium or low dynamics channels. (T. Kumpuniemi et al. 2015) The work is based on frequency domain measurements with a vector network analyzer in an anechoic chamber at a 2-8 GHz frequency band.
[ref] Timo Kumpuniemi, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Dynamic On-Body UWB Radio Channel Modeling”, ISMICT2015, (2015)

## Slide 13: Measured Characteristics
[ref] Timo Kumpuniemi, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Dynamic On-Body UWB Radio Channel Modeling”, ISMICT2015, (2015)

## Slide 14: Measured characteristics
[ref] Timo Kumpuniemi, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Dynamic On-Body UWB Radio Channel Modeling”, ISMICT2015, (2015)

## Slide 15: Distribution fitting and CDF
A distribution fitting was applied.
[ref] Timo Kumpuniemi, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Dynamic On-Body UWB Radio Channel Modeling”, ISMICT2015, (2015)

## Slide 16: Dynamic off-body channel modeling
Timo Kumpuniemi, Juha-Pekka Mäkelä, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Measurements and Analysis on Dynamic Off-Body Radio Channels at UWB Frequencies”, ISMICT2019. (2019)
Timo Kumpuniemi, Juha-Pekka Mäkelä, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Measurements and Analysis on Dynamic Off-Body Radio Channels at UWB Frequencies”, ISMICT2019. (2019)
Dynamic offbody radio channels in an UWB frequency range for wireless BAN was presented (T. Kumpuniemi et al. 2019) . Ten frequencies were examined at two links, and the path loss values and standard
deviations were determined. Then, all the links were considered at three discrete frequencies.

## Slide 17: Measured characteristics
Path loss variation at selected frequencies for the LE-PO and LWPO channels using dipoles.
Path loss variation at selected frequencies for the RE-PO and RWPO channels using dipoles.
[ref] Timo Kumpuniemi, Juha-Pekka Mäkelä, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Measurements and Analysis on Dynamic Off-Body Radio Channels at UWB Frequencies”, ISMICT2019. (2019)
Timo Kumpuniemi, Juha-Pekka Mäkelä, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Measurements and Analysis on Dynamic Off-Body Radio Channels at UWB Frequencies”, ISMICT2019. (2019)

## Slide 18: Measured characteristics
[ref] Timo Kumpuniemi, Juha-Pekka Mäkelä, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Measurements and Analysis on Dynamic Off-Body Radio Channels at UWB Frequencies”, ISMICT2019. (2019)

## Slide 19: Summary
Channel and Environmental models discussed in TG6a were described.
Importance to discuss dynamic and time-varying channel and environment modeling against person (user) and vehicle mobility was explained.
Introduced two examples of existing researches about measurement to be used dynamic channel modeling.

## Slide 20: Thank you for your attention

## Slide 21: Use case : On-vehicle Secure Key-less entry system
https://illust8.com/contents/2559
Smart key
Anchor node device
Anchor node device
on-vehicle environment
Around-vehicle environment

## Slide 22
Symmetric scenario
Coordinator
Node
In channel model (without EMI and Interference issues), two direction of propagation should be considered as equal:
Channel reciprocity.
Channel models of “Coordinator to node” and “Node to coordinator” without noise source should be the same.
Coordinator
Node
Asymmetric scenario
Coordinator
Node
Coordinator
Node
Noise and/or interference source
In case of environmental model including EMI, colored noise and interference issues, channel reciprocity does not hold.
In the Environmental model two different channel directions should be defined separately.
Environmental models of “Coordinator to node” and “Node to coordinator” should be different.

## Slide 23: Engine/Motor Compartment Environment
Many metallic components
Components existing in densely
Ignition noise, motor noise
Larger path-loss than free propagation
A lot of reflection of RF signal
Electro-magnetic interference, EMI issues
Ignition coil
Electric motor
High current battery and cable
Spark plug
Electric generator
https://www.as-web.jp/car/575374/attachment/03a_sub_dsc01273
Especially EV