## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: UWB and NB link budget comparison
Date Submitted: Jan, 2022
Source: Ziyang Guo, Peng Liu, Rani Keren, Xun Yang (Huawei Technologies)
Email: guoziyang@huawei.com
Abstract: Compare link budget between UWB, UNII-3, 15.4 OQPSK, BLE, BLE-coded
Purpose: Provide more link budget analysis and discuss whether NB signaling is more efficient than UWB signaling.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | Link budget analysis for UWB and how it compares with NB signaling schemes under different conditions
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3
  UWB next generation task group (TG 4ab) is considering the definition of an NB PHY that is coupled to UWB PHY in order to assist it in various ways, for example, transmission offload or synchronization.
  Such a UWB+NB coupled operation requires a NB PHY range that is equal or higher than the next generation UWB PHY range.
  [1] proposed a new UWB transmit scheme aimed for increased UWB range that relies on synchronization assistance from a NB PHY but no range comparison analysis.
  [3] initiated a link budget comparison and suggested that current UWB PHY (BPRF mode) is more or less balanced with some candidate NB PHYs, but states that there is no decisive conclusion.
  [4] provided a link budget calculation at the end showing that an NB PHY will not necessarily meet the required range of a potential new generation UWB.
Narrowband assisted UWB - Overview

## Slide 4
Purpose
  Analyze LM for ranging and LM improvement due to ranging preamble segmentation [1]
  Analyze LM for different SYNC PHY candidates, including NB and UWB PHYs
SYNC
Packet
t/ms
1
2
3
N
Frag 1
Frag 2
Frag 3
Frag N
Time and Freq Sync
Ranging Preamble

## Slide 5
Link Margin Analysis for Ranging
Where is link margin gain of ranging preamble segmentation from?

## Slide 6
  Tx Power:
  Rx Sensitivity:
  Path Loss @1m:
  Link Margin:
Link Margin Analysis for Ranging
BO: backoff
GG: gating gain (Tx power gain for short packets)
PG: Processing Gain
NF: noise figure

## Slide 7
  PG (Processing Gain):
  denotes the number of pulses in ranging preamble
  GG (Gating Gain):
  denotes the preamble duration during 1ms
  GG is also known as power boosting gain due to distributing power to limited pulses
Link Margin Analysis for Ranging

## Slide 8
CRB Bound of UWB pulse [7]:
where is effective bandwidth, W=533MHz for the IEEE 802.15.4z reference pulse [8]
Supposing cm ragning accuracy, at least SNR=10dB is required
In the LM calculation, assuming dB
Link Margin Analysis for Ranging

## Slide 9
Link Margin Analysis for Ranging
Cfg0: conventional approach without preamble fragment
Cfg1: N=32, Cfg2: N=16, Cfg3: N=8, Cfg4: N=4, Cfg5: N=2
Configurations refer to [2].
configurations | cfg0 | cfg1 | cfg2 | cfg3 | cfg4 | cfg5
Total preamble duration(us) | 960 | 960 | 960 | 960 | 960 | 960
N | NA | 32 | 16 | 8 | 4 | 2
PRF(MHz) | 64 | 64 | 64 | 64 | 64 | 64
Fragment Duration(us) | NA | 30 | 60 | 120 | 240 | 480
PSD(dBm/MHz) | -41.3 | -41.3 | -41.3 | -41.3 | -41.3 | -41.3
fc(Hz) | 7983000000 | 7983000000 | 7983000000 | 7983000000 | 7983000000 | 7983000000
B(Hz) | 499200000 | 499200000 | 499200000 | 499200000 | 499200000 | 499200000
backoff(dB) | 1 | 1 | 1 | 1 | 1 | 1
NF(dB) | 6 | 6 | 6 | 6 | 6 | 6
Processing Gain | 47.88451207 | 47.88451207 | 47.88451207 | 47.88451207 | 47.88451207 | 47.88451207
Preamble Duration | 0.00096 | 0.00003 | 0.00006 | 0.00012 | 0.00024 | 0.00048
GG | 0.17728767 | 15.22878745 | 12.2184875 | 9.20818754 | 6.197887583 | 3.187587626
Ptx | -15.1399666 | -0.08846678 | -3.09876674 | -6.10906669 | -9.11936665 | -12.1296666
SNRmin(1.5cm@CRB) | 10 | 10 | 10 | 10 | 10 | 10
Prx | -71.0172542 | -71.0172542 | -71.0172542 | -71.0172542 | -71.0172542 | -71.0172542
Path Loss | 55.87728767 | 70.92878745 | 67.9184875 | 64.90818754 | 61.89788758 | 58.88758763
PL_1m | 50.48509477 | 50.48509477 | 50.48509477 | 50.48509477 | 50.48509477 | 50.48509477
LM | 53.27670497 | 68.32820475 | 65.31790479 | 62.30760484 | 59.29730488 | 56.28700493

## Slide 10
Link Margin Analysis for Ranging
LM can be boosted by preamble segmentation
The LM improvement is all from Gating Gain, which is limited by regulation and power amplifier complexity
Lower than 18dB, stated in [2]
Chart: Number of fragments
| 32 | 16 | 8 | 4 | 2
 | 15.0515 | 12.0412 | 9.0309 | 6.0206 | 3.0103

## Slide 11
Link Margin Analysis for SYNC Packet Transmission
How to pick the PHY for SYNC packet transmission to get a comparable LM with ranging?

## Slide 12: Technologies of interest
We would like to perform a link budget analysis for the following technologies:
Technology |  | 
UWB-0.85 | 500 | 0.85
UWB-6.8 | 500 | 6.8
UNII-3* | 5 | 1.625
OQPSK* | 2 | 0.25
BLE | 2 | 1
BLE-coded | 2 | 0.125
Technology |  | 
UWB-0.85 | 500 | 0.85
UWB-6.8 | 500 | 6.8
UNII-3* | 5 | 1.625
OQPSK* | 2 | 0.25
BLE | 2 | 1
BLE-coded | 2 | 0.125
is bandwidth, is data rate.
UNII-3 and OQPSK are NB radios proposed in [2]. The data rate of UNII-3 is calculated from Wi-Fi (20MHz, MCS0, 6.5Mb/s).

## Slide 13
  Tx Power:
  Rx Sensitivity:
  Link Margin:
Link Margin Analysis for SYNC Packet
BO: backoff
GG: gating gain (Tx power gain for short packets)
NF: noise figure

## Slide 14
  According to FCC and CE regulations [5, 6],
    For OQPSK, BLE, BLE-coded, the maximum output power can go up to 20dBm.
    For UNII-3, the maximum output power for non-specific short-range device is 14dBm; If an adequate spectrum sharing mechanism (e.g., DFS and DAA) is implemented, the maximum output power can go up to 26dBm.
  LM of NB are larger than UWB.
Link Margin Analysis for SYNC Packet
Parameters | UWB(BPRF-0.85) | UWB(BPRF-6.8) | UNII-3 | OQPSK | BLE | BLE-coded
CC_rate | 0.5 | 0.5 |  |  |  | 
RS_rate | 0.87 | 0.87 |  |  |  | 
meanPRF(Hz) | 15600000 | 15600000 |  |  |  | 
Ncpb | 16 | 2 |  |  |  | 
Tdsym | 1.02564E-06 | 1.28205E-07 |  |  |  | 
Nsync | 64 | 64 |  |  |  | 
Nsfd | 8 | 8 |  |  |  | 
Tpsym | 9.9359E-07 | 9.9359E-07 |  |  |  | 
payload(bits) | 160 | 160 |  |  |  | 
EbN0(dB) | 3.5 | 3.5 | 1.5 | 8.5 | 8.5 | 4
PSD(dBm/MHz) | -41.3 | -41.3 |  |  |  | 
Output power(dBm) | -14.31725423 | -14.31725423 | 14 | 10 | 10 | 10
fc(Hz) | 7983000000 | 7983000000 | 5800000000 | 2450000000 | 2450000000 | 2450000000
B(Hz) | 499200000 | 499200000 | 5000000 | 2000000 | 2000000 | 2000000
Backoff(dB) | 1 | 1 | 1 | 1 | 1 | 1
Noise figure(dB) | 6 | 6 | 6 | 6 | 6 | 6
Rb | 848250 | 6786000 | 1625000 | 250000 | 1000000 | 125000
Td | 0.00030641 | 0.000100897 |  |  |  | 
GG | 5.136966756 | 9.961197909 | 0 | 0 | 0 | 0
Ptx | -10.18028748 | -5.356056325 | 13 | 9 | 9 | 9
Prx | -105.2147613 | -96.18386145 | -104.3914663 | -105.5205999 | -96 | -100
Path Loss | 95.03447384 | 90.82780512 | 117.3914663 | 114.5205999 | 105 | 109
PL@1m | 50.48509477 | 50.48509477 | 47.71033206 | 40.22509387 | 40.22509387 | 40.22509387
LM | 44.54937907 | 40.34271035 | 69.68113429 | 74.29550604 | 64.77490613 | 68.77490613

## Slide 15
For NB systems, 20dB multipath fading is assumed.
When multipath fading is considered, LM of NB using previous Tx power are comparable to UWB.
Increasing Tx power to the limit of regulations can further increase the LM of NB PHYs.
Multipath Fading Effect
Parameters | UWB(BPRF-0.85) | UWB(BPRF-6.8) | UNII-3 | OQPSK | BLE | BLE-coded
Output power(dBm) | -14.31725423 | -14.31725423 | 14 | 10 | 10 | 10
LM | 44.54937907 | 40.34271035 | 49.68113429 | 54.29550604 | 44.77490613 | 48.77490613
Parameters | UWB(BPRF-0.85) | UWB(BPRF-6.8) | UNII-3 | OQPSK | BLE | BLE-coded
Output power(dBm) | -14.31725423 | -14.31725423 | 26 | 20 | 20 | 20
LM | 44.54937907 | 40.34271035 | 61.68113429 | 64.29550604 | 54.77490613 | 58.77490613

## Slide 16
LM for ranging is usually larger than that for data transmission and can be improved by preamble segmentation
To obtain a comparable LM as ranging, NB PHYs for SYNC packet might be a good candidate, especially at LoS scenario
Alternatively, other methods might be required to improve LM of UWB PHY for SYNC packet transmission, e.g., new channel coding
Summary

## Slide 17
References
15-21-0605, Nba-mms-uwb-mac-considerations, Yong Liu et al (Apple Inc.)
15-21-0593, More on narrowband assisted multi-millisecond UWB, Ersen Ekrem et al (Apple Inc.)
15-21-0394, IR-UWB link budget analysis and how it compares with NB signaling, Koorosh Akhavan (Qualcomm Inc.)
15-21-0557, UWB Wakeup Signaling, Michael Mc Laughlin et al (Qorvo)
FCC: Sec 15.247
ETSI: EN 300 328
D. Dardari et al, Ranging With Ultrawide Bandwidth Signals in Multipath Environments, Proceedings of the IEEE, vol. 97, no. 2, pp. 404-426, 2009
I. Domuta et al, Timestamp Estimation in P802.15.4z Amendment, Sensors, vol. 20, no. 18, 2020