## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: The Capacity and Accuracy Optimization for DL-TDoA of UWB
Date Submitted: 21th Jan 2022
Source: Libra Xiao (NewRadio Technology), Weidong Tang (NewRadio Technology)
Contact: 1408, Building 4, Phase 1, Tianan Yungu, Bantian Street, Longgang District, Shenzhen, Guangdong, China
E-Mail: xiaojiaxing@newradiotech.com, tangweidong@newradiotech.com
Re: Call for contributions to IEEE 802.15 TG4ab
Abstract: UWB related capacity and accuracy solution for optimizing DL-TDoA
Purpose: Discussion of how to improve 802.15.4(z) to serve industrial positioning systems
Notice: This is a basis for discussion and is not binding on the contributing individual(s) or document prepared to assist the IEEE P802.15. The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
submission

## Slide 2
submission
PAR Objective | The Proposed Solution (how addressed)
Safeguards so that the high throughput data will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | Using FDMA/CDMA/SDMA schemes to improve capacity by reducing the interference among many UWB devices with higher density
Other coexistence improvements | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | Using channel pool, code pool or antenna pool to improve position accuracy / precision with the DL-TDoA algorithm against the TDMA scheme
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3
submission
Reverse TDOA Applications and Technical Characteristics
<15-21-0223-00-04ab>, April 2021, Zhenzhen Ye (Red Point Positioning)
Downlink TDOA (DL-TDOA) Location Service in 802.15
<15-21-0488-00-04ab>, Sept 2021, Zhenzhen Ye (Red Point Positioning)
DL-TDOA positioning TDMA scheme
<15-21-0530-00-04ab>, Oct 2021, Jean-Marie André (ST microelectronics), Sven Zeisberg (Zigpos)
Beacon and Ranging Frames to Support Downlink TDOA (DL-TDOA) Location Service in 802.15
<15-21-0616-00-04ab>, Nov 2021, Yongsen Ma and Zhenzhen Ye (Red Point Positioning)
Previous submissions

## Slide 4
submission
UWB Anchor: the FFD in page 57 of IEEE 802.15.4-2020 operated as a coordinator
UWB Tag: the FFD in page 57 of IEEE 802.15.4-2020 operated as a device
Channel pool: communication channels approved in a region
Code pool: a set of codes defined for the CDMA scheme.
Antenna pool: a set of antennae used in the SDMA scheme
Terminology

## Slide 5
submission
Full Blown UWB anchors are regular anchors. They are connected to the mains and can communicate as much as needed.
    Battery Powered UWB anchors are not connected to the mains. They are easy for installation and useful for densifying a place where accurate DL-TDoA is needed. For such devices, the operation time must be minimized in order to save power and maximize the lifetime of battery.
Recap of DL-TDoA

## Slide 6
submission
Extra Scheduling
  Complicate scheduling makes deployment more difficult and reduces capacity.
Inaccurate Positioning
  A moving UWB tag can not achieve accurate ranging result, because it receives messages at different locations.
The Problems of DL-TDoA with TDMA

## Slide 7
submission
Positioning of a moving tag
Note:
stand for the locations of the UWB tag during ranging
Figure1.T1
Figure2. T2
Figure3. T3
Figure4. T4
UWB Anchor A
UWB Anchor B
UWB Anchor C
UWB Anchor D
Moving UWB Tag
T1
UWB Anchor A
UWB Anchor B
UWB Anchor C
UWB Anchor D
Moving UWB Tag
T2
UWB Anchor A
UWB Anchor B
UWB Anchor C
UWB Anchor D
Moving UWB Tag
T3
UWB Anchor A
UWB Anchor B
UWB Anchor C
UWB Anchor D
Moving UWB Tag
T4
➀
➁
➂
➃
➀
➁
➂
➃
➀
➁
➂
➃
➀
➁
➂
➃
➀
➁
➂
➃
Ra
Rb
Rc
Rd

## Slide 8
submission
Inaccuracy caused by moving can be addressed by FDMA scheme, CDMA (Code Division Multiple Access) scheme, or SDMA (Space Division Multiple Access) scheme.
FDMA scheme
  Different UWB anchors operate at different frequencies.
  No scheduling is required during ranging.
FDMA Solution

## Slide 9
submission
An example of FDMA
A
B
Note：This example uses the channel pool of CH5/CH6/CH8/CH9 in IEEE 802.15.4-2020 as showed in the figure above

## Slide 10
submission
  CDMA
    Full available spectrum
    Each UWB anchor with a unique code
    Low power spectrum density
  SDMA
    All devices operate at the same time and use the same space.
    A single UWB anchor can communicate with more UWB tags with the same frequency.
    Because directional spot-beam antennae are used, the UWB anchors in SDMA can track a moving UWB tag.
CDMA and SDMA Solutions

## Slide 11
submission
  FDMA: mature technology, simple equipment, no need for network synchronization, reliable work, high-capacity lines, high-efficiency, suitable for occasions with few stations and large capacity
  CDMA: no frequency planning, good confidentiality, strong anti-jamming and anti-interception capabilities, using multi-path characteristics and using RAKE technology to improve performance
    Cons: low spectrum utilization rate, not suitable for large-capacity systems
  SDMA: the same space using multiple beams
Advantages of Proposed Solutions

## Slide 12
submission
FDMA uses four or more channels at the same time.
CDMA uses one channel, and four or more spread codes to differentiate UWB anchors.
SDMA uses directional information to tell the difference between UWB anchors.
Summary of Proposed Schemes

## Slide 13
submission
MAC: to support channel, code or antenna pools as option in specifications
PHY: to support multiple channels , codes or antennae to work at the same time.
Proposed changes for MAC & PHY

## Slide 14
submission
Thank you for listening!

## Slide 15
submission
Channels in IEEE 802.15.4-2020