## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: Interference detection for high-integrity ranging in UWB systems: Part II (the updated version of the contribution “A method to evaluate the quality of ToF measurement for IR-UWB”)
Source: Li Sun, Peng Liu, Yuwei Wang, David Xun Yang (Huawei Technologies)
Address : [Huawei Bantian Base, Longgang District, Shenzhen, 518129 China]
E-Mail: [sunli50@huawei.com]
Re: Task Group 4ab: UWB Next Generation for 802.15.4
Abstract: [ToF, Measurement quality evaluation, Trustworthiness level, Ranging]
Purpose:
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | This proposal presents a new metric to evaluate the trustworthiness level of ToF measurements, which can be used to adjust the ranging procedure flexibly.
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Related Contributions and Objectives
A method to evaluate the quality of ToF measurement for IR-UWB <15-22-0073-00-04ab>, Jan. 2022, Li Sun et. al.
Related Contributions
Objectives of this contribution
This presentation provides updates to the above contribution 15-22-0073-00-04ab
To clarify the background and motivations of the proposed technique in above contribution, and clearly describe the problem that the proposed technique wants to solve
To provide more explanations on how to exploit the proposed metric to optimize the ranging procedure

## Slide 4: Background and Motivations
Due to the openness of wireless medium, accidental or intentional interference from other transmitters may undermine the leading edge detection and cause performance degradation in ranging accuracy
If the receiver detects the possible existence of an interference, the ranging measurement result cannot be fully trusted or exploited for round-trip time estimation
It is desired to give a quantitative evaluation on the trustworthiness of the ranging measurement results and use this evaluation report to improve ranging performance

## Slide 5: Current Standard: FoM
If extension bit = 0, the Figure-of-Merit (FoM) characterizes the accuracy of the PHY estimate of the arrival time of the RMARKER at the antenna.
While FoM gives an evaluation of the ranging accuracy, there is no metric in current standard to provide an explicit indication of whether or not the ranging procedure is being interfered with.
FoM with extension bit 0 has a clear meaning, but FoM with extension bit 1 is not defined (unless bits 0~6 are all zeroes, which means the ranging result is incorrect).
FoM with extension bit=0 (Source: IEEE 802.15.4z-2020)0

## Slide 6: Proposal 1: Extend the Definition of FoM
Do integrity check to produce an integrity score z satisfying , where x is the length of the STS (the proposed integrity check method in 15-22-0072-02-04ab is assumed here as an example, but we do not exclude other methods)
Example (doc: 15-22-0072-02-04ab)
Notes: A natural thinking is to extend the definition of FoM to support the characterization of the trustworthiness of the ranging result. To realize this, the ranging protocol should support integrity check (or attack detection) functionality. If this is supported, you can do integrity check first to produce an integrity score. Different approaches might be used to realize this. Here, we only present an example which I have just shown in my previous presentation. In this example, integrity check is realized using a correlation-based method, and the obtained integrity score z satisfies −x≤z≤x.

## Slide 7: Proposal 1: Extend the Definition of FoM
Modified definition of FoM
: this corresponds to the case where the receiver is sure that an interference occurs. In this case, set bit 7=1 and all other bits to be 0  the measurement result cannot be used (compatible with current standard)
: the ranging procedure is being interfered with a possibility that is inversely proportional to z. Set bit 7=1, and other bits are the binary representation of the trustworthiness level, defined as
where
z=x: this corresponds to the case where the receiver is sure that no interference exists. In this case, bit 7 is set to be 0, and other bits are defined as is done in current standard to reflect ranging accuracy

## Slide 8: Proposal 1: Extend the Definition of FoM
Main points for the modified definition of FoM :
Bit 7=0: there is no interference, and bits 0~6 characterizes the accuracy of the ToF estimate, as is defined in current standard
Bit 7=1: there might be an interferer, and bits 0~6 characterizes the trustworthiness level of the ToF estimate (i.e., the possibility of not being interfered), defined as
Trustworthiness level=
Bit 7
Bits 0~6
You cannot characterize both accuracy and trustworthiness using one FoM unless bit 7=0  introduce a new metric

## Slide 9: Proposal 2: A new metric—— Trustworthiness Level (TL)
bit 7=0 if (the receiver is sure that the ranging procedure is being interfered and the measurement is thus useless) and bit 7=1 if (there might be an interference, but the receiver is not pretty sure, so the measurement can still be used)
If bit 7=0, bits 0~6 are all equal to 0 to indicate the measurement is useless
If bit 7=1, bits 0~6 are the binary representation of the trustworthiness level, defined as
usefulness indicator
Trustworthiness characterization
Do integrity check to produce an integrity score z satisfying , where x is the length of the STS
TL definition:
where
Bit 7
Bits 0~6

## Slide 10: The feedback of TL
Whether or not the feedback of TL is necessary depends on where the TL is computed and what it is used for.
For example, if the proposed integrity check method in slide 6 is used, TL is computed at the initiator and is used to measure the trustworthiness of the entire ranging round: No need to feedback
There are also other choices for integrity check. For example, if the receiver-only method is used (i.e., the benchmark B method shown in doc: 15-22-0072-02-04ab), TL is computed at the responder and is used to measure the trustworthiness of a single ToA measurement: Feedback is needed

## Slide 11: The feedback of TL from responder to initiator
Based on the collected TL reports, the initiator can adjust the ranging procedure flexibly.
For example, if multiple consecutive “poor” TL reports are collected, implying a higher possibility of being interfered, the ranging procedure should be suspended, and restarted after some time. This is because that ranging in heavily interfered environments is useless and only causes waste in energy.
More broadly, the TL reports can be provided to higher layers to enable various applications such as environmental sensing.
The TL reports can be included in the “RangingReportDescriptor” as a new element, and fed back from the responder to the initiator.
Initiator
Responder
timestamp repots & the associated TLs
Ranging
Ranging
t1
t2
t3
t4

## Slide 12: Summary
It is desired to evaluate the quality of ToF measurements in a more comprehensive way, which can reflect not only the accuracy but also the trustworthiness of the measurements
We propose two methods in this contribution, i.e., to extend the current definition of FoM or to introduce a new metric called trustworthiness level (TL)
When necessary, TL reports can be fed back from the responder to the initiator to enable a more flexible ranging procedure