## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Summary of Channel and Environmental Modeling Activities for BANs on TG15.6a
Date Submitted: May 10th, 2022
Source: Takumi Kobayashi, Minsoo Kim, Marco Hernandez, Ryuji Kohno
Company: (1)Yokohama National University (2) YRP International Alliance Institute
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp, Kohno@yrp-iai.jp]
Re: In response to call for technical contributions
Abstract: This provides draft of channel and environmental model and its classification for vehicle body area network(VBAN) of amendment of IEEE802.15.6-2012 for wireless body area network(BAN) with enhanced dependability.
Purpose: Material for discussion in P802.15.6a TG corresponding to comments in EC Meeting
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Summary of Channel and Environmental Modeling Activities for BANs on TG15.6a
Takumi Kobayashi (1,2), Marco Hernandez (2), Minsoo Kim (2), Ryuji Kohno(1,2)
(1)Yokohama National University, (2)YRP-International Ariane Institute

## Slide 3
This presentation is a summary of 3 documents below.
Channel and Environmental Models of Human and Vehicle Body Area Network, doc.# 15-21-0244-06-006a
Channel and Environmental Models Classification for Vehicle Body Area Network on TG15.6a, Doc.# 15-21-0560-01-006a
Dynamic Channel and Environmental Modeling Scheme for BANs on TG15.6a, Doc.# 15-22-0023-00-006a

## Slide 4: Channel models and scenarios in IEEE802.15.6-2012
IEEE 802.15.6-2012 channel models considered
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
CM1, 2, 3, 4
Scenario 1, to Scenario 7. (S1 – S7)
IEEE P802.15-08-0780-12-0006-TG6

## Slide 5: Channel models and scenarios in IEEE802.15.6ma
Fading ( Small scale/ large scale)
Path loss
Shadowing
Power delay profile
In-body (implant)
On-body (body surface)
In-body (BCI)
On-body (BCI)
capsule endoscopy
Need to discuss standard antenna issues.
Scenario | Description | Frequency Band | Channel Model
S1 | Implant to Implant | 402-405 MHz, 3.1-10.6 GHz UWB | CM1
S2 | Implant to Body Surface | 402-405 MHz, 3.1-10.6 GHz UWB | CM2
S3 | Implant to External | 402-405 MHz, 3.1-10.6 GHz UWB | CM2
S4 | Body Surface to Body Surface (LOS) | 13.5, 50, 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S5 | Body Surface to Body Surface (NLOS) | 13.5, 50, 400, 600, 900 MHz 2.4, 3.1-10.6 GHz | CM3
S6 | Body Surface to External (LOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM4
S7 | Body Surface to External (NLOS) | 900 MHz 2.4, 3.1-10.6 GHz | CM4
Specific use cases |  |  | 
Implant to Body Surface for BCI | Implant to Body Surface for BCI |  | 
Implant to External for BCI | Implant to External for BCI |  | 
Body Surface to External for BCI | Body Surface to Body Surface for BCI |  | 
Implant to External for capsule endoscopy | Implant to External capsule endoscopy |  | 

## Slide 6: Classification of Channel and Environment Models for Human and Vehicle Body Area Networks (HBAN&VBAN)
Note:
HBAN-model:
-Environment with co-existing systems is not considered.
VBAN model:
Key-less entry system
Localization in-body, on-body
Most dominant model should be defined and separatory defined as Mandatory and Optional.
Channel model
HBAN model
VBAN model
In-body (Implant)
On-body
Around body
Outdoor
Indoor
Home
Office
Medical (e.g. Hospital)
In-vehicle
On-vehicle
Around vehicle
Engine compartment
Cabin
Through Engine compartment and cabin
Roof
Side Right/Left/Front/back
Bottom
Static vehicle
Moving vehicle
※Covered by IEEE 802.15.6-2012
※Around means;
Desk, WiFi AP in the room etc.
Channel model
With environment
※
※
※
※
※
Implanted BCI model
※not covered yet
On skull BCI model

## Slide 7
Channel model
Large scale fading
Small scale fading
HBAN
Channel model
VBAN
Channel model
Path loss
Shadowing
In-body
On-body
Surrounding body
In-vehicle
On-vehicle
Surrounding vehicle
From 15.6-2012
From 15.4a
UWB Channel model
Simulation methodology
HBAN
Channel model
In-body
On-body
Surrounding body
VBAN
Channel model
In-vehicle
On-vehicle
Surrounding vehicle
15.4a Indoor residential
15.4 outdoor
15.4 Indoor residential
15.4 outdoor
Marco san provided
15.8
From 15.4ab

## Slide 8: Channel and Environmental Models
Path loss
Reflection
Multipath
Fading
LOS / NLOS model
White Gaussian noise
Interference from co-existing wireless systems e.g. Bluetooth, IEEE 802.11, IEEE 802.15.4 etc.
Interference from the other BANs.
Interference from the other electric systems, devices and components (Electro-magnetic interference; EMI from electric motors, spark plugs in vehicles, etc.
Electro-magnetic compatibility; EMC. Possibility to affect to the other systems and human body.
VBAN  HBAN interference
VBAN and HBAN  Vehicle control and human body impacts.
Colored noise (Impulse noise, spike noise, ignition noise etc.)
Time-varying channel and interference modeling (Statistic, non-static, pseudo static model)
※optional
or
?
Environment model
Channel model
Channel model
EMI EMC
Colored noise
Other wireless systems
Environment model
Time-varying modeling
※mandatory
※mandatory
※mandatory
※mandatory
※optional
※optional
※optional
※IEEE802.15.6-2012
※will be defined in this amendment
※mandatory
or
?
※mandatory
※Comments in May 2021.

## Slide 9
RF
ANT
Propagation Model （based on S-V Model）
Interference from the other BAN
Interference from the other UWB (not BAN)
+
EMI from vehicle system
Colored noise
EV Switching noise
Ignition noise
etc…
RF
ANT
Channel model
Distance dependent function
Distance dependent function
Standard antenna
Standard antenna
Environmental model
Interference from the other Wireless systems
We propose to define environmental models including antenna effect. Parameter measurements will be performed by using standard antennas which will be defined separately.

## Slide 10: Environment Model in Vehicle
5
1
2
3
4
6
Engine/motor diagnostic sensor and controller
Air pressure sensor, wheel health sensor and controller
Transmission monitoring sensor and controller
Cabin environment sensor (temperature, brightness, humidity etc.)
Sheet sensor, health care sensors for driver
Sheet sensor, health care sensors for passenger
Engine/Motor room environment model
Cabin room environment model
https://media.istockphoto.com/photos/transparent-car-design-wire-model3d-illustration-my-own-car-design-picture-id594040008?k=6&m=594040008&s=612x612&w=0&h=XE8LiBjpM51aB4pH2CFt6-MT6IvALRPnlxPcac0RXhg=
Note:
Various type of car/vehicles
Bus, Bulldozer, Heavy construction equipment needed each different sensors.

## Slide 11: Channel and Environmental models between VBAN and HBAN
On-vehicle to On vehicle(LOS)
On-vehicle to On Body
On-body to On-body
In-Vehicle to On-body

## Slide 12
HBAN coordinator to HBAN coordinator
Body surface to body surface
Considered similar

## Slide 13: Engine/Motor Room Environment
Many metallic components
Components existing in densely
Ignition noise, motor noise
Larger path-loss than free propagation
A lot of reflection of RF signal
Electro-magnetic interference, EMI issues
Ignition coil
Electric motor
High current battery and cable
Spark plug
Electric generator
https://www.as-web.jp/car/575374/attachment/03a_sub_dsc01273
Especially EV

## Slide 14: Environment models that can be applicable against different type of vehicles
Engine
Cabin
Engine
Cabin
Policy:
IEEE 802.15.6a defines several common environment models against most dominant use cases as mandatory models.
Categories:
Categorize several type of vehicle like “for passengers”, “bus”, “small cargo”, “middle cargo”, “Large cargo” and “special purpose vehicles” such as a construction machines and build models for various categories.
Different
Size;
Structure;...etc.
https://nohat.cc/f/heavy-truck-illustration-isolated-on-a-white-background/comvecteezy328938-201908251309.html

## Slide 15
Symmetric scenario
Coordinator
Node
In channel model (without EMC/EMI and Interference issues), two direction of propagation should be considered as equal:
Channel reciprocity.
Channel models of “Coordinator to node” and “Node to coordinator” without noise source should be the same.
Coordinator
Node
Asymmetric scenario
Coordinator
Node
Coordinator
Node
Noise and/or interference source
In case of environmental model including EMC/EMI . colored noise and interference issues, two direction between source and sink is not same meaning.
Environmental model of two different direction should be defined separately.
Environmental models of “Coordinator to node” and “Node to coordinator” should be different.

## Slide 16: Use cases
Failure and/or deterioration detection of vehicle components.
  - Nodes are in engine compartment / coordinator is in engine compartment
Sensing for safety driving support / Collision avoidance
  - Nodes are on outside surface of vehicle / coordinator is in engine compartment
Entertainment for passengers
  - Nodes are in cabin / coordinator is in cabin.
Key-less entry system - Node is around user outside of vehicle / coordinator is in engine compartment
Communication between user on pedestrian and vehicle
  - Node is around user outside of vehicle / coordinator is on outside surface of vehicle (vehicle moves at walking speed (<5km/h))
Vehicle controlling / Wireless herness
  - Coordinator and nodes are in between cabin and chassis of vehicle.
Driver’s health problem detection
  - Coordinator in engine compartment / nodes are on human (driver) body.
Driver’s and passenger’s healthcare application
  - Nodes and coordinator are on human body.

## Slide 17: Use cases
 | Use case | Sedan/RV / SUV with combustion internal engine | Sedan/RV / SUV EV | Bus | Cargo / pickup | Special purpose
1 | Failure and/or deterioration detection of vehicle components | Case 1.1 | Case 1.2 | Case 1.3 |  | Case 1.5
2 | Sensing for safety driving support / Collision avoidance | Case 2.1 C-N | Case 2.2 C-N | Case 2.3 C-N |  | Case 2.5 C-N
 |  | Case 2.1 N-C | Case 2.2 N-C | Case 2.3 N-C |  | Case 2.5 N-C
3 | Entertainment for passengers | Case 3.1 |  | Case 3.3 | Same as 3.1 | ---
4 | Key-less entry system | Case 4.1 C-N | Case 4.2 C-N | Case 4.3 C-N |  | ---
 |  | Case 4.1 N-C | Case 4.2 N-C | Case 4.3 N-C |  | ---
5 | Communication between user on pedestrian and vehicle | Case 5.1 C-N |  | Case 5.3 C-N |  | ---
 |  | Case 5.1 N-C |  | Case 5.3 N-C |  | ---
6 | Vehicle controlling / Wireless herness | Case 6.1 C-N |  | Case 6.3 C-N |  | Case 6.5 C-N
 |  | Case 6.1 N-C |  | Case 6.3 N-C |  | Case 6.5 N-C
7 | Driver’s health problem detection | Case 7.1 C-N |  | Case 7.3 C-N |  | Case 7.5 C-N
 |  | Case 7.1 N-C |  | Case 7.3 N-C |  | Case 7.5 N-C
8 | Driver’s and passenger’s healthcare application | IEEE 802.15.6 – 2012 Channel models can be applied |  |  |  | 

## Slide 18: Models between VBAN and HBAN
VBAN
coordinator
VBAN
node
VBAN
node
HBAN
coordinator
HBAN
coordinator
HBAN
node
HBAN
node
HBAN
node
HBAN
node
Channel and Environmental models for VBAN.
Channel and Environmental models for HBAN.
VBAN
coordinator
HBAN
coordinator
HBAN
coordinator
HBAN
node
Channel and Environmental models between VBAN coordinator and HBAN coordinators.
Channel and Environmental models between VBAN coordinator and VBAN coordinators.

## Slide 19: Channel and Environmental models between VBAN and HBAN
On-vehicle to On vehicle(LOS)
On-vehicle to On Body
On-body to On-body
In-Vehicle to On-body

## Slide 20: Scenario 3
Nodes and coordinator are in cabin room
Entertainment for passengers
  Nodes are in cabin room / coordinator is in cabin room.
  Symmetric environmental model
  EMI from engine and electric system are negligible. => channel model
Use case 3
Geometrical configuration
Noise source
Coordinator and node
 | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
3 | Entertainment for passengers | Case 3.1 |  | Case 3.3 | Same as 3.1 | ---

## Slide 21: Scenario 3’ for BUS
Nodes and coordinator are in cabin room
Geometrical configuration
coordinator
Noise source
VBAN Coordinator
HBAN Coordinator
Entertainment for passengers
  Nodes are in cabin room / coordinator is in cabin room.
Use case 3
 |  | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
3’VV | VBAN coordinator and VBAN coordinator | Case 3.1a |  | Case 3.3 | Same as 3.1 | ---
3’VH | VBAN coordinator and HBAN coordinator | Case 3.1b |  |  |  | ---

## Slide 22: Scenario 4
Key-less entry system
  Node is around user outside of vehicle / coordinator is in Engine compartment
  Asymmetric environment. Two direction model should be defined separatory.
Use case 4
Geometrical configuration
Engine compartment / body surface (outside)
 | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
4 | Key-less entry system | Case 4.1 V-H | Case 4.2 V-H | Case 4.3 V-H |  | ---
 |  | Case 4.1 H-V | Case 4.2 H-V | Case 4.3 H-V |  | ---
Noise source
VBAN Coordinator
HBAN Coordinator

## Slide 23: Scenario 5
Outside surface of vehicle / coordinator is in Engine compartment
Communication between user on pedestrian and vehicle
  Node is around user outside of vehicle / coordinator is on outside surface of vehicle (vehicle moves in walking speed (<5km/h))
  Asymmetric environmental model
Use case 5
Geometrical configuration
Moving at walking speed (<5km/h)
 | Use case | Sedan/RV / SUV with engine | Sedan/RV / SUV without engine | Bus | Cargo / pickup | Special purpose
5 | Communication between user on pedestrian and vehicle | Case 5.1 V-H |  | Case 5.3 V-H |  | ---
 |  | Case 5.1 H-V |  | Case 5.3 H-V |  | ---
Noise source
VBAN Coordinator
HBAN Coordinator

## Slide 24: Dynamic Channel Models Situations
Channel between a user on pedestrian and a vehicle.
Users in a vehicle are slightly moving due to vibration and acceleration.
Walking and/or standing users on a bus and train.
Between a tractor and trailer tail.
Moving at walking speed (<5km/h)
Noise source
VBAN Coordinator
HBAN Coordinator
LOS
NLOS
LOS

## Slide 25: Dynamic on-body channel modeling
Timo Kumpuniemi, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Dynamic On-Body UWB Radio Channel Modeling”, ISMICT2015, (2015)
Dynamic channel characteristics and parameters were derived categorizing the links into three classes: high, medium or low dynamics channels. (T. Kumpuniemi et al. 2015) The work is based on frequency domain measurements with a vector network analyzer in an anechoic chamber at a 2-8 GHz frequency band.
[ref] Timo Kumpuniemi, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Dynamic On-Body UWB Radio Channel Modeling”, ISMICT2015, (2015)

## Slide 26: Dynamic off-body channel modeling
Timo Kumpuniemi, Juha-Pekka Mäkelä, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Measurements and Analysis on Dynamic Off-Body Radio Channels at UWB Frequencies”, ISMICT2019. (2019)
Timo Kumpuniemi, Juha-Pekka Mäkelä, Matti Hämäläinen, Kamya Yekeh Yazdandoost, Jari Iinatti, “Measurements and Analysis on Dynamic Off-Body Radio Channels at UWB Frequencies”, ISMICT2019. (2019)
Dynamic offbody radio channels in an UWB frequency range for wireless BAN was presented (T. Kumpuniemi et al. 2019) . Ten frequencies were examined at two links, and the path loss values and standard
deviations were determined. Then, all the links were considered at three discrete frequencies.

## Slide 27: Summary
Environment model which has wider meaning than channel model has been proposed.
Environment model including not only channel characteristics but also including interference, colored noise, EMC and human impact issues.
Channel and Environmental models discussed in TG6a were described.
Importance to discuss dynamic and time-varying channel and environment modeling against person (user) and vehicle mobility was explained.

## Slide 28
Dynamic on-body measurement method can be applied to the measurement of channel modeling of on-vehicle VBAN.
Dynamic off-body measurement method can be applied to the measurement of channel modeling of surrounding vehicle VBAN.
IEEE802.15.4a, 4z, 4ab, 4f, and 8 channel model activities can be referred for our vehicle channel modeling.
TG6a (TG6) is forcusing on UWB channel model. 15.4a (4f, 4z, 4ab, 15.8 using the same model) can be used as common channels for UWB.

## Slide 29: Thank you for your attention