## Slide 1
Project: IEEE P802.15 Working Group for Wireless Speciality Networks (WSN)
Submission Title: Proposal to extend RIFS in IEEE Std 802.15.3d/e
Date Submitted: 4 March 2022
Source: Thomas Kürner TU Braunschweig(1), Keitarou Kondou HRCP(2), Fumihiro Nishiyama HRCP(3)
Address (1) Schleinitzstr. 22, D-38092 Braunschweig, Germany (2)(3) 1-24-2 Taito Taito-ku Tokyo, Japan
Voice: (1)+495313912416 (2) +81-334140206, FAX: (1)+495313915192 (2)+81-368060906, E-Mail: (1) t.kuerner@tu-bs.de (2) Keitarou.Kondou@hrcp.jp (3) Fumihiro.Nishiyama@hrcp.jp
Re: doc. 15-22/0071, 15-21-0398
Abstract: This document describes the required changes to extend RIFS in IEEE Std 802.15.3d/e to allow transmission at larger distances
Purpose: Input to Call for Proposal
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Proposal to extend RIFS in IEEE Std 802.15.3d/e
Thomas Kürner (TU Braunschweig)
Keitarou Kondou (HRCP)
Fumihiro Nishiyama (HRCP)
This inout is based on results from the ThoR project. ThoR has received funding from Horizon 2020, the European Union’s Framework Programme for Research and Innovation, under grant agreement No. 814523. ThoR has also received funding from the National Institute of Information and Communications Technology in Japan (NICT).

## Slide 3: Starting Point
  In doc. 15.21/0398 it was reported, that the current settings of the Retransmission Interframe Space (RIFS) is to short to cover the typical distances occurring at backhaul applications.
  The IEEE 802.15.3e chipset used in the ThoR project has been adapted to allow longer transmission distances
  RIFS is currently defined in Table 11a-20
  doc. 15.21/0398 suggests to increase RIFS by a factor of 10 and include new formulas to calculate RIFS

## Slide 4: Current Definition in IEEE Std 802.15.3d/e
    Section 13.2.6 provides rferences to section 11a.2.6.1 and Table 11a-20
MAC Parameter |  | Corresponding PHY Parameter | Definiton
SIFS |  | pPHYSIFSTime | 11a.2.6.3
RIFS | PRC | 2*pPHYSIFSTime + 3,01 ms | 7.4.1
 | DEV | 4*pPHYSIFSTime + 9,05 ms | 
RIFS(PRC) = 2 SIFS + tHdr
= 2 SIFS + 3.01 us
RIFS(PRC) = 4 SIFS + 3tHdr
= 4 SIFS + 9.05us

## Slide 5: Considering propagation delay
tpd = propagation delay
If 1-km link is assumed, tpd shall be 3.3us. Then RIFS should be increased by 6.7 us for PRC and 13.3 us for PRDEV

## Slide 6: Suggested changes
    Add a new table, which should be used for applications with transmission distances > 100 m
    tpd is set to 33.3 us, which supports up to 10 Km in distance.
    Add a flag in PRC/PRDEV capability and Pairnet operating parameters in section 6.4 Information IE for enabling longer distance operation.
MAC Parameter |  | Corresponding PHY Parameter | Definiton
SIFS |  | pPHYSIFSTime | 11a.2.6.3
RIFS | PRC | 2*pPHYSIFSTime + 69.7 ms | 7.4.1
 | DEV | 4*pPHYSIFSTime + 142 ms |