## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Channel Access Considerations on Fragmented UWB Format (More on)
Date Submitted: May, 2022
Source: Peng Liu, Ziyang Guo (Huawei Technologies)
Email: Jeremy.liupeng@huawei.com
Abstract: CCA support for fragmented UWB format to avoid interference or drop off invalid ToA estimation
Purpose: CCA support for fragmented UWB format to avoid interference or drop off invalid ToA estimation
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | conduct CCA before transmitting ranging fragment, indicate which fragments are not transmitted to drop off invalid ToA esitmation
Interference mitigation techniques to support higher density and higher traffic use cases | conduct CCA before transmitting ranging fragment, indicate which fragments are not transmitted to drop off invalid ToA esitmation
Other coexistence improvement | Coexistence of fragmented UWB format with legacy data transmission
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | New NB data frame to indicate CCA results of fragments
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3
  ~10*log10(N) dB link budget can be improved by segmenting ranging preamble with N fragments spanning N milliseconds[1-3] due to power boosting
  Meanwhile, interference will become worsen if multiple UWB pairs transmit simultaneously
Fragmented UWB Format (Recap)
Poll
t/ms
1
2
3
N
Frag 1
Frag 2
Frag 3
Frag N
Time and Freq Sync
Ranging Preamble
DATA
Res
1ms
1ms

## Slide 4
Interference Issues
  Interference from other UWB transmission may cause wrong ToA estimation of certain fragment
  Interference to other UWB transmissions may deteriorate their performance, e.g., packet loss or ToA estimation error, depending on their transmission scenarios, data transmission or ranging
SYNC
Packet
t/ms
1
2
3
N
Frag 1
Frag 2
Frag 3
Frag N
Time and Freq Sync
Interference from other UWB transmission
e.g., other ranging pair, other data transmission pair

## Slide 5
Interference Issues
Ranging using fragmented UWB format
Data transmission using IEEE 802.15.4z format@249.6 MHz PRF
tag
Simulation Settings | Descriptions
Fragment Duration | ~64us
Fragment Settings | 31-ternary codes, row No.1 of Table 15-4 at IEEE 802.15.4-2020 code length = 31; Peak PRF = 31.20MHz Mean PRF = 16.10MHz; Delta Length = 16; Symbol duration = 993.59ns
Preamble symbol repetition | 64
Coexisting data | IEEE 802.15.4z format@249.6 MHz PRF
Interference occurrence probability | 0.4
Channel model | CM4
Figure 1. A typical interference scenario
Table 1. Simulation Settings

## Slide 6
Interference Issues
Without IEEE 802.15.4z Interference
With IEEE 802.15.4z Interference
Back Search Window
Interference will cause wrong/invalid ToA estimation
20 samples
15dB
Ground True
Wrong ToA estimation

## Slide 7
Interference Issues (More on)
tag
D =10(m)
Dinter(m)：distance between interferer and tag
Interference impact becomes worsen as the decrease of interference distance
Number of Fragments: 8

## Slide 8
Channel Access Design
Poll
t/ms
Slot 1
Slot 2
Slot 3
Slot N
Frag 1
Frag 2
Frag 3
Frag N
Time and Freq Sync
1ms
1ms
DATA
CCA
Indicate which fragments are transmitted,
which are not due to CCA busy
  Sense channel for a fixed period of time (i.e., CCA duration) at the very beginning of each Slot
  If CCA is idle, transmit the fragment; otherwise not transmit
  At the end of the ranging round, transmit a data frame, indicating whether the fragment is transmitted. For example, N=8, the 2nd and 4th fragments are not transmitted due to CCA busy, a bitmap 11110101 can be transmitted in the indication frame.

## Slide 9
Channel Access Design
  CCA duration: it can be set in the Poll, less than 50us is recommended to ensure “coherent addition” of repeated preamble symbols [4]
  No backoff: simple and helpful to remain the time structure of 1ms spacing for power saving
  Data frame for indication: it is necessary in the case that interference may be similar to the ranging fragment. The ToA estimation will be wrong if the receiver does not know whether the received signal comes from the intentional transmitter
CCA Busy
Preamble of data transmission or ranging signal from other pair, which might be similar to or even identical to the fragment signal
E.g., the fragment and SYNC of interference employ the same sequence
Poll
t/ms
Frag 1
Frag 2
Frag 3
Frag N
1ms
1ms
DATA
Interference Signal
SYNC
DATA

## Slide 10
Benefits (More on)
  Efficient to discard the invalid ToA estimation results to get more reliable ranging results
  The benefits are incredible when the interferer is closer to the node of interest due to higher interference detection probability (CCA successful probability)
Dinter = 2, CCA succProb=~0.9
Dinter = 5, CCA succProb=~0.5
Dinter = 10, CCA succProb=~0.2
20%@2m to 80%@2m

## Slide 11
Benefits
  Easy to implement, CCA only
  Friendly to other coexistence UWB transmissions due to LBT
  Efficient to discard the invalid ToA estimation results to get more reliable ranging results; the stronger the interference, the more benefits achieved
  Remain periodic fragment time structure
  Support for fast termination or restart the ranging round after consecutive CCA busy
Poll
t/ms
Slot 1
Slot M
Terminate or Poll
CCA
Busy
CCA
CCA
Busy
Busy

## Slide 12
Wideband interference issue is highlighted for fragmented UWB format
CCA is recommended before transmitting each fragment
At the end of the ranging round, send a data frame to indicate the CCA results of each fragment to help the receiver discard the invalid ToA estimations
Easy to implement and not break mms- periodic fragment time structure
Summary

## Slide 13
References
More on narrowband assisted multi-millisecond UWB, 15-21-0593-02-04ab
15-22-0064-00-04ab-potentials-of-narrowband-assisted-uwb
15-22-0080-00-04ab-nba-mms-uwb-mac-followup
15-06-0160-00-004a-recommendation-parameters-cca-window-and-related-0-1mbps-issues