## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: Discussion on UWB sensing report
Date Submitted: March 8, 2022
Source: Pooria Pakrooh, Bin Tian, Steve Shellhammer and Koorosh Akhavan (Qualcomm)
E-Mail:{ppakrooh, btian, sshellha, kakhavan}@qti.qualcomm.com
Abstract: Follow-up discussion on UWB sensing capabilities support and report.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | We discuss design parameters for the window-based Channel Impulse Response (CIR) sensing approach and discuss CIR report format for it.
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Introduction
      We have proposed a window-based solution for CIR sensing report [1].
      Window-based CIR design is convenient because it addresses the following challenges in RF sensing
        Large dynamic range in CIR taps
        Consistency in CIR report for multiple CIR measurements to identify changes in the environment
Noise Threshold
-
Fixed window around the earliest detected tap
Earliest detected tap
Noise Threshold
-
Fixed window around the strongest detected tap
Strongest detected tap

## Slide 4: CIR Window Parameters
      In the window-based CIR report approach, there are CIR window parameters that need to be determined and included in the CIR report:
        Reference point for the CIR window
        Window offset
        Window length
        Number of windows
        CIR report sampling rate
        Number of bits for I/Q values in CIR report
      Additional parameters could be needed in the CIR report for multiple Rx antenna sensing scenario.
Noise Threshold
Sensing window parameters defined relative to the earliest detected tap
Reference Point: Earliest detected tap
+

## Slide 5: CIR Window: Reference and Number of Windows
      The reference point for the CIR window can be based on the earliest arrival tap of the estimated CIR.
      Other methods are possible for specifying the reference points for synchronized scenarios.
      One window is simple and may be sufficient.
        The duration and position of the window could be configurable to cover a large sensing area.
        Multiple windows increase complexity and potentially payload CIR feedback size. Its need requires to be discussed.

## Slide 6: CIR Window Length and Offset
      Through negotiation, and based on receiver’s capability, possible window length (), and initial offset of the window from the reference point () could be determined.
      Depending on the range of interest in a sensing application, specific window length and offset can be selected.
Noise Threshold
Sensing window parameters defined relative to the earliest detected tap
Reference Point: Earliest detected tap
+

## Slide 7: CIR Window Size
      Options for the duration of CIR window need to be specified in the standard so that so that HW implementation has a bounded complexity
      The window duration is determined by the delay spread in the sensing region, defined as = -
      The window size of around (32 taps at chipx2 sampling rate), can cover around 10m of sensing range spread. Sensing at farther range provides very low reflected power for most of sensing cases.
Initiator/ Tx
Responder/Rx
Object being
sensed
UWB Tx
UWB Rx

## Slide 8: Report of CIR values
      When window offset is zero, the CIR can be reported according the following approaches
        Approach 1: The CIR values can be interpolated and reported at sampling grid points relative to the interpolated first arrival path (Fig. 1). (At points , increases responder complexity
        Approach 2: [Preferred approach] To limit the complexity at the responder side Interpolation across CIR before reporting can be avoided (Fig. 2). (At points
          However, the earliest tap could be based on interpolation for ranging purpose.
          The CIR report includes the interpolated earliest tap offset from the grid ()
      When window offset is nonzero () then the sampling points in the above approaches would be shifted by
+2T
…
Earliest detected tap before interpolation
+2T
Earliest detected tap after interpolation
Second tap after interpolation
…
Second tap before interpolation
Fig. 1: CIR is interpolated before reporting (Green points are reported)
Fig. 2: CIR is reported at the grid point. Offset of earliest arrival path and grid point is contained in the report (Blue instances are reported), along with
Notes: 〖Δ𝑡〗_0 is related to the reply time in two way ranging. Le said the reply time is not related to earliest arrival path.
Window offset could be negative to include previous taps as well for interpolation.

## Slide 9: CIR Sensing Report: CIR Sampling Rate
Higher receiver sampling rate increases receiver complexity, and report overhead.
The payload size limit also need to be considered for CIR report.
Reported sampling rate: Chip ratex2 to provide a reasonable balance between accuracy and complexity, where chip rate is equal to the sensing bandwidth. Chip ratex1 may also be considered if feedback overhead is a concern.
  For single UWB channel, the sensing bandwidth is 499.2 MHz
  Sensing at multiple frequency segments is ongoing discussion. If adopted, chip rate is equal to the aggregated bandwidth, leading to larger sampling rates.

## Slide 10: CIR IQ Bit-width
      Number of bits in the report need to be limited
        Using large number of bits increases the report overhead
      Suggesting 12 bits for encoding signed I/Q each
        Even for dynamic range of around 48 dB, SQNR of 29 dB can be achieved
        The I/Q values can be normalized. The normalization (scaling) factor can be included in the report.
Full Scale
Smallest bit expected
8 bits ≃ 48 dB dynamic range
Quantization noise level ≃ -77 dBFs
Quantization noise is 29dB below LSB

## Slide 11: Multiple Rx Antennas
      Report of each antenna CIR, if requested, needs to be supported through negotiation.
      In the presence of multiple Rx antennas, Rx antennas can be reported sequentially.
      CIR report window for multiple antennas should be aligned
      The offset of grid points for the antennas relative to the common timing could be contained in the report
      For AoA analysis, Rx chain angle/latency calibration results can be included in the CIR report for compensation by initiator’s upper layer.
        It could be too cumbersome to compensate for the angle/latency at the responder side, as it requires interpolation over the antenna CIRs

## Slide 12: Content of the CIR Report
Field | Field length (bits) | Comments
Common Fields |  | 
Number of Rx antennas | TBD | 
Window duration () | 5 bits | 
Window offset () | 6 bits | offset from the reference point.
For Each Rx Chain |  | 
RF Chain Phase Calibration | TBD | One real value per Rx chain
RF Chain Latency Calibration | 7 bits | One real value per Rx chain; Like Ranging counter time unit, could be in units of of chipping period.
Timing Offset () | 7 bits | Offset of estimated EAP from grid points to assist with interpolation at initiator; Could be in units of of chipping period.
Normalization factor for I/Q | TBD | Common normalization value for In-phase and Quadrature CIR values
CIR In-Phase report | 12 bits | Per tap; normalized
CIR Quadrature report | 12 bits | Per tap; normalized
Field | Field length (bits) | Comments
Common Fields |  | 
Number of Rx antennas | TBD | 
 | 5 bits | 
 | 6 bits | offset from the reference point.
For Each Rx Chain |  | 
RF Chain Phase Calibration | TBD | One real value per Rx chain
RF Chain Latency Calibration | 7 bits | 
 | 7 bits | 
Normalization factor for I/Q | TBD | Common normalization value for In-phase and Quadrature CIR values
CIR In-Phase report | 12 bits | Per tap; normalized
CIR Quadrature report | 12 bits | Per tap; normalized

## Slide 13: References
[1] Pooria Pakrooh, Bin Tian, Steve Shellhammer, and Koorosh Akhavan “Link budget analysis and CIR reporting for UWB RF sensing”, IEEE 802.15-22-0066-01-4ab, January 2022
[2] Frank Leong, Wolfgang Küchler, Riku Pirhonen, “Sensing - Continued” January 2022