## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: MAC considerations for data communication
Date Submitted: March 2022
Source: Kangjin Yoon, Chunyu Hu, Carlos Aldana, Claudio Da Silva, (Meta Platforms, Inc)
Email: kyoon@fb.com
Abstract: High level overview and proposals about UWB data communication
Purpose: To discuss general direction for enhanced UWB data communication
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | Keeping slotted structure may help to make less impact to the coexisting ranging use-case
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | Scheduling can be used for data communication to save power
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | Scheduling mechanism for general data comm
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | Scheduling mechanism for general data comm, applicable to all described cases
Infrastructure synchronization mechanisms | 

## Slide 3: Previous Contributions for Data Communication
DCN 222r0 (Apr. 2021) “Data Communication enhancements”
  Introduced essential requirements for data communication in PHY perspective
DCN 501r0 (Sept. 2021) “Ways to achieve higher data rate for the HRP-UWB PHY”
  Shared options for achieving higher data rate
DCN 047r1 (Jan. 2022) “MAC layer considerations for UWB data streaming”
  Proposed channel access with energy detection sensing to improve coexistence performance

## Slide 4: UWB for Data Communication
UWB has low latency and relatively high PHY rate
 | BT Classic/LE | 802.15.4z UWB | 802.11 Wi-Fi
Latency | Low (No LBT [1]) | Low (No LBT) | High (LBT)
PHY rate | 3 Mbps | 31.2 Mbps | 100+ Mbps
Range | 10 m | 10 m (much shorter in NLOS) | 100 m
UWB is a good candidate for some type of time-sensitive traffic that requires higher PHY rate/throughput than BT Classic/LE can provide
In 4ab, we can enhance PHY rate and communication range while keeping low latency
[1] LBT: Listen-before-talk

## Slide 5: Target Network Topology
Star topology: One controller, one or more controlees
Controller
Controlee 2
Controlee 1
Controlee 3

## Slide 6: MAC Considerations for Data Comm.
To use UWB for data communication, we have following high level design questions as first step:
  Slotted structure vs. unslotted structure
  Contention-based vs. scheduling-based
  Control, scheduling mechanisms for data communication
  Ack mechanism for data frame (in separate contribution)

## Slide 7: Slotted Structure vs. Unslotted Structure
4z enhanced ranging utilizes slotted structure
 | Slotted Structure | Unslotted structure
Pros | Facilitate efficient scheduling Reuses 4z design Coex with ranging natively | More flexibility
Propose to focus on the slotted structure

## Slide 8: Contention-based vs. Scheduling-based
4z has both modes, while most of ranging applications utilize scheduling-based mode
 | Contention-based mode | Scheduling-based mode
Pros | Can support more devices than the number of slots No scheduling negotiation | Well defined in 4z-2020 Efficient channel usage thanks to no collision in intra-session Power saving
Fit | Bursty and unpredictable traffic per device | Recurring traffic pattern

## Slide 9: Scheduling-based Mode
Scheduling-based mode is preferred due to following reasons:
  Minimal change from 4z-2020
  More predictable latency if reliability can be maintained by link budget and retransmission
Contention-based mode might be still useful in some cases but probably limited and not always needed

## Slide 10: Control and Scheduling for Ranging
Controller sends Ranging Control Message (RCM) in the first slot of the Ranging Round
RCM contains:
  Advanced Ranging Control IE (ARC IE) for ranging control
    Which ranging method will be used (SS-TWR / DS-TWR)
    Which STS type will be used (SP0 / SP1 / SP2 / SP3)
    Which schedule mode will be used (Scheduling-based mode / Contention-based mode)
    Block duration, round duration, slot duration
    Etc.
  Ranging Device Management IE (RDM IE) for scheduling
    One or more RDM List elements
    Each RDM List element shows how the slot will be used
      Which device will use the slot
      What ranging role the device will take (Initiator or responder)

## Slide 11: Thoughts on Control and Scheduling for Data Comm
Controller can send Control Message similar to RCM
Control Message may contain:
  Existing IE for ranging
    Ranging and data communication can be performed in a single Ranging Round
  New IE for data session control
    Safeguards for ranging use-cases
    Interference mitigation
    Coexistence improvement
    Native discovery and connection setup
    Etc.
  New IE for scheduling signaling
    Efficient scheduling for data communication
Data
Ack
Ack
Controller
Controlee
Control Message
.
.
.

## Slide 12: Summary
Slotted structure is preferred over unslotted structure
Scheduling-based mode is preferred over contention-based mode
We need to define new IEs for control and scheduling for data communication

## Slide 13: Appendix

## Slide 14: Control Mechanism for Data Communication Session
In 4z-2020, Advanced Ranging Control IE (ARC IE) is used for Ranging Control information
Controller sends Ranging Control Message (RCM) which has ARC IE at the beginning of Ranging Round
[1] RIM: Ranging Initiation Message
[2] RRM: Ranging Response Message
[3] RFM: Ranging Final Message
[4] MRM: Measurement Report Message
RCM
RIM [1]
RRM [2]
RFM [3]
MRM [4]
Ranging Round
Ranging Slot

## Slide 15: Background: ARC IE [1]
Ranging configuration information
  Ranging specific configurations
    Multi-node Mode, Ranging Round Usage, STS Packet Config, etc.
  General configurations
    Schedule Mode, Ranging Block Duration, etc.
[1] IEEE 802.15.4z-2020, p. 78

## Slide 16: Background: RDM IE [1]
Controller sends Ranging Control Message (RCM) in the first slot
RCM includes Ranging Device Management IE (RDM IE), which is used for slot scheduling
By reading RDM List elements, controlees can figure out how slots will be used
[1] IEEE 802.15.4z-2020, p. 87