## Slide 1
Project: IEEE P802.15 Working Group for Wireless Personal Area Networks (WPANs)
Submission Title: [Recap of Narrowband / UWB Coupling MAC]
Date Submitted: [14 March, 2022]
Source: [Mingyu Lee, Taeyoung Ha, Junyoung Choi , Karthik Srinivasa Gopalan, Aniruddh Rao Kabbinale, Ankur Bansal, Clint Chaplin] Company [Samsung Electronics]
Address: [34, Seongchon-gil, Seocho-gu, Seoul, Korea]
E-Mail: [aniruddh.rao@samsung.com]
Abstract: [Recap for our discussion of how NB and UWB signaling can cooperate to mirror UWB Channel usage with channel hopping and collision avoidance]
Purpose: [ ]
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the authoring individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The authors(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2
PAR Objective | Proposed Solution (how addressed)
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | Channel hopping to mitigate interference and fading effects in Narrow Band
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEVs) | 
Improved link budget and/or reduced air-time | 
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | Off-loading of functionality to lower-complexity/power NB PHY helps reduce complexity of “heavier” UWB sub-system and power consumption of UWB system
Hybrid operation with narrowband signaling to assist UWB | Exploit tightly coupled concurrent operation of NB to help UWB
Enhanced native discovery and connection setup mechanisms | Provide collision avoidance scheme based on the energy detection and
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | 
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3: Contents
Motivation
Assumptions
NB Channels : Mirroring Channel
Collision Avoidance
Channel hopping in Mirroring Operation
Collision Avoidance in Mirroring Operation
Conclusions

## Slide 4: Motivation
In order to avoid collision in UWB channel, energy detection based schemes may not be the proper scheme for UWB because the spectral density of UWB is low
To avoid collision through energy detection and also using channel usage information, a MAC using NB mirroring channel coupled with UWB can be considered
Bands under consideration for NB for e.g., UNII3 are suspected to be affected by deep fades. Channel hopping can be considered to overcome effects of deep fades
Interference is possible from other NB assisted UWB systems and other technology using the same band as proposed. Channel hopping helps to mitigate the interference caused as well

## Slide 5: Assumptions
The concept of NB & UWB coupling MAC in this contribution is based on the assumption that a new NB technology for UWB will be introduced
- The energy consumption of NB is much lower than that of UWB - Data rate is enough to support the operations in this contribution - A set of channels available for system to frequency hop for mirroring operation - The band under consideration has deep fading issues and needs to be addressed.
NB clock and UWB clock are tightly synchronized

## Slide 6: RECAP

## Slide 7: Mirroring Channel (Recap)
An NB mirroring channel to be defined for each UWB channel (e.g., CH5, CH9)
The NB mirroring channel reflects the behavior of corresponding UWB channel
At a point in time, advertisement packet can be sent in the mirroring channel by NB/UWB device which occupies UWB channel at the specific period as controller.
Advertisement packet is used to announce that the specific period of UWB channel is being used and a few characteristics of the UWB transmission.
Advertisement packet is transmitted in NB right before transmission in UWB channel
By listening to this NB mirroring channel and receiving the advertisement packet, other devices can recognize whether the corresponding UWB channel is occupied or not
Controller in UWB shall listen the mirroring channels to find the available channel and time before establishing the connection

## Slide 8: Example Operation with Mirroring Channel (Recap)
Controller transmits an advertisement packet at every active ranging block/round in one of the mirroring channels
This packet is used for notifying the occupation status of the corresponding UWB channel to other devices
This packet includes the information about the usage of the corresponding UWB channel
  Start time of ranging rounds, Length of Ranging Block, Number of Ranging Rounds, Index of Active Round etc.
This packet may provide the information about the PHY parameters (e.g., BPRF/HRPF)
  Controller scans the mirroring channels before establishing UWB connection to find the available period and avoid collisions
  If the controller finds an idle period, it can send an advertisement packet for reserving the period in the corresponding UWB channel
Notations
A : Advertisement

## Slide 9: Collision Avoidance in Mirroring channel (Recap)
Collision Avoidance in Mirroring channel is necessary during reserving of open slots
  There are chances of two controllers choosing same time slot to be reserved.
We define a random delay timer - Reservation Delay Timer (RDT) to expire before the controllers starts advertising for reserving free slots
  RDT starts at the beginning of reservation window
  RDT can have a maximum value of difference between reservation window size and time duration of advertisement packet. This ensures the advertisement is transmitted completely within the reservation window that the controller wishes to reserve.
Notations
A : Advertisement
RAN : Ranging Access Network

## Slide 10: CA in Mirroring channel continued…(Recap)
Collision Avoidance in Mirroring channel is necessary during reserving of open slots
  There are chances of two controllers choosing same time slot to be reserved.
At any point during running of RDT, if channel is found busy, reservation is aborted in this cycle and attempted in a newly chosen slot in next cycle
From next cycle, post reservation, controller sends the advertisement at beginning of reservation window
Notations
A : Advertisement
RAN : Ranging Access Network

## Slide 11: Addressing Deep fades and interference
Mirroring Channels Hopping - Introduced to address deep fading effects in proposed band and interference from coexisting systems
Based on the channel feedback, the advertiser may decide to hop between multiple NB mirroring channels.
After every ranging block/round, the device hops within the set of mirroring channels allocated per UWB channel. This channel hopping mechanism helps in overcoming the effects of deep fading in NB channels.
Interference is possible from other NB assisted UWB systems and other technology using the same band as proposed. Channel hopping helps to mitigate the interference caused as well.
By listening to this set of channels and receiving the advertisement packet, other devices can recognize whether the corresponding UWB channel is occupied or not

## Slide 12: Mirroring Channels
A set of mirroring channels to be defined for each UWB channel (e.g., CH5, CH9)
There would be one mandatory mirroring channel, while rest would be optional
The set of channels collectively reflect the behavior of corresponding UWB channel
At a point in time, advertisement packet can be sent in one of the mirroring channels by NB/UWB device which occupies UWB channel at the specific period as controller.
Advertisement packet is used to announce that the specific period of UWB channel is being used and a few characteristics of the NB mirroring channel hopping and UWB transmission.
Advertisement packet is transmitted in NB right before transmission in UWB channel
By listening to this set of channels and receiving the advertisement packet, other devices can recognize whether the corresponding UWB channel is occupied or not

## Slide 13: Hopping within Mirroring Channels
Controller transmits an advertisement packet at every active ranging block/round in one of the mirroring channels.
  The number of mirroring channels per UWB channel would be upto 2 or maximum of 3.
  Transmitting Controller decides on a hopping pattern across the set of channels.
  One strategy: The pattern shall sweep N channels in N ranging blocks. N = Number of NB mirroring channels per UWB channel.
  Controller that is scanning is in same channel for N consecutive blocks.
  Hopping pattern can be conveyed in the advertisement in mirroring channel.
Notations
A : Advertisement

## Slide 14: Hopping within Mirroring Channels (contd…)
Reservation always happens at Mirroring Channel 0 or Default/mandatory mirroring channel to avoid two controllers reserving same slot, by sending Advertisement in two different mirroring channels.
  The controller can choose a pattern to hop to other mirroring channels from next block
Figure shows example operation for hopping between 2 mirroring channels per UWB channel
Controller shall listen to the set of mirroring channels pertaining to the UWB channel to find the available slot before establishing the connection.
Notations
A : Advertisement

## Slide 15: Collision Avoidance during Reservation
Collision Avoidance in Mirroring channel 0 or default mirroring channel is necessary during reserving of open slots
  There are chances of two controllers choosing same time slot to be reserved.
We define a random delay timer - Reservation Delay Timer (RDT) to expire before the controllers starts advertising for reserving free slots
  RDT starts at the beginning of reservation window
  RDT can have a maximum value of difference between reservation window size and time duration of advertisement packet. This ensures the advertisement is transmitted completely within the reservation window that the controller wishes to reserve.
Notations
A : Advertisement
RAN : Ranging Access Network

## Slide 16: CA in Mirroring channel continued…
Collision Avoidance in Mirroring channel is necessary during reserving of open slots
  There are chances of two controllers choosing same time slot to be reserved.
At any point during running of RDT, if channel is found busy, reservation is aborted in this cycle and attempted in a newly chosen slot in next cycle
From next cycle, post reservation, controller sends the advertisement at beginning of reservation window in one of the mirroring channels.
Notations
A : Advertisement
RAN : Ranging Access Network

## Slide 17: Conclusions
By coupling NB with UWB, clear channel assessment (CCA) for UWB channels is possible
NB mirroring channel is introduced for CCA
NB mirroring channel hopping helps addressing deep fading effects and mitigate interference in NB
CA method in the newly introduced NB channels is provided
NB-assisted UWB may reduce the power consumption of device and avoid collision between UWB communications

## Slide 18: Thank You