## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks (WSN)
Submission Title: New Data Rates
Date Submitted: March 15, 2022
Source: C.Murray (Qorvo)​, J.Niewczas (Qorvo), I.Dotlic (Qorvo), M.McLaughlin (Qorvo), B.Verso (Qorvo)
Abstract: Discusses proposals for new data rates in UWB.​
Purpose: To agree on approach to specifying new data rates in UWB.
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.
Notes: Jul 12, 2010
Page 1

## Slide 2
PAR Objective | 
Safeguards so that the high throughput data use cases will not cause significant disruption to low duty-cycle ranging use cases | 
Interference mitigation techniques to support higher density and higher traffic use cases | 
Other coexistence improvement | 
Backward compatibility with enhanced ranging capable devices (ERDEV | 
Improved link budget and/or reduced air-time | New higher data rates to reduce air-time but maintain link budget
Additional channels and operating frequencies | 
Improvements to accuracy / precision / reliability and interoperability for high-integrity ranging | 
Reduced complexity and power consumption | 
Hybrid operation with narrowband signaling to assist UWB | 
Enhanced native discovery and connection setup mechanisms | 
Sensing capabilities to support presence detection and environment mapping | 
Low-power low-latency streaming | 
Higher data-rate streaming allowing at least 50 Mbit/s of throughput | Adds higher data rates
Support for peer-to-peer, peer-to-multi-peer, and station-to-infrastructure protocols | 
Infrastructure synchronization mechanisms | 

## Slide 3
New Data Rates
C.Murray (Qorvo)​, J.Niewczas (Qorvo), I.Dotlic (Qorvo), M.McLaughlin (Qorvo), B.Verso (Qorvo)

## Slide 4: Submission Overview
PRF selection for maximizing Link Budget
Advantages/Disadvantages of QPSK
Advantages/Disadvantages of an Equalizer
Advantages/Disadvantages of Advanced Coding
Static vs Dynamic data rate configuration
Summary of Our Current View on New Data Rates

## Slide 5: Maximizing Link Budget
High Level Tx Power Regulations
  The Maximum Mean PSD = -41.3 dBm/MHz
    => -14.3 dBm in 500 MHz (upper bound)
    Will be less than this as realizable PSD will not be flat across 500 MHz
    Also must allow for spectral PAPR
  The Maximum Peak PSD = 0 dBm/50 MHz
  The Power Spectral Density (PSD) is measured over any 1 millisecond (ms)
To maximize the Link Budget the goal is –
  All transmissions to have 37nJ each ms ( = -14.3 dBm )
  Subject to the above and spectral/temporal mask constraints

## Slide 6: BPRF Example 1/2 0.65 Mbps PHR | 6.81 Mbps Payload

## Slide 7: BPRF Example 2/2 0.65 Mbps PHR | 6.81 Mbps Payload

## Slide 8: Tx Gain vs Packet duration for different PRFs
Because the Peak PSD constraint has least impact on HPRF, the Tx Power
can be optimized over the full range of 1 packet any millisecond sizes with HPRF

## Slide 9: Understanding Origin of Peak Limit
HPRF distributes the energy more uniformly in time and avoids the peak constraint (mostly)

## Slide 10: Optimized Tx Power can offset majority of the Link Budget loss due to data rate doubling (1 packet any millisecond)
Assumes 3dB sensitivity loss per data rate doubling

## Slide 11: Further improvement possible when SYNC Tx power reduced by 3 dB every data rate doubling

## Slide 12: Advantages/Disadvantages of QPSK
Advantages
  Natural candidate for data rates above 124.8 Mbps
    For the same BER, the same noise level, and a 3dB increase in transmit power QPSK provides twice the bit rate of BPSK
  More robust channel matched filter (CMF) performance in 2-path symbol spaced channels
  Exercises both I and Q evenly – Rx statistics less sensitive to CFO
Disadvantages
  For full benefit re Rx statistics, the SYNC should be QPSK
  Carrier recovery more difficult
  Analog I/Q balance becomes important

## Slide 13: Advantages/Disadvantages of an Equalizer
Advantages
  ISI becomes significant at symbol rates > 124.8 Msps
    An equalizer improves overall performance
  At 124.8 Msps (mega symbols per second) an equalizer performs 1 to 2dB better than a CMF for CM1 channels (with 4z k=7 CC)
    CM1 channels are very dispersive and rich in multi-path
Disadvantages
  An equalizer has little benefit for symbol rates ≤ 62.4Msps
  Different symbol structures are optimum for an equalizer vs a CMF based receiver
  An equaliser requires training

## Slide 14: Advantages/Disadvantages of Advanced Coding (LDPC measurements used for representative purpose only)
Advantages
  Appears to be robust to non-Gaussian noise
    Less sensitive to ‘type’ of noise source
    Complementary to CMF re uncancelled ISI
  For short payloads LDPC has ~1dB lower Eb/N0 than 4z k=7 CC for a packet error rate of 1%
  As payload increases LDPC improves by up to 1 dB
  As payload increases 4z k=7 CC drops between 1 and 2 dB
Disadvantages
  Increased power consumption
  Increased die area
  May need to design a code specifically for UWB use cases
  Another coding scheme added to standard

## Slide 15: Dynamic or Static Data Rates
Advantages of Dynamic vs Static
  Allows for unilateral change of data rates
  Allows for peer-to-many-peers communication links with different data rates for each individual peer-to-peer link
Disadvantages of Dynamic
  PHR data rate must be common to all payload data rates
  The data rate must be signalled in the PHR – increases the number of PHR bits
  Imposes a constant overhead
  PHR decoding is necessary before PHR bits can be utilized eg before payload demodulation

## Slide 16: PHR Overhead Calculator
B2B =
back to back

## Slide 17: Summary of Our Current View 1/2 Data Rate Components
Which PRF should we use?
  124.8/249.6 MHz PFR give most flexibility in maximizing link budget
Do we need QPSK?
  Complicates the design with not enough benefit unless data rates greater than 124.8Mbps required
Do we need an Equalizer?
  Boundary between CMF and Equalizer performance is 124.8Msps
  Sacrifice some performance at 124.8Msps to avoid need for equalizer
Do we benefit from Advanced Coding?
  Up to a 4 dB increase in Link Budget compared to 4z k=7 CC
  Advanced coding complements CMF as it is robust to moderate ISI
Static or Dynamic data rate configuration?
  Dynamic feature may be of limited use if optimum Tx gains used

## Slide 18: Summary of Our Current View 2/2 Data Rate Configurations
Open to new preamble – being explored independently
  Currently assuming 32 symbol SYNC, 4 symbol SFD at PRF 124.8 MHz (HPRF)
New/Optional 124.8/249.6 MHz PRF data rates of 7.8, 15.6, 31.2, 62.4 and 124.8 Mbps
  Use optimum Tx gain to maximize link budget
  BPSK chip modulation similar to 4z
  Symbols optimized for CMF – no explicit pilots for equalizer training
  Continue with static data rate configuration
    Data rate PHR with 4z k=7 CC and code rate = 0.5 coding
    Or fixed low-rate PHR coding (may be better if using advanced coding for payload)
  Default payload coding 4z k=7 CC and code rate = 0.5
New optional advanced code (eg Polar, LDPC)
  Base code rate = 0.5
  Performance for short (~64-byte) as well as long packets important