## Slide 1
Project: IEEE P802.15 Working Group for Wireless Specialty Networks
Submission Title: Considerations for MAC protocol in IEEE 802.15.6 BAN with Enhanced Dependability
Date Submitted: May 17th, 2022
Source: Minsoo Kim, Takumi Kobayashi, Marco Hernandez, Ryuji Kohno
Company: (1)Yokohama National University (2) YRP International Alliance Institute
Address: (1)79-5 Tokiwadai, Hodogaya-ku, Yokohama, 240-8501 Japan,
(2) YRP1 Blg., 3-4 HikarinoOka, Yokosuka-City, Kanagawa, 239-0847 Japan
Voice:[+81-90-5408-0611] E-Mail:[minsoo@minsookim.com, kobayashi-takumi-ch@ynu.ac.jp, marco.hernandez@ieee.org, kohno@ynu.ac.jp]
Re: In response to call for technical contributions
Abstract:
Purpose: Material for discussion in P802.15.6a TG
Notice: This document has been prepared to assist the IEEE P802.15. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Release: The contributor acknowledges and accepts that this contribution becomes the property of IEEE and may be made publicly available by P802.15.

## Slide 2: Introduction
Unlike when the original standard was first published 10 years ago, personal wireless systems such as Bluetooth and Wi-Fi are already prevalent today.
Therefore, BANs should focus on applications that require higher reliability that cannot be achieved with other wireless systems. Such applications include medical devices and automotive systems.
To make the standard concise and implementable, it may be required to remove some parts of the original standard that do not meet the goal of high reliability.

## Slide 3: PHY and MAC access modes
Physical (PHY) layer
  Narrowband
  Ultra-wideband
  Human Body Communication
Medium access control (MAC) sublayer
  Beacon mode with superframes
  Non-beacon mode with superframes
  Non-beacon mode without superframes
It would be reasonable to focus only on ultra-wideband and beacon mode, as they are beneficial to achieving high dependability.
Other PHYs or MACs, such as narrowband or non-beacon mode, may be left as optional for backward compatibility.

## Slide 4: Access phases
We intend to simplify the superframe structure, while maintaining backward compatibility.
  Simplified superframe (mandatory)
  802.15.6-2012 superframe (optional, for backward compatibility)
The new superframe structure may contain time slots for coordinator-to-coordinator (C2C) link and/or Time-Sensitive Networking (TSN) support.

## Slide 5: Priority mapping
Priority | User priority | Traffic designation | 
 |  | Human BAN | Vehicle BAN
Lowest | 1 | Background (BK) | 
 | 2 | Best effort (BE) | 
 | 2 | Excellent effort (EE) | 
 | 3 | Video (VI) | 
 | 4 | Voice (VO) | 
 | 5 | Medical data or network control (e.g., body temperature) | Passenger vital information observed by the vehicle
 | 6 | High-priority medical data or network control (e.g., electrocardiogram (ECG), oxygen saturation (SpO2)) | 
Highest | 7 | Emergency or medical implant event report (e.g., heart attack, respiratory failure) | Proximity alert
Vehicle BAN traffic priorities should be mapped.
Traffic types may be simplified.

## Slide 6: Priority mapping (cont.)
A list of application would be useful for prioritizing each application.
We may consider introducing criteria to determine priorities for future applications.
High priority is usually interpreted as requiring low latency, but can also mean low error rates or high data rates.
Priority-related parameters can be categorized into (a) requirements such as packet error rate, data rate, latency, and (b) implementations to achieve these requirements, such as contention window.

## Slide 7: QoS Parameters
Parameters | Low Data rate BAN (Typical HBAN) | High Data rate (BCI) | Typical VBAN * Ref. .4z | Comments
Aggregate data rate | 2 Mbps | 49 Mbps | Few hundreds of Mbps | 
Comm. range | 0.5 m | 2 cm across the skin tissue / 1 m | 3 m | 
Delivery ratio | > 99 % | > 95 % | > 99.9 % | 
Latency | 10 ms | 100 ms | 4-250 ms | 
Ranging capability | Sub-centimeter accuracy | Not required | Not required / Sub-centimeter accuracy | * Ref. .4z
From doc. # 15-21-0493-02-006a., “Draft Technical Requirement of IEEE802.15.6a for Amendment of 15.6 BAN with Enhanced Dependability”

## Slide 8: Summary
Some parts of the original standard that do not meet the goal of high reliability may be removed, in the sense of focusing on ultra-wideband and beacon mode with superframes, which are advantageous for achieving high dependability.
The superframe structure may also be simplified by reducing the types of access phases. Meanwhile, time slots for C2C and TSN may be included.
Priority mapping for vehicle BAN traffics is required. Priorities of Human BAN traffics can also be reconsidered.